## Slide 1: SFD Proposal on Retransmission
Date: 2017-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We decided retransmission policy of unicast wake up packet in last meeting
Also we decided that 802.11ba spec shall define a mechanism to wake up multiple WUR mode STAs
In this submission, we address transmission failure cases in multiple wake up scenario
  We discuss possible solutions and propose fine retransmission policy in multiple wake up scenario

## Slide 3: Accepted Motions in March meeting : Unicast wake-up [1]
A STA should send a response frame to the AP using primary connectivity radio after receiving a unicast wakeup packet
After AP sends a unicast wake-up packet to a STA, AP waits for a timeout interval
  If AP receives any transmission from the STA within the timeout interval, then the wake-up packet transmission is successful
  Otherwise, the wake-up packet transmission fails, and AP may retransmit the wake-up packet to the STA

## Slide 4: Accepted Motions in March meeting : Multiple wake-up [1]
802.11ba spec shall define a mechanism to wake up multiple WUR mode STAs (e.g., multi-user wake-up frame)

## Slide 5: Transmission failure cases in Multiple Wake up
Case 1: Wake-up packet fails
  The STA couldn’t receive wake-up packet and then operates in WUR mode

## Slide 6: Transmission failure cases in Multiple Wake up
Case 2: Trigger frame or PS-Poll frame fails
  The STA received wake-up packet successfully but transmission of trigger frame or PS-Poll frame is failed
  STA will operate in WLAN mode and content to transmit unicast PS-Poll frame

## Slide 7: Problem statement
If there is transmission failure in multiple wake-up scenario, AP will not be sure of STA’s operating mode
  STA can operate in WLAN or WUR mode
This uncertainty can occur very long latency and power consumption
  So we should have a fine retransmission policy in multiple wake-up scenario

## Slide 8: Possible solutions
Retransmit Trigger frame (or transmit Data frame)
Retransmit Wake-up packet

## Slide 9: Retransmit Trigger frame
Retransmitting trigger frame works well only when the STA operates in WLAN mode
If the STA operates in WUR mode, however, retransmission of trigger frame is nothing but wasting resource

## Slide 10: Retransmit Wake-up packet – 1
If the STA operates in WLAN mode and responses to AP within Retransmission Limit time, AP doesn’t have to retransmit any frame and will transmit Data frame to the STA
  It is the best scenario in terms of latency and resource utilization

## Slide 11: Retransmit Wake-up packet – 2
If an AP couldn’t receive any response from the STA during Retransmission Limit time, AP will retransmit Wake-up packet to the STA
  If the STA operates in WUR mode, this retransmission procedure works well

## Slide 12: Retransmit Wake-up packet – 3
If the STA couldn’t response to AP within Retransmission Limit time because of busy channel, channel error, or collision, retransmission of Wake-up packet doesn’t look good solution because the STA operates in WLAN mode
  Retransmission of wake-up packet wasn’t necessary
  The STA is contending to transmit PS-Poll in very bad channel
  A lot of electronic power of the STA is consumed during WLAN mode

## Slide 13: Proposed Solution
Retransmitting Wake-up Packet is better solution when there is transmission failure in multiple wake-up scenario
  Whatever the STA operates in WUR mode or WLAN mode, retransmission of wake-up packet works well
  However, the STA will waste its electronics power if the STA cannot transmit PS-Poll frame to the AP within a certain time because of bad and/or busy channel
    In such case, it is better for the STA to return WUR mode and wait to receive a wake-up packet in better channel condition

## Slide 14: Proposed Solution
So we propose that
  the AP shall retransmit wake-up packet to the STA when it couldn’t receive any response frame from the STA after multiple wake-up scenario
  the STA can change its operating mode into WUR mode if the STA couldn’t transmit any frame to an AP and receive any response frame from the AP within a certain time after wake up

## Slide 15: Summary
We addressed transmission failure case in broadcast wake up scenario
  Retransmitting wake up packet looks better solution
  Also we proposed STA’s operation to reduce latency and power consumption in a certain case

## Slide 16: Straw poll 1
Do you support the following modification of sentence if SFD?
  After AP sends a unicast wake-up packet to a STA or a multi-user wake-up packet to multiple STAs, AP waits for a timeout interval
    If AP receives any transmission from the STA within the timeout interval, then the wake-up packet transmission is successful
    Otherwise, the wake-up packet transmission fails, and AP may retransmit the wake-up packet to the STA

## Slide 17: Straw poll 2
Do you support following sentences?
  A STA may change its operating mode into WUR mode if the STA is not able to transmit any frame to an AP and receive any response frame from the AP within a certain time after wake up

## Slide 18: References
[1] 11-17-0526-00-00ba-meeting-minutes-march-2017