## Slide 1: WUR Legacy Preamble Design
Date: 2017-05-07
Authors:

## Slide 2: Introduction
Wake-up Radio (WUR) frame is designed to be compatible with other 802.11 devices to correctly set CCA and backoff.
A simple design is to append 802.11 legacy preambles to the WUR packet, the same as HT mixed mode/VHT/HE packet format
If WUR symbol adopts narrow-band design, for example 4MHz [1], the legacy preamble portion preceding WUR symbols may trigger 802.11n devices to false detect WUR packet to be a 11n type, and erroneously set the PHY-CCA.indication(IDLE)
To address this issue, several design options are proposed

## Slide 3: 802.11n Device Rx State Machine
As show in IEEE 802.11mc standards [2], if HT-SIG CRC fails, the PHY-CCA.indication(IDLE) is set when receive level drops below threshold.

## Slide 4: WUR Packet Format
Legacy preambles: LSTF+LLTF+LSIG, needs to be added to spoof 802.11 devices for CCA
The popular WUR preamble design is based on narrow band (e.g. 4MHz) signaling [1]
The unpopulated tones in the WUR portion will be received as noise with random phase
For WiFi devices supporting up to 802.11n, the auto detection mechanism may false detect the WUR packet as 11n packet with higher probability.
Need a design to spoof 802.11n devices to correct set CCA
LSTF
LLTF
LSIG
WUR Preamble
WUR Payload

## Slide 5: Proposed Solutions
Solution: add a dummy 4us OFDM symbol with BPSK modulation before narrow-band WUR preamble.
This symbol is designed solely to spoof 802.11n device
This OFDM symbol could be a 4-us LLTF, or any other BPSK modulated 20MHz OFDM symbol.
WUR STA will start WUR packet reception after this symbol
Negligible impact on the WUR preamble processing and packet reception
LSTF
LLTF
LSIG
WUR Preamble
WUR Payload
4us Symbol

## Slide 6: Simulation Settings
Packet: WUR with LSTF + LLTF + LSIG + WUR Portion
  WUR Portion bandwidth: 4MHz signal
  WUR Portion modulation: OOK
20MHz Rx sampling
Impairments:
  Tx/Rx IQ imbalance, Tx/Rx Phase Noise
  Using 11ax design parameters
  WUR Rx will have worse impairments
  No CFO

## Slide 7: Channel AWGN

## Slide 8: Channel D

## Slide 9: UMi-LOS

## Slide 10: Discussions-1
The 4MHz narrow band signal may typically degrade the 11n device QBPSK detection by 3+ dB in fading channels—based on one particular QBPSK detection method.
Existing 11n devices may have various methods of doing QBPSK classification, therefore it is hard to design a 4MHz signal spoofing ALL existing 11n devices reliably.

## Slide 11: Discussions-2
The 802.11n device spoofing can also be achieved with MAC options by transmitting CTS-to-self before each WUR packet for proper protection
There are several disadvantages of this MAC solution
  High communication overhead
  No former example of MAC solution for format protection
    The exception is 11n green-field packet, but gets little industry adoption
For the extra BPSK symbol design, we may not need standardize the content of the symbol as long as it is BPSK modulated

## Slide 12: Conclusions
802.11n device may have high false alarm probability for WUR packets
This issue can be addressed with PHY design by adding an extra BPSK modulated OFDM symbol before narrow-band WUR symbol

## Slide 13: Straw Poll 1
Do you agree to have L-STF, L-LTF, and L-SIG appended in 11ba packets, and add an extra full-bandwidth (20MHz) OFDM symbol with BPSK modulation after LSIG in the 11ba packets to spoof legacy devices?
  Yes
  No
  Abstain

## Slide 14: References
[1] Minyoung Park et al., “LP-WUR (Low-Power Wake-Up Receiver) Follow-Up”, IEEE 802.11-16/0341r0, Mar. 14, 2016.
[2] IEEE draft P802.11REVmc_D8.0.pdf