## Slide 1: Consideration of EDCA for WUR Signal
Date: 2017-05-08
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Minyoung Park |  |  |  | minyoung.park@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Thomas Kenney |  |  |  | thomas.j.kenney@intel.com

## Slide 2: Abstract
In [1], we have agreed to do EDCA for transmitting wake-up packet, and the EDCA parameter is TBD
We provide our view to follow up on this important topic and discuss consideration of EDCA for WUR signal including unicast wake-up packet, multicast wake-up packet, and WUR Beacon

## Slide 3: Reuse Existing AC and EDCA Parameters
There are four ACs for EDCAF: AC_VO, AC_VI, AC_BE, and AC_BK.
We think there is no need to define new AC or new EDCA parameters for WUR signal including unicast wake-up packet, multicast wake-up packet, and WUR Beacon
  Defining new AC likely requires us to define more than one new AC for meeting various latency requirement
  Defining new AC or new EDCA parameters probably will not provide higher channel access priority than AC_VO. Note that default AIFSN and CWmin for AC_VO are already small (2 and (aCWmin+1)/4-1, respectively).
  Similar to the reason mentioned above, defining new AC or new EDCA parameters probably can not provided channel access that can be differentiated from the channel access of existing 4 ACs
  11ax goes through the same discussion for Trigger frame and does not define new AC or new EDCA parameters for Trigger frame
  Hence, we propose that an AP reuses existing 4 ACs and corresponding EDCA parameters to transmit WUR signal

## Slide 4: Access Category of WUR Signal: Multicast
We propose that an AP may use any AC for sending multicast wake-up packet or WUR Beacon based on the following considerations
  Most of the existing AC category selection rule is for unicast packet.
  For multicast packet, the rule is more relaxed as shown below.
    As discussed in 11ax, AP can use any AC to send Trigger frame
    As listed in baseline, AP can use any AC to send VHT NDP Announcement frame or Beamforming Report Poll frame
  For an AP, how to buffer the WUR signal for transmission and initialize EDCAF together with other existing traffic is implementation specific
  Allow any AC for sending multicast wake-up packet or WUR Beacon gives full flexibility for AP to do optimization and simplifies the spec work

## Slide 5: Access Category of WUR Signal: Unicast
For unicast wake-up packet, there may be several options if there are buffered frame for a STA when the unicast wake-up packet is sent to the STA.
  Open for discussion.
It is also possible that there are no buffered frame for a STA when the unicast wake-up packet is sent to the STA.
  The STA is waked up for receiving main radio beacon, which is not a buffered frame for a specific STA
  The STA is waked up prior to an incoming traffic based on known traffic pattern
  The STA is waked up so that AP can send trigger frame later to trigger response for the data collecting by the STA
  To simplify the rules for these various cases, we propose that an AP may use any AC for sending a unicast wake-up packet to a STA if the AP does not have pending buffered frame to the STA
    Give full flexibility for AP to do optimization and simplify the spec work

## Slide 6: CW and Retry Count Update
Currently, CW and retry count will be updated for a failed transmission that initiates TXOP through EDCA.
Since the indication of failure for unicast wake-up packet only comes around 10 ms later[2], we do not think it is necessary to update CW and Retry Count after 10 ms [2]
  Channel condition may already change
For multicast wake-up packet or WUR Beacon, there is no indication of failure, and even if we design one later, there is still no need to update CW and Retry Count due to the same reason as described above
We propose that
  CW and retry count will not be updated after transmitting WUR Signal
  CW and retry count will not be updated after identifying failure for unicast wake-up packet transmission

## Slide 7: Conclusion
We discuss the following consideration for transmitting WUR Signal, i.e., wake-up packet and WUR Beacon
  Reuse existing 4 ACs and corresponding EDCA parameters
  AP may use any AC to send multicast wake-up packet and WUR Beacon
  AP may use any AC for sending a unicast wake-up packet to a STA if the AP does not have pending buffered frame to the STA
  CW and Retry Count update after using EDCAF to transmit WUR Signal

## Slide 8: Straw Poll 1
Do you support the following?
  An AP reuses existing 4 ACs and corresponding EDCA parameters to transmit WUR signal
  Note that WUR signal includes unicast wake-up packet, multicast wake-up packet, and WUR Beacon

## Slide 9: Straw Poll 2
Do you support the following?
  An AP may use any AC for sending a multicast wake-up packet
  An AP may use any AC for sending a WUR Beacon

## Slide 10: Straw Poll 3
Do you support the following?
  An AP may use any AC for sending a unicast wake-up packet to a STA if the AP does not have pending buffered frame to the STA

## Slide 11: Straw Poll 4
Do you support the following?
  After an AP sends a WUR signal using EDCAF of a particular AC, the AP shall not update CW and retry count of the AC
  After identifying failure for an unicast wake-up packet that is sent using EDCAF of a particular AC, AP shall not update CW and retry count of the AC

## Slide 12: Reference
[1] 11-17-0354-02 Initial thoughts on MAC procedures
[2] 11-14-0980-16 Tgax Simulation Scenarios
[3] 11-17-0342-04 WUR Negotiation and Acknowledgement Procedure Follow up