## Slide 1: Examples of Integrating WUR with Existing Power Save Protocol
Date: 2017-05-08
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Minyoung Park |  |  |  | minyoung.park@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com

## Slide 2: Abstract
In [1], we discuss the high level concept for integration WUR with existing power save protocol
In this presentation, we share further examples on integrating WUR with existing Power Save Protocols

## Slide 3: Discussion of Existing Power Save Protocols
We think we can roughly classify existing power save protocols into two categories
  Power save protocols without existing negotiated service period
    Examples include PSM, PSP, and U-APSD as discussed in [2]
  Power save protocols with existing negotiated service period
    Examples include TWT, as discussed in 11ax/ah, and WNM sleep mode
We consider PSM, PSP, U-APSD, and TWT and provide examples of integrating WUR with these power save protocols

## Slide 4: Examples: PSM
AP buffers this frame
DATA
Wake-up packet
ACK
A-MPDU
BA
PM=0
ACK
PM=1
By default, transition to WUR operation
AP
STA
WUR operation
Assume STA enters WUR operation through TBD signaling and STA is in Power save mode
AP buffers this frame
DATA
Wake-up packet
Signaling to disable WUR Operation and stop receiving wake-up packet from AP
ACK
ACK
A-MPDU
BA
PM=0
AP
STA
WUR operation
Assume STA enters WUR operation through TBD signaling and STA is in Power save mode
ACK
PM=1
WUR operation
Doze State

## Slide 5: Examples: TWT
TWT service period
AP buffers this frame
A-MPDU
DATA
BA
Wake-up packet
TWT service period
A-MPDU
DATA
BA
Wake-up packet
AP
STA
AP
STA
WUR operation
Resume only the TWT service period that covers the wake-up packet reception time
Assume STA enters WUR operation through TBD signaling to suspend TWT service period and STA is in Power save mode
Resume only the next TWT service period
WUR operation
Assume STA enters WUR operation through TBD signaling to suspend TWT service period and STA is in Power save mode
AP buffers this frame
WUR operation
Signaling to disable WUR Operation, stop receiving wake-up packet from AP, and resume all TWT service periods
ACK
TWT service period
Doze State
By default, transition to WUR operation

## Slide 6: Examples: PSP
AP buffers this frame
DATA
Wake-up packet
By default, transition to WUR operation
AP
STA
WUR operation
Assume STA enters WUR operation through TBD signaling and STA is in Power save mode
WUR operation
ACK
PS-Poll
MPDU
STA starts CCA for PS-Poll
AP starts EDCA for downlink one MPDU
ACK
AP buffers this frame
DATA
Wake-up packet
AP
STA
WUR operation
Assume STA enters WUR operation through TBD signaling and STA is in Power save mode
ACK
PS-Poll
MPDU
STA starts CCA for PS-Poll
AP starts EDCA for downlink one MPDU
ACK
ACK
Signaling to disable WUR Operation and stop receiving wake-up packet from AP
Doze State

## Slide 7: Examples: U-APSD
AP buffers this frame
DATA
Wake-up packet
ACK
A-MPDU
BA
A-MPDU
BA
EOSP=1
MPDU
EOSP=0
ACK
AP buffers this frame
DATA
Wake-up packet
A-MPDU
BA
A-MPDU
BA
EOSP=1
MPDU
EOSP=0
ACK
AP
STA
WUR operation
AP
STA
WUR operation
Assume STA enters WUR operation through TBD signaling and STA is in Power save mode
Assume STA enters WUR operation through TBD signaling and STA is in Power save mode
By default, transition to WUR operation
Signaling to disable WUR Operation and stop receiving wake-up packet from AP
WUR operation
Doze State

## Slide 8: Conclusion
We consider PSM, PSP, U-APSD, and TWT and provide examples of integrating WUR with these power save protocols
We think it is important to have the following consideration for further design
  Have signaling to enable/disable WUR operation
  Suspend existing MR negotiated schedule rather than terminate existing MR negotiated schedule when entering WUR operation
  Resume only one existing MR negotiated schedule/service period after receiving wake-up packet
  Preserve the existing sequence exchange for power save protocols without negotiated schedule such as PSM, PSP, and U-APSD and enter WUR operation after sequence exchange ends

## Slide 9: Reference
[1] 11-17-0071-00 High Level MAC Concept for WUR
[2] 11-14-1161-03 Parameters for Power Save Mechanisms