## Slide 1: AP re-discovery in WUR
Date: 2017-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
When does STA in WUR mode turns on its primary connectivity radio?
  when the packet for waking up the STA is received
  Other case?
Re-discovery of WUR STAs by AP[1][2]
  IEEE 802.11ba shall provide mechanisms to enable re-discovery of WUR stations by AP.
Then, need re-discovery of AP by WUR STA ?

## Slide 3: AP re-discovery (1/3)
WUR Beacon [3]
  AP transmits the WUR Beacon periodically
  WUR STA can synchronize with its AP by receiving the WUR Beacon
However, the WUR STA cannot receive WUR Beacon when the STA is out of TX range of its AP
For WLAN service, the STA in WUR mode should be able to know if it’s in the AP’s TX range or not

## Slide 4: AP re-discovery (2/3)
When STA in WUR mode does not receive any packet (e.g., WUR beacon or WUP) from its AP during a specific period(e.g., Keep alive check period), the STA turns on its WLAN and
  waits to receive any WLAN packet from its AP or
  send a frame (e.g., QoS Null/PS-Poll) through WLAN to confirm if it’s in the range of AP or not
If the STA receives WLAN packets sent by its AP or receives a response frame from the AP, the STA re-enters the WUR mode
Otherwise, the STA performs scanning procedure for discovering other AP
Whenever STA in WUR mode receives any packets from its AP, the STA resets the keep alive check period

## Slide 5: AP re-discovery (3/3)
AP
STA1:
WUR
STA1:
WLAN
WUR
WUR
Keep alive check period
Keep alive check period
WUR
Keep alive check period
AP
STA1:
WUR
STA1:
WLAN
WUR
WUR
Keep alive check period
QoS Null
ACK
Turn on
WLAN
AP
STA1:
WUR
STA1:
WLAN
WUR
WUR
Keep alive check period
QoS Null
ACK
Turn on
WLAN
Entering WUR mode
Probe Request
Scanning procedure

## Slide 6: Conclusion
The STA in WUR mode need to be able to know if it’s in the AP’s TX range or not
When the WUR STA finds that it’s out of the TX range, the STA turns on its primary connectivity radio and performs the procedure to find its AP or other AP

## Slide 7: References
[1] 11-17-0575-00-00ba-spec-framework
[2] 11-17-0027-04-00ba-re-discovery-problems-in-wur-wlan
[3] 11-17-0343-00-00ba-wur-beacon
[4] 11-16-1445-01-0wur-overall-mac-procedure-for-wur

## Slide 8: Straw Poll 1
Do you support the following?
  IEEE 802.11ba shall provide mechanisms to enable re-discovery of AP by WUR mode STA.
  Yes
  No
  Abstain