## Slide 1: AP re-discovery by WUR STA
Date: 2017-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
When does STA in WUR mode turns on its primary connectivity radio?
  when the packet for waking up the STA is received
  Other case?
Re-discovery of WUR STAs by AP[1][2]
  IEEE 802.11ba shall provide mechanisms to enable re-discovery of WUR stations by AP.
Then, need re-discovery of AP by WUR STA ?

## Slide 3: AP re-discovery (1/2)
WUR Beacon [3]
  AP can transmit the WUR Beacon periodically with longer WUR Interval than Beacon Interval of WLAN
  WUR STA can synchronize with its AP by receiving the WUR Beacon
WUR STA may not receive WUR Beacon
  Because the STA is out of TX range of its AP or
  Because of collision with OBSS transmission in dense network
If the STA is out of the AP TX range, the STA need to find another AP. Otherwise, the STA need to return to the WUR mode for more power saving
Therefore, in this case the STA should be able to know if it’s in the AP’s TX range

## Slide 4: AP re-discovery (2/2)
When STA in WUR mode does not receive any packet (e.g., WUR beacon or WUP) from its AP during a specific period, the STA turns on its WLAN and
  waits to receive any WLAN packet from its AP or
  send QoS Null frame through WLAN to check if it’s in the range of AP or not
If the STA receives WLAN packets sent by its AP or receives a response frame from the AP, the STA can re-enter the WUR mode
Otherwise, the STA can perform scanning procedure for discovering other AP
QoS Null frame
Ack
Keep alive check period

## Slide 5: Conclusion
When the WUR mode STA does not receive WUR Beacon or WUR packet during a specific period, the STA mode need to check know if it’s in the AP’s TX range
If the WUR STA is in the AP’s TX range, the STA returns to the WUR mode. Otherwise, the STA can perform the scanning procedure to find another AP

## Slide 6: References
[1] 11-17-0575-00-00ba-spec-framework
[2] 11-17-0027-04-00ba-re-discovery-problems-in-wur-wlan
[3] 11-17-0343-00-00ba-wur-beacon
[4] 11-16-1445-01-0wur-overall-mac-procedure-for-wur

## Slide 7: Straw Poll 1
Do you support the following?
  IEEE 802.11ba shall provide mechanisms to enable re-discovery of AP by WUR mode STA.
  Yes
  No
  Abstain