## Slide 1: WUR Security Proposal
Date: 2017-05-08
Authors:
May 2017

## Slide 2: Abstract
Malicious attacks on a WUR device running on coin-battery can cause the WUR to falsely wake up the Primary Connectivity Radio (PCR) the battery and ultimately disable the device [1].
Some potential solutions have been shown in [2]
  “One solution is to encrypt the LP Wakeup Req.”
  “Another solution could be Wakeup Request frame carries secret information that both AP and destined STA aware.”
However, these solutions increase the complexity and power consumption of the WUR receiver (WURx).
This presentation proposes a low complexity solution to address issues of potential attacks on WUR devices.
May 2017

## Slide 3: Outline of the Proposal
Upon waking up, the STA informs the AP the reason of its wake-up. Then, the AP determines whether the STA’s WURx receives a spoofed wake-up packet (under attack).
If the AP considers the STA’s WURx is safe, the AP proceeds with the normal wake-up procedure (based on proposal in [3] as shown in the next slide).
If the AP considers the STA’s WURx is under attack, AP performs additional steps to mitigate the impact of potential repeated attacks on the STA.
May 2017

## Slide 4: WUR Normal Wake-up Procedure
Step 1: The AP sends a wake-up packet (WUP) to the STA carrying the STA’s wake-up ID (WUID).
Step 2: The STA’s WURx receives the WUP and wakes up its PCR.
Step 3: The STA sends a wake-up response frame to the AP using its PCR, indicating that the STA’s PCR is woken up due to receiving a WUP (as opposed to sending a RTS, a data, or a wake-up response frame indicating that the STA wakes up on its own, when the STA indeed wakes up on its own).
Step 4: After the AP receives the wake-up response frame,
  Since the AP did send the WUP to the STA’s WURx, the AP considers the STA is safe.
  Then, the AP proceeds with the data exchange with the STA’s PCR.
WUP
AP
STA’s WURx
STA’s PCR
Wake-up
Wake-up response frame from STA to AP
Woken by WUP
Data packet
ACK
May 2017

## Slide 5: Wake-up Procedure under Attack 1/2
Option 2: AP asks STA the reason of wake-up, then STA replies to AP’s request.
Spoofed WUP
Attacker
STA’s WURx
STA’s PCR
Wake-up
Wake-up response frame
AP
ACK
Ask for reason of wake-up
New WUID
Inform reason of wake-up
Woken by WUP (which the AP didn’t send)
Spoofed WUP
Attacker
STA’s WURx
STA’s PCR
Wake-up
Wake-up response frame carrying the reason of wake-up
AP
New WUID
ACK
Woken by WUP (which the AP didn’t send)
…
Option 1: The Wake-up response frame indicates the reason of wake-up.
  Since the AP didn’t send the WUP to the STA’s WURx earlier, the AP considers that the STA is under attack and performs additional steps to mitigate potential repeated attacks, such as changing the identifier of WURx (for its next wake-up).
May 2017

## Slide 6: Wake-up Procedure under Attack 2/2
Option 3: STA reports the reason of wake-up after sending a wake-up response frame.
Spoofed WUP
Attacker
STA’s WURx
STA’s PCR
Wake-up
Wake-up response frame
AP
ACK
New WUID
Inform reason of wake-up
ACK
Woken by WUP (which the AP didn’t send)
…
timeout
May 2017

## Slide 7: Conclusion
A low complexity WUR security solution was presented.
  After waking up, the STA informs the AP the reason of its wake-up.
  The AP determines whether the STA’s WURx is under attack.
  If the AP determines that the STA’s WURx is under attack, the AP performs additional steps to mitigate potential repeated attacks.
Benefits
  Providing mechanisms, which are implemented over the STA’s PCR, for detecting attacks on WURx and for mitigating potential repeated attacks, without increasing the complexity or power consumption of the WURx.
May 2017

## Slide 8: Straw Poll
STA may send a frame carrying a reason of its wake-up due to a unicast wake-up packet to the AP using its PCR, in order to assist the AP in determining whether the STA’s WURx receives a spoofed unicast wake-up packet.
Y/N/A:
May 2017

## Slide 9: Reference
[1]. 11-16-0927-00-0wur-securing-the-wur
[2]. 11-16-1460-01-0wur-wur-mac-discussion
[3]. 11-17-0354-02-00ba-initial-thoughts-on-mac-procedures
May 2017