## Slide 1: WUR Coexistence and Packet Format
Date: 2017-05-08
Authors:
Authors:

## Slide 2: Introduction
From 11ba PAR: “The WUR devices coexist with legacy IEEE 802.11 devices in the same band”
WUR transmission needs to be protected from legacy 802.11 devices
In this presentation two options of WUR coexistence methods and corresponding packet formats are discussed
  L-SIG based
  CTS based

## Slide 3: L-SIG Based Coexistence
WUR packet starts with a legacy preamble and relies on the L-SIG length field for protection
  Legacy preamble is intended for legacy .11 OFDM devices and does not need to be decoded by WUR receiver
    WUR receiver may use it for coarse AGC setting
  Protection duration up to 5.6ms
  Slightly lower overhead than CTS based approach
Issue of power variation between legacy preamble and OOK portion
  Due to the PSD limits in many geographical regions, narrowband OOK signal may have to be transmitted at lower power
    Leads to sudden drop in the power between legacy preamble and OOK portion
      Maybe seen as signal/carrier loss by some legacy devices and degrade the protection
    If legacy preamble power is lowered to the level of OOK portion, the L-SIG protection range may be hurt.

## Slide 4: WUR Packet Format with Legacy Preamble
Why one additional OFDM symbol, WUR Mark, is needed after L-SIG?
  Devices search for a Q-BPSK HT-SIG (to detect the packet as 11n) using the 1st symbol after L-SIG
  Narrowband WUR signal may cause a false positive in Q-BPSK check which is performed on 20MHz BW
    Leads to misclassification of the WUR signal as 11n signal
      Once that happens, the devices try to check for an HT-SIG CRC, and failure of which forces those devices to go back to energy detect and not respect L-SIG duration
L-STF
L-LTF
L-SIG
WUR signal
WUR Mark
Pre-WUR (OFDM)
WUR (OOK)

## Slide 5: WUR Mark Symbol
WUR Mark symbol has to be BPSK modulated to avoid misclassification to 11n
The content of the WUR Mark symbol is open for discussion.
  WUR Mark can contain some information for future generation devices to identify and understand WUR packet
  One example: WUR Mark using MCS0 can carry 24 bits
    6 bits for BCC encoding tail.
    8 bits for CRC + Signature to identify WUR frame
    6 bits BSS color
    4 bits TBD
L-STF
L-LTF
L-SIG
WUR signal
WUR Mark
Pre-WUR (OFDM)
WUR (OOK)

## Slide 6: CTS Based Coexistence
WUR packets are all modulated by narrowband OOK
  Also opens the door for WUR signal to be deployed in non-20MHz channel
Protection provided by proceeding CTS
  Can support longer duration of protection. NAV setting up to 32ms.
  Can provide protection to multiple cascade WUR packets
CTS
WUR signal

## Slide 7: Summary
Two options of WUR coexistence methods are discussed
  Legacy preamble (L-SIG) based approach is slightly preferred due to its lower overhead
WUR frame format with legacy preamble is proposed
  A BPSK modulated ‘WUR Mark’ symbol after L-SIG is needed to avoid 11n misclassification

## Slide 8: Strawpoll 1
Which option of WUR packet format do you support
  Option 1: with legacy preamble
  Option 2: both with and without legacy preamble

## Slide 9: Strawpoll 2
If WUR packet has a legacy preamble portion, do you support the packet format as shown below
  WUR mark is a BPSK modulated symbol. The content is TBD
L-STF
L-LTF
L-SIG
WUR signal
WUR Mark
Pre-WUR (OFDM)
WUR (OOK)