## Slide 1: Discussion of CID 9021
Date: 2017-05-05
Authors:

## Slide 2: CID 9021

## Slide 3: Discussion
Purpose of PE is to extend RX processing time without changing CCA
  PE does not have content that needs to be processed at the receiver
  As such, no strictly defined format or content required
However, “arbitrary” may be too loose
  Specifically, this includes possible PE formats that can cause leakage outside of the RU that is used by the PPDU
    See illustrations on next slides
  Doing so could cause intermittent noise to systems sharing the channel
Additional constraints on PE may be needed
  Prevent formats leading to undesirable behavior
  Leave sufficient freedom for implementers to determine the format

## Slide 4: Example
Signal:
  80 MHz OFDMA, one RU occupying 242-tone RU 3
  TXTIME 288 usec
  16 usec Packet Extension
Tested two Packet Extension formats
  Type I: Random Gaussian samples (average power identical to signal)
  Type II: Cyclic extension of last symbol
-40
-20
0
20
40

## Slide 5: Spectrogram of HE PPDU with two different PE realizations
16 msec PE consisting of Gaussian signal
PE creates considerable signal
outside of the RU
16 msec PE consisting of cyclically extended signal
PE signal is contained
within the RU

## Slide 6: Spectrogram of HE PPDU with two different PE realizations
16 msec PE consisting of Gaussian signal
16 msec PE consisting of cyclically extended signal

## Slide 7: Another (bad) example
PE completely outside of RU
Doesn’t even fulfil the intended purpose of PE (maintain CCA state)
BUT: fully compliant with current specification for PE
  Same average power as Data field
  Arbitrary content

## Slide 8: Conclusion
PE as currently specified allows for undesirable behavior
PE built from random samples can create significant “out-of-RU” leakage
This will affect systems using the spectrum not occupied by OFDMA payload
Problematic for e.g. punctured preamble cases
  Puncturing is intended to free up unused spectrum to other systems
16 usec noise will typically corrupt up to two symbols
  Non-stationary noise
Definition of PE should be enhanced to eliminate bad options

## Slide 9: Possible resolutions
Explicitly specify PE format
  Probably too stringent
Requirement on power distribution, in addition to power level
Informative note
  Purpose of PE
  Guidelines on proper signal

## Slide 10: Proposed resolution
Modify the first paragraph of 28.3.12 as follows:
28.3.12 Packet extension
An HE PPDU may have a Packet Extension (PE) field appended at the end of the PPDU, with possible durations
being 0 μs, 4 μs, 8 μs, 12 μs, or 16 μs. The PE field, when present, shall be transmitted with the same average
power as the Data field and shall not cause significant power leakage outside of the spectrum used by the Data field.
Other than that, and its content is arbitrary.