## Slide 1: Wake up packet contents
Date: 2017-05-08
Authors:

## Slide 2: Background
Wake-up packet (WUP) structure is proposed in [1-5]
  Widely agreed to include legacy preamble part, WUP preamble part and WUP payload part.
  Legacy preamble to protect the WUP packet and spoofing other legacy devices
  WUP preamble part transmits in lowest supported rate. This part help WUR to:
    Adjust AGC, synchronization, packet detection and signal the rate of the following WUP payload part [6].
  WUP content part shall include type field, Tx id field and other contents vary for different type of WUPs.
    Possible type includes WU beacon, individual WUP, group WUP etc.
Legacy preamble part
WUP preamble
Contents in WUP payload
Frame type
Transmitter ID
Receiver ID
OOK modulated part
Other information
May not include
Receiver ID in
Some WUP types.

## Slide 3: WUP contents for WU beacon
WU beacon [7] will be defined to maintain connection and synchronization for WUR STAs.
  TSF is proposed for synchronization. Other information TBD.
We propose to allow WU information appending to the beacon
  Can save the overhead and smaller latency with no cost.
    A specific type can be defined for WU beacon with appended WU info
    Appended field can be Receiver ID or Group ID with additional control information such as wake up complete time(WCT) and access category (AC) etc.
    May use a length field in the appended info to indicate the length of the appended part.
Legacy preamble part
WUP preamble
WUP contents
Frame type
Transmitter ID
TSF
TBD info
type = BEACON
Appending WU info
Receiver ID/Group ID
Length
Type = BEACON with WU info
Control info

## Slide 4: Content of WUP for single WUR
Propose to include a priority/Access category field
  Priority field indicates the highest AC of the buffered DL data for the target STA.
  This field can be 2 bit access category (AC_VO,AC_VI,AC_BE,AC_BK).
  Benefit:
    WU STA can send PS_POLL based on the indicated access category.
    WU STA can decide whether wake up or not. In low battery mode, STA may choose to wake up less frequently or wait until higher priority data arrives.
TSF field should be included in all WUPs.
  Help WU STAs in duty cycle mode to synchronize the clock more often. With more precise timing, duty cycle WU STAs can wake up less time for each wake up window and further save the power.
Legacy preamble part
WUP preamble
WUP contents
Frame type
Transmitter ID
Receiver ID
Priority (AC)
TSF
type = SU
Other info such as WCT etc.

## Slide 5: Contents of WUP for a group of STAs
Group ID with a TIM is proposed in [2]. We propose to include a per user field for each WUR STA in the group to be woken up.
  Similar to 11ax HE SIG B, number of per user field and order of per user field is decided by the TIM field. Per user field can include the AC for this user and other TBD control information.
  WCT can also be signaled in per user field to be more flexible or signaled outside the per user field as a common WCT to save the overhead.
Legacy preamble part
WUP preamble
WUP contents
Frame type
Transmitter ID
Group ID
TIM for group
Per User fields
Common WCT
TSF
type = Group
0 0 1 … 0 1 0
Per User field 1
N bits TIM
Per User field 2
…
Per User field K
Indicating user 1
user K

## Slide 6: Segmented error check for WUP
We propose to use multiple FCS to check segments of a WUP.
  Different part of WUP has different importance. Some information are more essential while other information improve the performance but WUR still works without it. Check segments separately will help improve the WUR performance.
  One FCS to check the essential segment including frame type, transmitter ID, receiver ID fields etc. If this segment failed, the whole WUP shall be discarded.
  WUR still works without WCT, AC and TSF field etc. These fields shall be placed in other segment(s). The non-essential information fields can also be partitioned into segments and check by separate FCSs. More FCSs will help increase the total number of correctly received information fields.
Legacy preamble part
WUP preamble
WUP contents
Essential segment, including field like
Frame type, Tx id, Rx id etc.
Segment 2
FCS
FCS
Segment 3
FCS

## Slide 7: SP 1
Do you support to allow wake up information fields appending to the WUR beacon?
  Y:
  N:
  Abs:

## Slide 8: SP2
Do you support to include access category field in wake up packet?
  The access category field indicates the highest AC of the queueing data for the target STA
  Y:
  N:
  Abs:

## Slide 9: SP3
Do you support to include per user fields in group addressed WUP?
  Y:
  N:
  Abs:

## Slide 10: SP4
Do you support to use multiple FCSs to separately check the segments of a WUP?
  Y:
  N:
  Abs:

## Slide 11: Reference
[1] 11-17-0036-02-00ba-wur-frame-structure
[2] 11-17-0054-03-00ba-wur-mac-issus
[3] 11-17-0066-00-00ba-wur-packet-design
[4] 11-17-0124-01-00ba-wur-mac-and-wakeup-frame
[5] 11-17-0352-01-00ba-wur-frame-structure-follow-up
[6] 11-17-0679-00-00ba WUR packet format and preamble design
[7] 11-17-0343-03-00ba-wur-beacon