## Slide 1: Follow-up on Update Wake-Up Information in WLAN with Wake-Up Radio Receivers
Date: 2017-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: False Wake-up Problems
      Main applications of WUR WLANs include IOT sensors running on batteries. Frequently falsely wake up the main receiver for a regular data packets can quickly drain the battery and ultimately disable the device.
      The following false wake-ups can happen in WUR WLAN
        False wake-ups due to wake-up information collisions in dense OBSS environment;
        Wake-up attacks by self-generating wake-up information or re-play wake-up information.
      When a WUR station detects the false wake-ups or wake-up information collisions, WUR information should be updated or re-assigned.

## Slide 3: Assign or Update Wake-up Information
Wake-up information of WUR STAs are assigned for each STA either:
  As part of the onboarding process, like how a password or a client certificate is provisioned to a STA before it is associated to an AP
  Or as part of the authentication and session key generation process
          Wake-up Information updating can be initiated either by STAs via sending a wake-up information change request or by the AP via sending a packet that contains wake-up information change entities directly.
  A WUR STA can initiate a request to change the wake-up information
    When a STA repeatedly wakes up, but no meaningful regular packet is received or the received packet is not for itself. Then the STA can initiate a process of update of wake-up information
  AP can initiate the update of wake-up information
    When an AP detects there are collisions of wake-up information from OBSS or AP needs to re-assign the wake-up information for a STA or a group of STAs, then AP can initiate the update of wake-up information directly.

## Slide 4: Wake-up information updating
For wake-up information updating, it is important to make sure that both the AP and the WUR station know if the update is successful.
  A simple send the packet and receive ACK scheme may not work well. For example, if the AP sends the packet with wake-up information update information, the WUR station updated its wake-up information, but the ACK is failed at the AP. Then the AP does not know if the WUR station has updated its wake-up information or not.
The wake-up sequence update or assign is regarded as complete only after successful hand-shaking frame exchange.

## Slide 5: Sequence of Wake-Up information Update – Immediate ACK Case
ACK

## Slide 6: Straw Poll #1
Do you agree that IEEE 802.11ba shall provide a Wake-Up information update mechanism?

## Slide 7: Straw Poll #2
Do you agree with the packet exchange sequence for information (related to wake-up receiver) update shown in slide #5?
  The detailed frame formats are TBD.