## Slide 1: BSS color updated for TWT STAs
Authors:
Date: 2017-03-22

## Slide 2: CID 9574
9574 | 181.01 | 1 | 27.7.2 |  |  | If a TWT STA is not required to listen to beacon frame, it may need a mechanism to update the BSS information when AP udpates BSS info in the beacon frames. | define a rule or mechanism for TWT stations to synchronize the BSS information change when AP updates the BSS information in beacon frame.

## Slide 3: Background
The following text is included in 11ax Draft1.2 [1]
  An HE AP sets the BSS Color Disabled subfield in the HE operation element to 1 if the HE AP decides to disable the use of the BSS color for the BSS that it serves, for example, after detecting a BSS Color overlap in the neighborhood as described in 27.11.4 (BSS_COLOR).
  The BSS Color Change Announcement element is used by an HE AP to advertise a BSS Color change and the value of the new BSS color
Both the BSS Color Change Announcement element and the HE operation element are optionally present in Beacon，Probe Response (Re-)Association response frame.
11ax Draft1.2 also specifies: An HE STA that successfully sets up an individual TWT agreement and operates in PS mode shall not be required to listen to Beacon frames as defined in 11.2.2.1 (General)

## Slide 4: Discussion
  TWT STAs may not be able to get the updated information about BSS color Disabled/Change timely without listening to the beacon frame.
  For TWT scheduled STAs，the TWT scheduling AP may notify them to listen to the Beacon by sending a TIM frame with the check Beacon field setting to 1 at the beginning of the broadcast TWT SP when the AP decides to disable or change the BSS color for the BSS that it serves.
  With the check Beacon field in TIM frame, TWT STAs can not utilize the current TWT SP until it received the update BSS color information.
  Another way to notify the update info about BSS color is through probe response frame in TWT SP. However it is not efficient when ONLY the BSS color related information is changed.

## Slide 5: Proposal
  We propose a scheme to indicate the BSS Color related update information for both TWT scheduled and TWT requesting STAs in the TWT SP.
    AP indicates the BSS color related information in the TWT SP by reusing the DTIM Count field of the TIM element in TIM frame which is reserved.
    the Check Beacon field of a TIM frame remains unchanged when BSS color is disabled or updated ;
    Set Bit0 of the DTIM Count field to 1 to indicate BSS Color disabled ;
    Bit 1~6 of the DTIM Count field indicate the BSS color;
    Bit 7 is reserved;
    Pros :TWT STA can get the update info within its TWT SP and avoid waking up to receive the next beacon frame

## Slide 6: Summary
  We discussed the current available ways for TWT STAs to get the updated information about BSS color Disabled/Change.
  Propose to indicate the BSS Color related update information for both TWT scheduled and TWT requesting STAs in the TWT SP.
  With the proposed scheme, the TWT STA can get the BSS color update info within its TWT SP without waiting for the next beacon frame

## Slide 7: Proposed text change(1)
The text change to the current Spec is as follows:
  9.4.2.6 TIM element
    When included in TIM frames and FILS discovery frames at the beginning of a broadcast TWT SP by an HE AP:
      — Bit 0 of the DTIM count field is reserved set to 1 to indicate the BSS color disabled，otherwise it set to 0 . Bit 1~6 indicates BSS color. Bit 7 is reserved.
    The Length field may set to 4 to indicate that the partial virtual bitmap is not present in TIM frame when it is sent in an individual TWT SP .
  11.2.2.17 TIM Broadcast
    The AP shall increase the value (modulo 256) of the Check Beacon field in the next transmitted TIM frame(s) when a critical update occurs to any of the elements inside the Beacon frame. The following events shall classify as a critical update:
      m) Modification of an HE Operation element except when only the BSS color related information is updated. eg. BSS color disabled field is set to 1
      o) Inclusion of BSS Color Change Announcement element

## Slide 8: Proposed text change(2)
The text change to the current Spec is as follows:
  27.14.3.1 AP operation for opportunistic power save
    An HE AP sends a TIM frame with Bit 0 set to 1in the DTIM Count field to indicate the BSS color is disabled and advertise the BSS color in the broadcast or individual TWT SPs.

## Slide 9: Straw Poll 1
Do you agree that the AP can inform the BSS color updated information in the TWT SP?

## Slide 10: Straw Poll 2
Do you agree the proposed text change in slide 9 and 10?

## Slide 11
[1] IEEE P802.11ax/D1.1, February 2017
[2] IEEE P802.11-2016