## Slide 1
WUR retransmission procedure
Date: 2017-05-08
Authors:

## Slide 2: Introduction
The wake-up radio transmission procedures are agreed [1]
  4.5.2 Unicast Wake-up Operation
    R.4.5.2.B: A STA should send a response frame to the AP using primary connectivity radio after receiving a unicast wake-up packet.
    LP-WUR enables energy efficient data reception mode without increase of latency
  4.5.3 Multicast Wake-up Operation
    R.4.5.3.B: After the transmission of broadcast wake-up frame, the AP can transmit broadcast/multicast frames through primary connectivity radio after the preparation period.
However, the retransmission of wake-up packet may cause power inefficiency and larger transmission delay
  In case of transmitting downlink packet after the wake-up packet, the transmission failure of downlink packet may cause the retransmission of the wake-up packet, with large delay and power consumption in STA
  In case of transmitting response frame to AP after the wake-up packet, the various contention delay or retransmission of the response frame may cause more delay because of the retransmission of the wake-up packet
In this presentation, the retransmission procedure in the wake-up radio mode is discussed.

## Slide 3: Recap: Wake-up radio procedure
Data transmission procedure using Wake-up radio
  After sending the wake-up packet, AP may wait for the wake-up delay, contend to access the channel, and send the downlink packet
  If AP and STA are negotiated to use a response frame, AP may wait for the response frame (WU Poll) first, and then transmit the data frame

## Slide 4: Wake-up packet retransmission procedure
If AP and STA are negotiated not to use a response frame (e.g. multicast wake-up case), the retransmission of wake-up packet is initiated if AP determines that the transmission of the downlink frame has been failed.
If AP and STA are negotiated to use a response frame, the retransmission of wake-up packet is initiated if there is no ACK for wake-up packet for a certain timeout duration.

## Slide 5: Inefficiency in data transmission-w/o response frame in unicast transmission
In case of downlink frame failure (no ACK from STA), the wake-up packet is retransmitted
  STA should wait for long wake-up delay; the delay of the data transmission is increased
  STA should stay in awake state; power is wasted for the wake-up delay

## Slide 6: Inefficiency in data transmission-w/o response frame in unicast transmission
To solve the inefficiency in transmission failure of downlink packet, the retransmission procedure to handle this problem is needed
  AP may check the STA’s wake up status before the retransmission of the wake up packet.
  (The frame format of checking STA’s state may vary)

## Slide 7: Inefficiency in data transmission-with response frame in unicast transmission
If the negotiated wakeup delay time is inaccurate, AP may retransmit the wake-up packet before a response frame from the STA is transmitted; STA should wait for the EIFS duration more before transmitting the response frame
  The contention delay of response frame is longer than the timeout of wake-up packet expiration
  The transmission of the response frame has been failed

## Slide 8: Retransmission procedure - with a response frame in unicast transmission
If a STA is in awake state and PCR is able to decode the wake-up packet, STA can transmit a response frame immediately upon the reception of the wake-up packet.

## Slide 9: Conclusion
In this presentation, we discussed the retransmission procedure in wake-up radio transmission
  The retransmission procedure in case STA transmits a response frame in unicast transmission
  The retransmission procedure in case AP transmits the downlink frame after the wake-up packet
In case of the downlink packet transmission failure w/o a response frame in unicast transmission, checking STA’s state prevents the power waste
In case of a unicast response transmission, an immediate response to the wake-up packet can reduce the delay of poll frame transmission

## Slide 10: Reference
[1] IEEE 802.11-17/0575r0 “Spec framework”

## Slide 11: Straw poll 1
Do you agree to add the followings to 802.11 ba SFD?
  When a response frame to a wake-up packet by the unicast transmission is not required, 802.11ba AP may check the STAs’ status using the primary connectivity radio before the retransmission of wake-up frame.

## Slide 12: Straw poll 2
Do you agree to add the followings to 802.11 ba SFD?
  When a response frame to a wake-up packet by the unicast transmission is required, 802.11ba STA, whose primary connectivity radio has a capability of decoding a wake-up frame, may immediately respond to the retransmitted wake-up frame with a response frame through the primary connectivity radio.

## Slide 13: Motion
Move to add the followings to 802.11ba SFD
  When a response frame of a wake-up packet by the unicast transmission is not required, 802.11ba AP may check the STAs’ status using the primary connectivity radio before the retransmission of wake-up frame.
Move : Hanseul Hong
Second :
Y/N/A :