## Slide 1: Unifying QoS Control and BSR A-Control for Buffer Status Report
Date: 2017-05-03
Authors:
Name | Affiliation | Address | Phone | Email
Zhou Lan | Broadcom Ltd. |  |  | Zhou.lan@broadcom.com
Chunyu Hu |  |  |  | 
Matthew Fischer |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 2: Abstract
TGax spec. defines two mechanisms for buffer status report to assist UL MU scheduling.
  QoS Control and BSR Control
This contribution discusses the problems of BSR Control
  from the perspective of incompatibility with QoS control
  from the perspective of supporting 11ax specific features for performance improvement
    256 BA window
    MCS 1024 QAM
    TWT
This contribution proposes an alternative BSR Control to facilitate 11ax UL MU scheduling

## Slide 3: Problem statement
Contribution 0477r0 [1] pointed out the incompatibility issue of supporting two buffer status report mechanisms
  The Queue Size in QoS Data is reported per TID while Queue Size in BSR A-Control is reported per AC
  All the BA agreements are established based on per TID info
  Eventually the per AC Queue size needs to be separately recorded and converted to per TID Queue size
In addition, QoS Null frame that has both QoS control and BSR Control present is used for solicited BSR report
  AP will get confused if the buffer size in the QoS control conflicts with that in the BSR control
As a results, most implementation will end up with only using QoS control for UL MU scheduling while ignoring the BSR Control.
Providing buffer size info in a different format (i.e. per AC) doesn’t provide significant benefit while complicating the implementation and adding extra overhead

## Slide 4: Problem statement further
Current BSR Control in Draft spec 1.2 is limited in size of 4.1M octets with 1.6K octets scaling factor in both Queue Size High and Queue Size All fields
Per baseline spec, the maximum MPDU size is 11454 octets, in order to support 256 BA window the required buffer size is 11454*256 = 2932224 octets
If the STA supports 2 TIDs with 256 BA agreement, 3*2= 6 M octets is needed in the Queue Size High field
If the STA supports two ACs each supporting two TIDs with 256 BA agreement, 12 M octets is needed in the Queue Size All field
The current BSR Control can not support the above use cases and there is no reserved bits available for further range extension
No reserved bits to further extend the range

## Slide 5: Problem statement (cont.)
The current BSR Control fails to support Multi-TID aggregation due to similar reasoning as presented in the previous slide
  Draft spec. 1.2 support Multi-TID aggregation with 256 BA window
  The current BSR Control will not be able to support Multi-TID aggregation with more than two TID supporting 256 BA window
  In order to support TWT operation, a STA may need to buffer UL data to wait for the next service period
  Assuming the STA is scheduled in a 996 RU with Nss =1 and MCS 11 for 1024QAM
  Assuming the STA is under a TWT agreement of 5ms wake interval
  4M Octets total Queue size for all AC may not be sufficient to support TWT operation

## Slide 6: Proposal
Extend the supported Queue Size of QoS control from 64 768 octets to 1024 K octets as suggested in contribution 0477r0 [1]
Replace the per AC Queue size in the BSR Control with per TID Queue size as follow
  Two per TID queue size fields allow a STA to report each time two TID related queue size with up to 4M octet
  The QoS control field can be used to report an extra TID with queue size up to 1 M octet
These changes together increase the total maximum expressible buffer size from:
  2,996,992 Bytes = 2,932,224 + 64,768
  to:
  9,412,608 Bytes (aka octets) = 1,024,000 + 2 * 256 * 16384
B0 B3 | B4 B11 | B12 B15 | B16 B23 | B24 B25
First TID | Queue Size | Second TID | Queue Size | Scaling factor
4 bits | 8 bits | 4 bits | 8 bits | 2 bits

## Slide 7: Straw poll
Do you support to
  Replace the current BSR Control field with the proposed new BSR Control field as shown in slide 6
  Yes
  No
  Abstain