## Slide 1: EDMG-STF for OFDM
Date: 2017-05-05
Authors:
Name | Company | Address | Phone | Email
Jinmin Kim | LG Electronics |  |  | jinmin1230.kim@lge.com
SunWoong Yun |  |  |  | sunwoong.yun@lge.com
SungJin Park |  |  |  | allean.park@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sang G. Kim |  |  |  | sanggook.kim@lge.com
Saehee Bang |  |  |  | saehee.bang@lge.com

## Slide 2: Introduction
In this contribution, we will deal with the EDMG-STF for OFDM
First, we define the design criteria for EDMG-STF of OFDM packet
Then, we propose the EDMG-STF sequence in single channel

## Slide 3: Design criteria
We consider the criteria below when we design EDMG-STF for OFDM
  Frequency / time domain sequence
  Processing time for L-Header decoding
  Compatible structure to EDMG-STF for SC
  Prevent unintentional BF
  PAPR / correlation performance

## Slide 4: Why should EDMG-STF be defined in the frequency domain?
2 Channel bonding
Slide 4
3.52GHz
2CB in SC
3.99GHz
(1.825*2+0.34)
2CB in OFDM
0.34GHz is additional bandwidth due to channel bonding
There exists 0.47GHz difference between SC and OFDM bandwidth
4 Channel bonding
7.04GHz
4CB in SC
8.32GHz
(1.825*4+0.34*3)
4CB in OFDM
1.02GHz(3*0.34) is additional bandwidth due to channel bonding
There exists 1.28GHz difference between SC and OFDM bandwidth
  BW mismatch is getting worse as CB increases
  It can make incorrect AGC operation if we reuse EDMG STF which was defined in the single carrier

## Slide 5: Processing Time for L-Header decoding
We already define EDMG-STF for SC to be 18+1 sequences of Ga considering L-Header processing time
  (18+1) sequences of Ga take 1.3818us
Similarly, we have to consider L-Header processing time when we design EDMG-STF for OFDM
So, we propose 6 OFDM symbols for EDMG-STF
  1 OFDM symbol(TDFT+TGI) is 0.2424us.
  1.3818us / 0.2424us = 5.7 symbols

## Slide 6: Compatible Structure to EDMG-STF for SC
EDMG-STF for SC can be interpreted as 4 repetitions in a single carrier block. This is effective value for,
  AGC stabilization
  Coarse timing/freq. synchronization
Also, considering 11ad’s CP length(TDFT/4), 4 repetitions in a DFT period make unified structure during EDMG-STF
So, we propose EDMG-STF to have 4 repetitions in a DFT period

## Slide 7: Proposed EDMG-STF for CB=1 (1/2)
The sequence is defined in frequency domain
1st~6th EDMG-STF symbols:
    where “iSTS” is the space-time stream number and 1 ≤ iSTS ≤ 4
    where “iSTS” is the space-time stream number and 5 ≤ iSTS ≤ 8
  The sequences and are defined as follows:

## Slide 8: Proposed EDMG-STF for CB=1 (2/2)
  The sequences and are generated using the following recursive procedure
    for iSTS =1, 2, … , 8
    for iSTS =1, 2, … , 8
    where k defines iteration index, the value of the defines the weight for sequence of iSTS-th space-time stream and k-th iteration

## Slide 9: PAPR performance
The proposed EDMG-STF has acceptable PAPR properties in the table below
  And, all sequences for space-time stream are mutually orthogonal
  4 x upsampling is considered to estimate PAPR
Stream # | W vector | PAPR(dB) | Stream # | W vector | PAPR(dB)
1 | [+1,+1] | 3.00 | 5 | [+1,+1] | 2.99
2 | [+1,-1] | 2.99 | 6 | [+1,+1] | 3.00
3 | [-1,+1] | 2.99 | 7 | [+1,+1] | 3.00
4 | [-1,-1] | 3.00 | 8 | [+1,+1] | 3.00

## Slide 10: Correlation performance
To investigate correlation performance, we use merit factor introduced in [1]
    , where “N” defines sequence length
Proposed sequences have reasonable performance compared to legacy Golay sequences
[1] M.J.E. Golay, “Sieves for low autocorrelation binary sequences,” IEEE Trans. Inform. Theory, IT-23, no. 1, pp. 43-51, 1977
Sequence | Ga32 | Ga64 | Ga128 | Proposed sequence |  |  |  |  |  |  | 
 |  |  |  | Stream 1 | Stream 2 | Stream 3 | Stream 4 | Stream 5 | Stream 6 | Stream 7 | Stream 8
Merit factor | 2.90 | 3.0 | 3.12 | 2.94 | 2.94 | 2.94 | 2.94 | 2.94 | 2.94 | 2.94 | 2.94

## Slide 11: Conclusion
We consider criteria when we design EDMG-STF for OFDM
We proposed EDMG-STF sequence based on design criteria
Proposed sequence has acceptable performance compared to other preambles

## Slide 12: SP/M #1
Do you agree to include the text for EDMG-STF for EDMG OFDM mode in single channel proposed in (11-17-0546-00-00ay-EDMG-STF for OFDM in single channel) to the spec draft?