## Slide 1: EDMG Capabilities for SU-MIMO
Date: 2017-5-08
Authors:

## Slide 2: Introduction
  Draft IEEE802.11ay D0.3 [1] specifies in 9.4.2.250 regarding EDMG Capabilities element.
This contribution discusses and proposes EDMG Capabilities related to SU-MIMO.

## Slide 3: Observation (1/3)
    In multi-path environments, frequency domain equalization (FDM) is necessary to obtain good performance for SC.
M Precoding matrix
T Channel matrix N Receive vector
    Transmit vector:
    Receive vector:
    An example of FDM in 2x2 MIMO:

## Slide 4: Observation (2/3)
Estimated Channel matrix
Estimated Modulated vector
MMSE Detection with FDE (Frequency Domain Equalizer)

## Slide 5: Observation (3/3)
    However, it is difficult to obtain good performance in multi-path environments when using the only MIMO linear (e.g. MMSE) detection with FDM in SC. Therefore, in order to obtain performance in SC similar to OFDM, introduction of serial interference cancellation or MLD considering multi-path at receivers is necessary in SC.
    This means that the complexity of MIMO detection for SC will have lager than that for OFDM. In particular, performance is worse in increase of the number of streams in SC.
    Therefore, we propose separate maximum number SU-MIMO spatial streams capability information in SC and OFDM.

## Slide 6: PHY Capability field
Draft IEEE802.11ay D0.3 [1] specifies in 9.4.2.250.5 regarding PHY Capability field in EDMG Capabilities element as follows.
Figure 26 – PHY Capability field format
 | B0 | B1 | B2 | B3 | B4 B7
 | PH Supported | Open Loop Precoding Supported | DCM SQPSK Supported | Long LDPC CW Supported | Reserved
Bits: | 1 | 1 | 1 | 1 | 4

## Slide 7: Proposed field in PHY Capability field
Both “Maximum Number SU-MIMO Spatial Streams Supported” field for SC and OFDM should be specified in the PHY Capability field, because the complexity of MIMO detection for SC will have larger than that for OFDM.
Name | Number of bits | Description
SC Maximum Number SU-MIMO Spatial Streams Supported | 3 | This field indicates the maximum number of SU-MIMO spatial streams for SC that the STA can demodulate. The value of this field is in the range 1 to 8, with the value being equal to the bit representation plus 1.
OFDM Maximum Number of SU-MIMO Spatial Streams Supported | 3 | This field indicates the maximum number of SU-MIMO spatial streams for OFDM that the STA can demodulate. The value of this field is in the range 1 to 8, with the value being equal to the bit representation plus 1.
Table: Proposed PHY Capability field

## Slide 8: Summary
It is proposed to include 6(=3x2) bits related to SU-MIMO in the PHY Capability field of the EDMG Capabilities element.
SC Maximum Number SU-MIMO Spatial Streams capability information (3 bits)
OFDM Maximum Number SU-MIMO Spatial Streams capability information (3 bits)

## Slide 9: Straw poll
  Do you agree to add the following capability information in the PHY Capability field of the EDMG capabilities element, as shown in 11-17-0757-00-00ay-text-for-phy-capability-field-in-edmg-capabilities-element, into the Draft IEEE802.11ay specification?
  - SC Maximum Number of SU-MIMO Spatial Streams Supported
  - OFDM Maximum Number of SU-MIMO Spatial Streams Supported

## Slide 10
Reference
Draft P802.11ay_D0.3