## Slide 1: “Near-far” self-classification capabilities of EDMG STAs
Authors:
Name | Affiliation | Address | Phone | Email
Alexander Maltsev | Intel | Turgeneva 30, Nizhny Novgorod, 603024, Russia | +7 (831) 2969444 | alexander.maltsev@intel.com
Ilya Bolotin | Intel |  |  | ilya.bolotin@intel.com
Andrey Pudeyev | Intel |  |  | andrey.pudeyev@intel.com
Artyom Lomayev | Intel |  |  | artyom.lomayev@intel.com
Oren Kedem | Intel |  |  | oren.kedem@intel.com
Hiroyuki Motozuka | Panasonic |  |  | motozuka.hiroyuki@jp.panasonic.com
Gaius Wee | Panasonic |  |  | yaohuang.wee@sg.panasonic.com
Takenori Sakamoto | Panasonic |  |  | sakamoto.takenori@jp.panasonic.com

## Slide 2: Problem statement
In accordance with Candidate Draft P802.11ay_D0.3 in beamforming procedure for the asymmetric link each STA tries to perform negotiation in A-BFT and then, if it fails, STA performs negotiation in Beamforming training (BFT) allocation during the DTI. Thus the far away EDMG STAs in new outdoor dense deployment scenario will perform a lot of useless transmissions in A-BFT producing undesirable collisions and interference.
Therefore, it is desirable to sort the STAs by its range and capabilities, and separate the EDMG STAs that can be served with the legacy procedure (negotiation in A-BFT and access in legacy allocations) from the EDMG STAs that can be served only by using the directional transmission-reception.

## Slide 3: Near-far self- classification (1/3)
The AP should provide its capabilities to the STAs. With knowledge of the AP parameters, its own parameters and RSSI measurements, the EDMG STA can decide, whether its transmitted signal can be reliably received by the AP in quasi-omni mode (in A-BFT and legacy allocations), or it should try to negotiate during the BFT allocation.
The EDMG STA can go through the legacy procedure (negotiation in A-BFT and access in legacy allocations) if the inequality (2) below is satisfied:
(1)
(2)

## Slide 4: Near-far self- classification (2/3)
Substituting (1) in (2) we obtain
(3)
We can denote PAPsensitivity as follows: PAPsensitivity = Pmin_sensitivity - GAPadd_gain
where Pmin_sensitivity is the receiver sensitivity in 11ad, and GAPadd_gain is additional sensitivity gain at the receiver of the AP (due to specific implementation)
The final condition to classify STA as “near” looks like:

## Slide 5: Near-far self- classification (3/3)
 | B0 | B1 B9 | B10 B15 | B16 B17 | B18 | B19 B22 | B23
 | Direction | CDOWN | Sector ID | DMG Antenna ID | Quasi-omni TX | PCP/AP Coverage Parameter | Reserved
Bits | 1 | 9 | 6 | 2 | 1 | 3 | 2
To implement this solution in the standard, the DMG Beacon frame, broadcasted by AP in BTI, should contain the quantized value for PCP/AP Coverage Parameter:
PCP/AP Coverage Parameter = (EIRPAP – GAPomni_rx – GAPadd_gain) (4)
3 bits of the SSW field in the DMG Beacon (see Figure 47, in Candidate Draft P802.11ay_D0.3) may be able to contain the quantized value (4):
Codes 0-7: 14 – 42 dBm (4 dB quantization step)
NOTE: as far as antenna gain values in (4) may vary depending on the direction, the value of PCP/AP Coverage Parameter may be sector-specific

## Slide 6: The behavior of EDMG STA with “near-far” self- classification capability

## Slide 7: SP/M #1
Do you agree to include the text for “Near-Far” self-classification capabilities of EDMG STAs proposed in (11-17-0764-02-00ay-text-near-far-self-classification-capabilities-of-edmg-stas) to the spec draft?

## Slide 8
BACKUP

## Slide 9: AP Coverage Parameter range estimation
AP Coverage Parameter = (EIRPAP – GAPomni_rx – GAPadd_gain)
EIRPAP – GAPomni_rx
Upper limit: FCC requirements for 60GHz - EIRP < 43dBm. GAPomni_rx > 0
Lower limit: the 11ad standard defines the maximal difference between peaks of directional and quasi-omni patterns as 15 dB (20.10.1 of 11mc). We are confident that for 11ay, where the large antenna arrays will be used, this difference will be higher:
GAP – GAPomni_rx > 15dB => EIRPAP – GAPomni_rx > 20dBm
GAPadd_gain
Upper limit: this parameter is the gain over the sensitivity defined in Table 20-3. The values in that table were obtained under assumption of 5 dB implementation loss and 10 dB noise factor. So, the theoretical maximum of GAPadd_gain is 15dB. However, we are confident, that, in reality, this value will not be more than 6dB. GAPadd_gain < 6dB
Lower limit: the value is definitely positive as otherwise it will not satisfy the minimal sensitivity defined in Table 20-3. GAPadd_gain > 0dB
14dBm < (EIRPAP – GAPomni_rx – GAPadd_gain) < 42dBm

## Slide 10: AP antenna gain value mismatch impact
GAPtx considered in this proposal is a peak AP antenna gain
There will be cases where the signal was received by STA not in the peak gain. So, the value, provided by AP (GAPmax), will be higher than actual value (GAPtx = GAPmax – GAP_mismatch).
The AP antenna beamforming mismatch leads to the overestimation of Pathloss in equation (1) and, therefore, can be considered as an additional margin for criterion (3). So, STA will define itself farther than it actually is. The reduction of this effect may be done by proper correction of AP Coverage Parameter.