## Slide 1: MU-MIMO codebook based transmission flow in IEEE802.11ay
Authors:
Name | Affiliation | Address | Phone | Email
Alexander Maltsev | Intel | Turgeneva 30, Nizhny Novgorod, 603024, Russia | +7 (831) 2969444 | alexander.maltsev@intel.com
Ilya Bolotin | Intel |  |  | ilya.bolotin@intel.com
Andrey Pudeyev | Intel |  |  | andrey.pudeyev@intel.com
Artyom Lomayev | Intel |  |  | artyom.lomayev@intel.com

## Slide 2: Abstract
This presentation proposes the MU-MIMO codebook based transmission flow for IEEE802.11ay. The flow contains the Enhanced SLS beamforming which provides extended coverage and beam training for both TX and RX of all EDMG STAs. The proposed MU-MIMO transmission flow also contains scheduling procedure. System level simulations have shown that such training is enough accurate to establish MU-MIMO links with high throughputs.

## Slide 3: MU-MIMO channel access and transmission flow

## Slide 4: Enhanced SLS
DTI
A-BFT
BTI
BTI
DTI
BFT allocation
Directional CBAP/SP
Far away STAs

## Slide 5: MU Grouping and Scheduling
During Enhanced SLS EDMG STA reports to PCP/AP several best sectors defined during BTI to give the PCP/AP scheduler more flexibility in MU grouping.
The Destination AID field of the Allocation field of the Extended Schedule element may contain the Group ID.
To associate a Group ID with a group of STAs a EDMG Group ID Set element is already defined in D0.3 (9.4.2.254 EDMG Group ID Set element). It should be sent together with Extended Schedule element in DMG Beacon or Announce frames.
But the EDMG Group fields in the EDMG Group ID Set element should contain not only the STAs AIDs but also the indexes of the AP TX sectors (from the best sectors reported by STAs) which will be used by the AP for transmission to each STA in MU mode of operation.
Bits 8 8 2 8 2 8 2
Octets 1 1 1 1 11 11

## Slide 6: DL MU-MIMO transmission flow
AP reserves space-time slots for ACK and feedback for each STA.
Timing and order of ACK transmission follows the order of STAs in EDMG Group fields.

## Slide 7: System level simulations
To demonstrate that codebook-based AWVs, obtained during the Enhanced SLS BF phase, are enough accurate to establish MU-MIMO links with high throughputs, the system level simulations based on IEEE 802.11ad OFDM PHY were carried out. The comparison between two types of antenna systems configurations and beamforming was done:
  Full adaptive antenna (FAA) array with SVD-based wideband beamforming and scheduling
  Multi-Stream Phased Antenna Array (MS PAA) with codebook-based wideband beamforming and scheduling (2D DFT codebook was used)
2D DFT codebook for 8x16 antenna array

## Slide 8: System level simulator parameters
Parameters |  |  | Assumption
Deployment |  |  | Open area, Street canyon, Hotel lobby
Channel model |  |  | Quasi-Deterministic Open area, Street canyon, Hotel lobby
Carrier / BW |  |  | 60 GHz / 2,16 GHz
AP antenna array | Height |  | 6m
 | Configuration |  | 8x16 elements
 | TX power |  | 19 dBm
 | Gain |  | 26 dBi
STA antenna | Height |  | 1.5m
 | Gain |  | Omni, 0 dBi
Transmission scheme |  |  | DL MU-MIMO w TPC
AP antenna array type/BF |  |  | FAA/Wideband SVD based MS PAA/Codebook-based 2D DFT
Number of RF chains |  |  | FAA – 128 MS PAA – 8
Channel estimation |  |  | Perfect
Scheduling |  | Type | Greedy PF MU scheduling
 |  | Traffic load | Full buffer

## Slide 9: Simulation results
Scenario | AP antenna array model and beamforming scheme | AP throughput, Gbps | Avg. user throughput, Mbps | Cell-edge user throughput, Mbps | Avg. size of MU group
Open area | FAA/Wideband SVD | 10.2 | 205 | 107 | 4.8
 | MS PAA/Codebook based | 7.2 (-29%) | 144 | 70 | 3.8
Street canyon | FAA/Wideband SVD | 10.0 | 222 | 81 | 2.5
 | MS PAA/Codebook based | 7.8 (-22%) | 173 | 75 | 2.3
Hotel lobby | FAA/Wideband SVD | 17.0 | 848 | 484 | 4.5
 | MS PAA/Codebook based | 11.5 (-32%) | 575 | 367 | 3.5
The system level simulations for DL MU-MIMO mode in main large area dense environments have shown that the MS PAA codebook-based 2D DFT wideband beamforming (which can be realized by using the proposed transmission flow) demonstrates acceptable degradation (20-30%) comparing to the FAA SVD-based wideband beamforming.
Note: FAA array requires a number of RF chains equal to the number of antenna array elements (here 128), while the MS PAA requires the number of RF chains equal to the number of streams (which here was limited by 8).

## Slide 10: Simulation results
Figures below demonstrate the average number of STA in MU group in codebook-based MU-MIMO versus the number of best AP TX sectors reported to AP by each STA
As it can be seen from the simulation results, for efficient MU-MIMO grouping it is sufficient for EDMG STA to report only two AP TX sectors, received by EDMG STA with best quality in BTI. It may give up to 8% throughput increasing in complex multipath channels.

## Slide 11: SP/M #1
Do you agree to include to the spec draft the text:
“EDMG Group fields of EDMG Group ID Set element should contain the STAs AIDs and the corresponding indexes of the AP TX sectors (chosen from the best sectors reported by STAs), which may be used by the AP for transmission to each STA in MU mode of operation.”