## Slide 1: Thoughts on Doppler Design in 802.11ax
Date: 2017-05-09
Authors:
Name | Affiliation | Address | Phone | Email
Lochan Verma | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | lverma@qti.qualcomm.com
Bin Tian |  |  |  | btian@qti.qualcomm.com
Sameer Vermani |  |  |  | svverman@qti.qualcomm.com
Youhan Kim |  |  |  | youhank@qca.qualcomm.com
Lin Yang |  |  |  | linyang@qti.qualcomm.com

## Slide 2: Introduction
802.11ax D1.0 has 1 bit in HE-SIG-A to signal Doppler mode but no procedure for Doppler is provided
  It is needed to support outdoor mobility use cases (e.g., Drones)
Doppler design options
  802.11ah Walking pilot based approach
  Mid-amble based approach
  Leave Doppler handling to implementation. No Spec. changes
    e.g., Rx data aided channel update
This slide-set is an introduction to the Mid-amble based Doppler design for 802.11ax

## Slide 3: What is a mid-amble
A mid-amble has one or many HE-LTF symbols
  # of HE-LTF symbols is a function of # of space-time streams (Nsts)
  HE-LTF can be used for channel estimation updates
Need for an HE-STF in a mid-amble is open for discussion
  Generally, amplitude variation through the packet duration not significant
  HE-STF may not be needed for AGC adjustment
Mid-amble frequency represents the number of data symbols between two mid-ambles
Coding is continuous across mid-amble
L-STF
L-LTF
L-SIG
RL-SIG
HE-SIG-A
HE-SIG-B
HE-STF
HE-LTF1
HE-LTFn
…
Data Symbol
…
Mid-amble
Data Symbol
…
Mid-amble
Data Symbol
PE
Mid-amble Frequency
HE-LTF1
HE-LTFn
…

## Slide 4: Benefits of Mid-amble over Walking Pilot-based Doppler Design
Mid-amble based approach | Walking Pilot based approach
Applicable to wide range of Doppler speeds | Difficult to adapt this approach to different Doppler speeds - Channel update interval is fixed
Applicable to all RU sizes | Needs study -Pilot density for 80 MHz (16/996) may be insufficient
Easily extensible to multiple streams | Have to sacrifice either on channel estimation update interval or frequency selectivity related loss while extending to multiple streams
In our view, slightly simpler implementation - No change to the channel estimation signal processing; just re-done multiple times in a PPDU | 

## Slide 5: Simulation Setup
Channel : UMI-NLOS; 5 GHz
Ntx = Nrx = 2; NSS = 1; STBC: Off
MCSs = 0, 1, 3, and 5
GI = 3.2 us
Doppler
  15 Km/h on all taps
  30 Km/h on all taps
  60 Km/h on all taps
  60 Km/h on 2nd and 3rd tap and all other taps at 3 Km/h

## Slide 6: Mid-amble frequency Ntx = Nrx = 2; NSS = 1
Doppler/MCS | BPSK (MCS0) | QPSK (MCS1) | 16 QAM (MCS3) | 64 QAM (MCS5)
60 Km/h on 2nd/3rd tap | 50 | 30 | 15 | 8
60 Km/h on all taps | 30 | 20 | 10 | 5
30 Km/h on all taps | 60 | 40 | 20 | 10
15 Km/h on all taps | 120 | 80 | 40 | 20
Mid-amble frequency for 1 ~ 2 dB performance loss @ 10% PER compared with No Doppler

## Slide 7: Summary
We introduced the Mid-amble based Doppler design for 802.11ax
  A mid-amble has one or many HE-LTFs
  HE-STF may not be present in mid-amble
  Coding is continuous across mid-ambles
The benefits of mid-amble based Doppler design over walking pilot-based Doppler design are enumerated
Preliminary simulation results depicting the mid-amble frequency for various Doppler speeds and MCSs are provided

## Slide 8: SP#1
Which Doppler Design option do you prefer for 802.11ax?
Option 1: Mid-amble based approach
Option 2: 802.11ah Walking pilot based approach
Option 3: Leave the Doppler handling to implementation

## Slide 9: SP#2
If mid-amble is adopted, the coding shall be continuous across mid-ambles?
Y/N/A