## Slide 1: Ranging PHY Security
Date: 2017-05-09
Authors:

## Slide 2: Abstract
This presentation conveys some reflections on choices of UL MU ranging options for location in light of the Rx power imbalances that can be present among UL MU users when they are received by an AP.

## Slide 3: UL MU Limitations for Ranging Measurements
11ax specifies support for two classes of client devices
  Class A, TX output power accuracy +/- 3dB and RSSI accuracy +/-3dB resulting in 12dB power discrepancy between peers for UL MU operation
  Class B, TX output power accuracy +/- 9dB and RSSI accuracy +/-5dB resulting in 28dB power discrepancy between peers for UL MU operation
UL MU operations may practically limited to Class A devices
  Tx power imbalance from Class B devices may caused too high errors in channel estimation and interference in data demodulation
Class B devices likely to be scheduled using temporal multiplexing for UL transmissions
Two approaches we could take
  Approach 1- allow spatially multiplexed UL MU ranging for Class A devices only and use temporally multiplexed UL MU ranging for Class B devices
    Results in two modes - Might not be desirable
  Approach 2 – support only temporally multiplexed UL MU ranging for both Class A & B devices
    Trading off potential downsides for Class A devices

## Slide 4: Ranging PHY Security Attacks
Levels of attacks
Denial of service attack:
  The attacker interferes with the ranging signal such as to generate a denial-of-service attack. This is very hard to protect from.
Perturbation attack:
  The attacker is interfere with the victim’s ranging, but is the attacker is not able to control the resulting perceived range.
Spoofing attack:
  The attacker interferes with the victim’s ranging and is able to control the victim’s perceived range.
The spoofing attack is the most dangerous kind of attack as it has the greatest potential to provide an incentive for the attacker.

## Slide 5: Overlay Attack on NDP based Ranging
Initiator
Responder
NDPA
NDP
T1
T3
T4 or T4*
T2 or T2*
Computed incorrect RTT* = (T2*-T1 + T4* – T3)/2
Attacker
NDP Attack
T2/T2* and T3 feedback
Example training sequence overlay attack
NDP
NDP Attack

## Slide 6: Example PHY Security Techniques (1)
Phase encoding of LTF base sequence:
Apply varying phase rotations to the LFT base sequence
High variability in training sequence
May affect PAPR
Using sequences with good PAPR can be an option
Requires HW change

## Slide 7: Example PHY Security Techniques (2)
Cyclic shifting of training signal:
Apply varying cyclic shifts to the training signal
Less variability in training sequence
Preserves PAPR
Can likely be implemented in SW or possibly with smaller HW change

## Slide 8: Cyclic Shift PHY Security in NDP Frames (1)
Variable cyclic shift on ranging training
Attacker does not know the shift => Attacker can in general not perform a spoofing attack
To counter attackers repeatedly guess in the shift to apply => Require a sequence of ranging measurements for arbitrarily high security
No change in basic channel estimation is needed
  No data is demodulated
Compensate for shift in SW in ranging calculations

## Slide 9: Cyclic Shift PHY Security in NDP Frames (2)
Can include the cyclic shift applied in a packet extension payload
  The cyclic shift would also be applied to the PE itself
The cyclic shift info does not need to be encrypted
  Once the attacker learns the cyclic shift, it is to late to use
Alternatively the cyclic shift used can be conveyed encrypted prior to the LTF where it is applied.

## Slide 10: Cyclic Shift PHY Security Applied to 802.11Revmc FTM evolution
Variable cyclic shift applied to LTF and subsequent fields
  Enables decoding of payload in frame
  No change required to channel estimation and data processing in receiver
  Change to cyclic shift required in transmitter
    May only require SW or smaller HW change
  Compensate for cyclic shift in SW for ranging purposes

## Slide 11: Proposal
Apply per packet varying cyclic shifts to NDP LTFs used for ranging to prevent spoofing attacks
Convey cyclic shift used in PE or encrypted prior to LTF