## Slide 1: Ranging PHY Security
Date: 2017-05-10
Authors:

## Slide 2: Abstract
This presentation describes some techniques for protecting frames for ranging measurements from PHY level attacks.

## Slide 3: Ranging PHY Security Attacks
Levels of attacks
Denial of service attack:
  The attacker interferes with the ranging signal such as to generate a denial-of-service attack. This is very hard to protect from.
Perturbation attack:
  The attacker is interfere with the victim’s ranging, but is the attacker is not able to control the resulting perceived range.
Spoofing attack:
  The attacker interferes with the victim’s ranging and is able to control the victim’s perceived range.
The spoofing attack is the most dangerous kind of attack as it has the greatest potential to provide an incentive for the attacker.

## Slide 4: Overlay Attack on NDP based Ranging
Initiator
Responder
NDPA
NDP
T1
T3
T4 or T4*
T2 or T2*
Computed incorrect RTT* = (T2*-T1 + T4* – T3)/2
Attacker
NDP Attack
T2/T2* and T3 feedback
Example training sequence overlay attack
NDP
NDP Attack

## Slide 5: Example PHY Security Techniques (1)
Phase encoding of LTF base sequence:
Apply varying phase rotations to the LFT base sequence
High variability in training sequence
May affect PAPR
Using sequences with good PAPR can be an option
Requires HW change

## Slide 6: Example PHY Security Techniques (2)
Cyclic shifting of training signal:
Apply varying cyclic shifts to the training signal
Less variability in training sequence
Preserves PAPR
Can likely be implemented in SW or possibly with smaller HW change

## Slide 7: Cyclic Shift PHY Security in NDP Frames
Variable cyclic shift on ranging training
Attacker does not know the shift => Attacker can in general not perform a spoofing attack
No change in basic channel estimation is needed
  No data is demodulated
Compensate for shift in SW in ranging calculations

## Slide 8: Cyclic Shift PHY Security Applied to 802.11Revmc FTM evolution
Variable cyclic shift applied to LTF and subsequent fields
  Enables decoding of payload in frame
  No change required to channel estimation and data processing in receiver
  Change to cyclic shift required in transmitter
    May only require SW or smaller HW change
  Compensate for cyclic shift in SW for ranging purposes

## Slide 9: Compensation for Used Cyclic Shift
The cyclic shift used need not be conveyed but can be included in the time stamps.
The transmitting STA knows the CSD applied and can thus compensate for it the time stamps it either communicates, or just uses.
For example, if the initiator applies a CSD of t_a to ‘the first measurement frame’, the initiator can instead of sending the true t_1, send a compensated t_1
  t_1’ = t_1 + t_a (or is it ‘- t_a’…)
Similarly, if the responder applies a CSD of t_b to the ‘second measurement frame’, then responded can instead of using t_3 in its calculations, use a compensated t_3:
  t_3’ = t_3 + t_b (or is it ‘-t_b’…)
Other time stamps communicated or used can be compensated correspondingly.

## Slide 10: Enhanced Security
The most vulnerable use case is that of range estimation, e.g. confirmation of one STA being close to another STA
  E.g. car key close to car
Require multiple range estimates for such sensitive use cases.
Attacker has to guess a whole sequence of applied CSDs
Can make it arbitrarily difficult for the attacker to guess the CSDs

## Slide 11: Proposal
To prevent spoofing attacks, apply per packet varying CSDs to
  LTFs used for ranging in NDP based ranging measurement frames
  L-LTF fields and beyond in evolution of 802.11REVmc FTM frames
Used CSDs can be ‘conveyed’ by compensating communicated or used time stamps
Especially sensitive use cases can have the security enhanced by requiring multiple ranging measurements, each with a different varying CSD applied.