## Slide 1: OBSS_PD simplification
Date: 2017-05-09
Authors:

## Slide 2: Problem statement
In March, we agreed to resolve CID 3222 with doc 452r2

## Slide 3: LB225, CID 3222 27.9.2.1, P190L30

## Slide 4: Current resolution
TGax Editor: Change the following after 27.9.2.1
If the PHY of a STA issues a PHY-CCA.indication with a value equal to BUSY followed by an RXSTART.indication due to a PPDU reception then the STA’s MAC sublayer may a) issue a PHYCCARESET. request primitive and b) not update its NAV timers based on frames carried in the PPDU if all the following conditions are met:
— The received PPDU is an Inter-BSS PPDU (see 27.2.1 (Intra-BSS and inter-BSS frame detection))
— The received PPDU is not a non-HT PPDU carrying a response frame and the RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the NON SRG OBSS_PD level (defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power)). Or, the received PPDU is a non-HT PPDU carrying a response frame and the RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the OBSS_PD_min_default level (defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power))
— The PPDU is not one of the following:
A non-HT PPDU that carries an individually addressed Public Action frame where the RA field is equal to the STA MAC address
A non-HT PPDU that carries a group addressed Public Action frame
A non-HT PPDU that carries an NDPA

## Slide 5: Problem statement
We agreed previously that CTS was disallowing OBSSPD, but if we received both RTS and CTS, OBSSPD was possible.
The rational is that the receiver was protected by the proportional rule.
With last meeting’s addition, it is no longer possible to discard the NAV from any control frames, including BA..
This is going against the original intention.
And it is complexifying the mechanism, while it is supposed to be very as simple as possible.

## Slide 6: Proposal
We propose to revisit CID 3222 with the proposed resolution:
  Rejected – NON SRG OBSS_PD mechanism already protects the receiver (-82dBm) in the scenario presented, so there are no reasons to disallow OBSS_PD in such case. Modify 802.11ax D1.2 with the proposed changes in slide 7 of doc 17/0477r0
In addition to it, we propose to simplify protection by relying on CTS-to-self instead of defining exceptions for every types of frames.

## Slide 7: New proposed resolution
TGax Editor: Change the following after 27.9.2.1
If the PHY of a STA issues a PHY-CCA.indication with a value equal to BUSY followed by an RXSTART.indication due to a PPDU reception then the STA’s MAC sublayer may a) issue a PHYCCARESET. request primitive and b) not update its NAV timers based on frames carried in the PPDU if all the following conditions are met:
— The received PPDU is an Inter-BSS PPDU (see 27.2.1 (Intra-BSS and inter-BSS frame detection)) or the received PPDU contains a CTS and a PHY-CCA.indication transition from BUSY to IDLE occurred within the PIFS time immediately preceding the received CTS and that transition corresponded to the end of a PPDU that contained an RTS that was ignored following this procedure
— The received PPDU is not a non-HT PPDU carrying a response frame and the RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the NON SRG OBSS_PD level (defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power)). Or, the received PPDU is a non-HT PPDU carrying a response frame and the RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the OBSS_PD_min_default level (defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power))
— The PPDU is not one of the following:
A non-HT PPDU that carries an individually addressed Public Action frame where the RA field is equal to the STA MAC address
A non-HT PPDU that carries a group addressed Public Action frame
A non-HT PPDU that carries an NDPA

## Slide 8: New proposed resolution (continued)
If the PHY of a STA issues a PHY-CCA.indication with a value equal to BUSY followed by an RXSTART.indication due to a PPDU reception then the STA’s MAC sublayer may a) issue a PHYCCARESET. request primitive and b) not update its NAV timers based on frames carried in the PPDU if all the following conditions are met:
— The received PPDU is an Inter-BSS PPDU (see 27.2.1 (Intra-BSS and inter-BSS frame detection)) or the received PPDU contains a CTS and a PHY-CCA.indication transition from BUSY to IDLE occurred within the PIFS time immediately preceding the received CTS and that transition corresponded to the end of a PPDU that contained an RTS that was ignored following this procedure
- The received PPDU is an SRG PPDU (see 27.2.1a SRG and non-SRG frame determination)
— The most recently received Spatial Reuse Parameter Set element from the AP associated with the STA had the SRG Information Present subfield equal to 1 or the STA is an AP and its most recently transmitted Spatial Reuse Parameter Set element had the SRG Information Present subfield equal to 1
— The RXVECTOR parameter RSSI_LEGACY in the PHY-RXSTART.indication primitive, which defines the received power level measured from the legacy portion of the PPDU is below the SRG OBSS_PD level defined in 27.9.2.2 (Adjustment of OBSS_PD and transmit power)
— The PPDU is not one of the following:
• A non-HT PPDU that carries an individually addressed Public Action frame where the RA field is equal to the STA MAC address
• A non-HT PPDU that carries a group addressed Public Action frame
A non-HT PPDU that carries an NDPA

## Slide 9
TGax Editor: Suppress the sub-section Transmission of an OBSS_PD-based SR PPDU
27.9.2.2b Transmission of an OBSS_PD-based SR PPDU
Provided that other conditions are fulfilled to allow the transmission of an OBSS_PD-based SR PPDU, a STA may transmit the PPDU only if one of the following conditions is met:
the medium was idle for PIFS preceding the received OBSS PPDU that was discarded based on OBSS_PDlevel
a PHY-CCA.indication transition from BUSY to IDLE occurred within the PIFS time immediately preceding the received OBSS PPDU and the transition corresponded to the end of a PPDU that did not contain a CTS
a PHY-CCA.indication transition from BUSY to IDLE occurred within the PIFS time immediately preceding the received OBSS PPDU and the transition corresponded to the end of a PPDU that contained a CTS and a PHY-CCA.indication transition from BUSY to IDLE occurred within the PIFS time immediately preceding the received CTS and that transition corresponded to the end of a PPDU that contained an RTS