## Slide 1: Trigger Frame for Random Access
Date: 2017-05-09
Authors:
May 2017

## Slide 2: Comments
May 2017
CID | P.L | Clause | Comment | Proposed Change
9333 | 41.34 | 9.3.1.23 | Most of the User Info subfields in the Trigger frame can be the same for RUs for UL OFDMA-based random access. This means the Trigger frame can be shorter and more efficient. | Limit the RU size that can be used for UL OFDMA-based random access in each Trigger frame and reduce the redundancy.
9969 | 45.36 | 9.3.1.23 | Random access RUs have to be allocated one by one by setting AID12 field to 0. If plenty of random access RUs need to be allocated, then lots of user info fields are needed, which is a large overhead. | Devise a mechanism to allocate multiple random access RUs in an efficient way.

## Slide 3: Problem Statement
When the number of RUs assigned for random access is large, we need a lot of per user info fields in the Trigger frame, one for each RU assigned for random access, which has larger overhead
  E.g., for 20MHz, if we want to allocate 9 random access RUs, we need 9 user info fields (most of which are duplicated)
Length
AID=0
RU Allocation
MCS
……
AID=0
RU Allocation
MCS
……
AID=0
RU Allocation
MCS
……
BW
# of LTF
……
Random access
Random access
Random access
Random access
Random access
20 MHz
Common info field
User info field
AID=0
RU Allocation
MCS
……
Random access
Random access
Random access
Random access
……
……

## Slide 4: Scheme
In the user info field with “AID = 0 or 2045”
  Replace “SS Allocation” field with “random access RU number”: the number of RUs allocated for random access. These RUs are allocated consecutively.
  Interpret “RU Allocation” in another way:
    The RU position indicated by the RU Allocation field is the random access RU starting position
    The size of the RU indicated by the RU Allocation field is the random access RU size
RU for random access
RU for random access
RU for random access
……
K RUs
The first random access RU
Random access RU
Starting position
Random access RU size
  The spatial stream number of each random access RU is 1

## Slide 5: Overhead reduction
Length
AID=0
RU Allocation
MCS
……
AID=0
RU Allocation
MCS
……
AID=0
RU Allocation
MCS
……
BW
# of LTF
……
Random access
Random access
Random access
Random access
Random access
20 MHz
Common info field
User info field
AID=0
RU Allocation
MCS
……
Random access
Random access
Random access
Random access
……
Length
BW
# of LTF
……
Common info field
AID=0
RU Allocation
MCS
……
User info field
MPDU size:
82 bytes
MPDU size:
34 bytes
59% overhead reduced! (20MHz)
Overhead reduction can be up to 86% for 80MHz

## Slide 6: Conclusion
  We propose a simplified resource allocation scheme for OFDMA-based random access to resolve CID 9333 and 9969
  MPDU overhead reduction up to 59% for 20MHz, can be higher for larger bandwidth (86% for 80MHz)
    Assume 20MHz, 9 RUs are allocated for random access, common info field has 8 bytes, per user info field has 6 bytes
    PPDU overhead reduction up to 49% (assuming 6Mbps PHY rate, non-HT PPDU) (81.5% for 80MHz)