## Slide 1: HE Frame Sequences
Date: 2017-05-09
Authors:

## Slide 2: Abstract
This presentation provides an overview of HE frame exchange sequences in a slightly more coherent manner than is provided by the spec
It assumes that some of the comment resolution proposed during this session is adopted
The presentation is mostly a tutorial but introduces some terminology we may want to adopt in the spec
NOTE that this is not the spec but simply my interpretation of the spec

## Slide 3: Overview of HE frame exchange sequences
This presentation covers:
  Protection sequences
  Data transfer sequences
    Basic SU and MU sequences
    Multi-TID sequences
    Cascade sequences
This presentation does not cover:
  BSRP and BQRP sequences
  GCR sequences
  UORA sequences for associated STAs
  UORA sequences for unassociated STAs
  Sounding sequences

## Slide 4: Terminology (1)
Single user (SU) PPDU
  A non-HT PPDU, non-HT duplicate PPDU, HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU that carries the content of a single PSDU. An SU PPDU carries groupcast or unicast frames. SU PPDUs are transmitted by both AP and non-AP STAs in the role of either TXOP holder or TXOP responder.
DL multi-user (MU) PPDU
  A VHT PPDU or HE MU PPDU that carries the content of two or more PSDUs. Each PSDU carries unicast frames, although in the case of an HE MU PPDU it is possible for one of the PSDUs to carry groupcast traffic intended for STAs not receiving unicast traffic in the same PPDU. DL MU PPDUs are transmitted by an AP in the role of TXOP holder.

## Slide 5: Terminology (2)
HE TB PPDU
  Transmitted by a non-AP STA (in the role of TXOP responder) in response to a Trigger frame or frame that includes a UMRS Control field sent by the AP. More than one HE TB PPDU may be transmitted simultaneously by more than one non-AP STA.
Synchronized non-HT [duplicate] PPDU
  Carries a CTS frame and is transmitted by a non-AP STA in response to an MU-RTS Trigger frame. The non-HT PPDU or non-HT duplicate PPDU is “synchronized” if the TXVECTOR parameter TRIGGER_RESPONDING is true. May be transmitted by more than on non-AP and the content of the CTS is identical in each (same frame content and same scrambler seed)

## Slide 6: Terminology (3)
Block ack sequence
Either one or more QoS Data frames that belong to a single block ack agreement, or a BlockAckReq frame for a block ack agreement included in an A-MPDU. A BlockAckReq frame is not sent together with QoS Data frames or QoS Null frames of the same block ack agreement.
We need this definition when describing “multi-TID” since we need to describe an A-MPDU that includes multiple of these things

## Slide 7: Terminology (4)
In this document, we use a modified S-MPDU definition:
S-MPDU
  An MPDU that is the only MPDU in an A-MPDU and that is carried in an A-MPDU subframe with the EOF subfield of the MPDU delimiter field equal to 1.

## Slide 8: Options: UMRS support
An HE non-AP STA that has 1 in the UMRS Control Support subfield in the HE MAC Capabilities Information field of the HE Capabilities element it transmits is able to respond to a frame that includes the UMRS Control field and is said to support UMRS.

## Slide 9: Options: Cascading support
An HE non-AP STA that has 1 in the MU Cascading Support subfield in the HE MAC Capabilities Information field of the HE Capabilities element it transmits is able to receive an A-MPDU that includes an Ack frame or BlockAck frame as well as a Trigger frame. Such a STA is said to support cascading.
“MU” in the subfield name is misleading. It is possible to have a cascade exchange between the AP and a single STA.
The actual spec description is “indicates whether the STA supports participating in an MU Cascading sequence.”
However, the only extra thing that the STA does by participating in a cascade sequence is receive an A-MPDU that includes an Ack frame or BlockAck frame plus Trigger frame
An HE AP does not need to signal cascading support since it controls cascading using the TID Aggregation Limit field in the Trigger frame.

## Slide 10: Options: Multiple ack context support (Multi-TID support)
An HE STA that can receive an A-MPDU where the frames present solicit either an acknowledgement or a block acknowledgement is said to support a single ack context. All HE STAs support a single ack context. An HE STA that can receive an A-MPDU where the frames present solicit more than one acknowledgement and/or block acknowledgement is said to support multiple ack contexts. An HE STA sets the Multi-TID Aggregation Support subfield of the HE MAC Capabilities Information field of the HE Capabilities element it transmits to indicate the number of acknowledgement contexts it supports.
The actual spec description is “indicates the number of TIDs minus 1 of QoS Data frames that an HE STA can aggregate in a multi-TID A-MPDU.”
The is misleading for two reasons:
Action frames can be included
It is what the STA is capable or receiving and not what it is capable of transmitting that is relevant

## Slide 11: MU protection sequence
An HE AP may transmit an MU-RTS Trigger frame in a non-HT PPDU, non-HT duplicate PPDU, HT PPDU, VHT PPDU that carries a single PSDU, HE SU PPDU, or HE ER SU PPDU.
An HE non-AP STA that receives an MU-RTS Trigger frame with a User Info field addressed to it, responds (if the medium is idle) with a CTS frame carried in a non-HT PPDU or non-HT duplicate PPDU with TXVECTOR parameter TRIGGER_RESPONDING set to true and data rate 6 Mbps. The TXVECTOR parameter CH_BANDWIDTH is set based on the RU Allocation field in the Trigger frame so that the PPDU occupies one of the following:
  The primary 20 MHz channel
  The primary 40 MHz channel
  The primary 80 MHz channel
  The 160 MHz or 80+80 MHz channel

## Slide 12: Initial PPDU (soliciting UL data, control or management)
An HE AP may send to an HE non-AP STA one of the following:
  A Basic Trigger frame with the TID Aggregation Limit subfield in the User Info field addressed to the HE non-AP STA set to 1 carried in a non-HT PPDU, non-HT duplicate PPDU, or HT PPDU with TXVECTOR parameter AGGREGATION set to 0.
  An A-MPDU that contains one or more Basic Trigger frames with the TID Aggregation Limit subfield in the User Info field addressed to the HE non-AP STA set to 1. The A-MPDU is carried in a VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU.
There are various ways to send the Trigger frame:
Broadcast frame with multiple User Info field in an SU PPDU
Unicast frame with single User Info field in an SU PPDU
Unicast frames with single User Info field in one or more A-MPDUs in an MU PPDU
Broadcast frame in broadcast RU in an HE MU PPDU

## Slide 13: Initial PPDU (DL data with triggered control response)
An HE AP may send to an HE non-AP STA one of the following (continued):
  An A-MPDU that contains one or more Basic Trigger frames with the TID Aggregation Limit subfield in the User Info field addressed to the HE non-AP STA set to 0 and QoS Data frames belonging to a single block ack agreement and with ack policy HTP Ack or Block Ack. The A-MPDU is carried in a VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU.

## Slide 14: Initial PPDU (BAR with triggered control response)
An HE AP may send to an HE non-AP STA one of the following (continued):
  An MU-BAR Trigger frame with a User Info field addressed to the HE non-AP STA carried in a non-HT PPDU, non-HT duplicate PPDU, HT PPDU with TXVECTOR parameter AGGREGATION set to 0.
  An A-MPDU that contains one or more MU-BAR Trigger frames with a User Info field addressed to the HE non-AP STA. The A-MPDU is carried in a VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU.
We don’t send a Trigger frame + BlockAckReq frame to shift the block ack window and solicit BlockAck frame.
And we also don’t send a BlockAckReq frame with UMRS Control field.
Instead, we have a special Trigger frame: the MU-BAR Trigger frame

## Slide 15: Initial PPDU (DL management or data with triggered ack)
An HE AP may send to an HE non-AP STA that supports Ack Enabled Multi-TID Aggregation the following:
  An A-MPDU that contains one or more Basic Trigger frames with the TID Aggregation Limit subfield in the User Info field addressed to the HE non-AP STA set to 0 and an S-MPDU that is an Action frame, QoS Data frame with ack policy HTP Ack, or QoS Null frame with ack policy HTP Ack. The A-MPDU is carried in an HE MU PPDU.
We need special handling when aggregating a Trigger frame and Action frame since we don’t want the responder sending an Ack frame in an SU PPDU if it does not receive the Trigger frame. So, we only allow Trigger frame + S-MPDU in the HE MU PPDU.

## Slide 16: Initial PPDU (UL, DL and peer-to-peer)
An HE STA may send to another HE STA one of the following:
  An Action frame, QoS Data frame with ack policy Normal Ack, or QoS Null frame with ack policy Normal Ack carried in a non-HT PPDU, non-HT duplicate PPDU or HT PPDU with TXVECTOR parameter AGGREGATION set to 0.
  An S-MPDU that is an Action frame, QoS Data frame with ack policy Normal Ack, or QoS Null frame with ack policy Normal Ack carried in a VHT PPDU, HE SU PPDU, or HE ER SU PPDU.
  An A-MPDU that contains QoS Data frames with ack policy Implicit Block Ack Request or Block Ack and belonging to a single block ack agreement. The A-MPDU is carried in an HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU.
  A BlockAckReq frame carried in a non-HT PPDU, non-HT duplicate PPDU, HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU, HE MU PPDU.

## Slide 17: Initial PPDU (DL data with triggered control response using UMRS)
An HE AP may send to an HE non-AP STA that supports UMRS one of the following:
  An S-MPDU that is an Action frame that has a UMRS Control field present or a QoS Data frame with UMRS Control field present and that has ack policy HTP Ack. The S-MPDU is carried in a VHT PPDU, HE SU PPDU, HE ER SU PPDU, HE MU PPDU.
  An Action frame that has a UMRS Control field present, or a QoS Data frame or QoS Null frame that has a UMRS Control field present and that has ack policy HTP Ack. The frame is carried in a non-HT PPDU, non-HT duplicate PPDU, or HT PPDU with TXVECTOR parameter AGGERGATION set to 0.
  An A-MPDU that contains QoS Data frames with a UMRS Control field present and with ack policy HTP Ack. The A-MPDU is carried in an HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU, HE MU PPDU.

## Slide 18: Initial PPDU (DL multi-TID)
An HE AP may send to an HE non-AP STA that supports multiple ack contexts one of the following:
  An A-MPDU that contains one or more Basic Trigger frames with the TID Aggregation Limit subfield in the User Info field addressed to the STA set to 0 and QoS Data frames that belong to more than one block ack agreement and with ack policy HTP Ack. The A-MPDU is carried in an HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU.
  An MU-BAR Trigger frame with two or more User Info fields addressed to the TXOP responder carried in a non-HT PPDU, non-HT duplicate PPDU, HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU.

## Slide 19: Initial PPDU (UL, DL, and peer-to-peer multi-TID)
An HE STA may send to another HE STA that supports multiple ack contexts one of the following:
  An A-MPDU that contains one or more QoS Data frames that belong to more than one block ack agreement and with ack policy Implicit Block Ack Request or Block Ack. The A-MPDU is carried in an HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU or HE MU PPDU.
  A Multi-TID BlockAckReq frame with more than one BAR Information field carried in a non-HT PPDU, non-HT duplicate PPDU, HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU.

## Slide 20: Initial PPDU (DL multi-TID with UMRS)
An HE AP may send to an HE non-AP STA that supports both UMRS and multiple ack contexts, an A-MPDU that includes QoS Data frames and/or QoS Null frames belonging to more than one block ack agreement and that include a UMRS Control field and have ack policy HTP Ack.

## Slide 21: Initial PPDU (cascading)
An HE AP may send to an HE non-AP STA that supports cascading one of the following:
  An A-MPDU that contains one or more Basic Trigger frames with the TID Aggregation Limit subfield in the User Info field addressed to the STA set to a value greater than 0 and an S-MPDU that is an Action frame, QoS Data frame with ack policy HTP Ack, or QoS Null frame with ack policy HTP Ack. The A-MPDU is carried in an HE MU PPDU.
  An A-MPDU that contains one or more Basic Trigger frames with the TID Aggregation Limit subfield in the User Info field addressed to the STA set to a value greater than 0 and one or more QoS Data frames and/or QoS Null frames that belong to the same block ack agreement and with ack policy HTP Ack. The A-MPDU is carried in a VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU.

## Slide 22: Initial PPDU (DL multi-TID with cascading)
An HE AP may send to an HE non-AP STA that supports both cascading and multiple ack contexts an A-MPDU that contains one or more Basic Trigger frames with the TID Aggregation Limit subfield in the User Info field addressed to the STA set to a value greater than 0 and QoS Data frames and/or QoS Null frames that belong to more than one block ack agreement and with ack policy HTP Ack. The A-MPDU is carried in an HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU, or HE MU PPDU.

## Slide 23: HE TB PPDU response
Basic principles:
  A HE non-AP STA responds with a HE TB PPDU if it receives either a Trigger frame or UMRS Control field
  Since not all frames in an A-MPDU are necessarily received the rules must not allow SU PPDU response when a HE TB PPDU response is expected
  Ack policy HTP Ack means: “you should have received a Trigger frame or UMRS Control field so only send ack if you did”
  We need special rules for Action frames since these don’t have an ack policy (soliciting the ack is implicit in the Action subtype)
  Also, a STA that receives a Trigger frame only responds if it has something to send

## Slide 24: HE TB PPDU response (when not to respond)
An HE non-AP STA that receives, in an HE MU PPDU, an S-MPDU that is an Action frame shall not respond unless one of the following conditions are met:
  The frame includes a UMRS Control field
  A Basic Trigger frame is received in the A-MPDU that contains the Action frame
An HE non-AP STA that receives a QoS Data frame with ack policy HTP Ack, or QoS Null frame with ack policy HTP Ack shall not respond unless one of the following conditions are met:
  The frame includes a UMRS Control field
  A Basic Trigger frame is received in the A-MPDU that contains the Action frame
The rules around when not to respond are not very clear in the spec

## Slide 25: HE TB PPDU response (UMRS)
A STA that receives an S-MPDU that is an Action frame, QoS Data frame with ack policy HTP Ack, or QoS Null frame with ack policy HTP Ack and that includes a UMRS Control field, responds with an Ack frame carried in an HE TB PPDU.
A STA that receives an A-MPDU that includes QoS Data frames with ack policy HTP Ack and that include a UMRS Control field responds with a Compressed BlockAck frame or Multi-STA BlockAck frame carried in an HE TB PPDU. The response is a Compressed BlockAck frame if the QoS Data frames belong to a single block ack agreement and a Multi-STA BlockAck frame if the QoS Data frames belong to more than one block ack agreement.

## Slide 26: HE TB PPDU response (triggered control frames)
An HE non-AP STA that receives, in an HE MU PPDU, an A-MPDU that includes a Basic Trigger frame and an S-MPDU that is an Action frame, QoS Data frame with ack policy Normal Ack or QoS Null frame with ack policy Normal Ack, responds with an Ack frame carried in an HE TB PPDU.
An HE non-AP STA that receives an A-MPDU that includes a Basic Trigger frame and QoS Data frames with ack policy HTP Ack responds with a Compressed BlockAck frame or Multi-STA BlockAck frame carried in an HE TB PPDU. The response is a Compressed BlockAck frame if the QoS Data frames belong to a single block ack agreement and a Multi-STA BlockAck frame if the QoS Data frames belong to more than one block ack agreement.

## Slide 27: HE TB PPDU response (triggered PS-Poll frame)
An HE non-AP STA that receives a Basic Trigger frame where the TID Aggregation Limit field of the User Info field addressed to it is greater than 0, may respond with a PS-Poll frame carried in an HE TB PPDU.

## Slide 28: HE TB PPDU response (triggered data or management frames)
An HE non-AP STA that receives a Basic Trigger frame where the TID Aggregation Limit field of the User Info field addressed to it is greater than 0, may respond with an HE TB PPDU that carries an A-MPDU with one or more block ack sequences and/or one S-MPDU that is an Action frame, QoS Data frame with ack policy Normal Ack, or QoS Null frame with ack policy Normal Ack. The number of block ack sequences shall be less than the value of the TID Aggregation Limit field if an S-MPDU is not also present and less than the TID Aggregation Limit minus one if an S-MPDU is also present.
If the A-MPDU that carries the Basic Trigger frame includes a frame that solicits a control response the control response frame is the first frame in the A-MPDU of the HE TB PPDU.

## Slide 29: SU PPDU response (control responses only)
A STA that receives an A-MPDU that includes QoS Data frames and/or QoS Null frames with ack policy Implicit Block Ack Request belonging to the same block ack agreement, responds with a Compressed BlockAck frame carried in an SU PPDU.
A STA that receives an A-MPDU that includes QoS Data frames and/or QoS Null frames with ack policy Implicit Block Ack Request belonging to more than one block ack agreement, responds with a Multi-STA BlockAck frame that has a Per AID TID field for each block ack agreement carried in an SU PPDU.

## Slide 30: HE AP response to an HE TB PPDU (single TID)
An HE AP that receives an A-MPDU in an HE TB PPDU that contains an S-MPDU that is a management frame soliciting acknowledgement, QoS Data frame with ack policy Normal Ack, QoS Null frame with ack policy Normal Ack, or PS-Poll frame responds with one of the following:
  An Ack frame
  A Multi-STA BlockAck frame with a Per AID TID Info field addressed to the TXOP responder that has ack context
An HE AP that receives an A-MPDU in an HE TB PPDU that contains QoS Data frames with ack policy Implicit Block Ack and belonging to the same block ack agreement responds with one of the following:
  A Compressed BlockAck frame
  A Multi-STA BlockAck frame with a Per AID TID Info field addressed to the TXOP responder that has block ack context or, if supported, all ack context

## Slide 31: HE AP response to an HE TB PPDU (multi-TID)
An HE AP that receives an A-MPDU in an HE TB PPDU that contains a block ack sequence and an S-MPDU or contains more than one block ack sequence responds with a Multi-STA BlockAck frame with a Per AID TID Info field with block ack context for each block ack sequence and with Per AID TID Info field with ack context for the S-MPDU if present.
We also need a rule for a Multi-STA BlockAck frame with a single Per AID TID Info field with all ack context, but I don’t know how to write that

## Slide 32: HE AP response to an HE TB PPDU (cascading)
An HE AP that is responding to a frame that solicits a control response sent in an HE TB PPDU by an HE non-AP STA that supports cascading, may send an A-MPDU that includes the Ack frame or BlockAck frame control response and one of the following:
  One or more Basic Trigger frames together with QoS Data frames that solicit an immediate response
  QoS Data frames that include a UMRS Control field and that solicit an immediate response

## Slide 33: Including frames that don’t solicit a response
A TXOP holder may include in an A-MPDU that it sends in an HT PPDU, VHT PPDU, HE SU PPDU, HE ER SU PPDU, HE MU PPDU the following:
QoS Data frames with ack policy No Ack
QoS Null frames with ack policy No Ack
Action No Ack frames
A TXOP responder may include in an A-MPDU that it sends in an HE TB PPDU the following:
QoS Data frames with ack policy No Ack
QoS Null frames with ack policy No Ack
Action No Ack frames

## Slide 34: Summary
We have summarized HE frame sequences in a more coherent way than laid out in the spec
We have identified a few issues with names and definitions
  Cascading support is really just what an HE non-AP STA can receive in an A-MPDU (ack/block ack and data in the same A-MPDU).
  Multi-TID is better defined in terms of the number of ack states a STA can track while receiving an A-MPDU
  When not to respond is not clearly defined in the spec