## Slide 1: Short SSW Format For Unassociated STAs
Date: 2017-06-28
Authors:

## Slide 2: Abstract
A Short SSW format to support usage by unassociated STAs during the CBAP is proposed

## Slide 3: Background
11ay aims to support STAs with larger arrays
Use of Short SSW packet instead of SSW frame allows 37% savings
D0.35 [1] only supports use of Short SSW by associated STAs
Short SSW packet format should be modified to support transmission by unassociated STAs to facilitate efficient discovery

## Slide 4: Current format
The format of Short SSW (I-TXSS) for SU addressing mode is:
Source and destination addressing is based on AID
  Unassociated STAs do not have AIDs
  Unassociated STA may not know BSS AID of the AP/PCP

## Slide 5: Proposed solution for CBAP (unassociated)
Short SSW (I-TXSS) [STA]
  Unassociated field to identify transmission from unassociated STA
  Source AID and Destination AID fields contain 8-bit random values (0-255) to identify the STA
Short SSW (R-TXSS) [AP/PCP]
  Source AID and Destination AID fields contain Source AID and Destination AID field values in received Short SSW
SSW-Feedback [STA]
  RA contains BSSID
  TA contains STA MAC address
  CDOWN Select 1/2 [2] contains CDOWN of best received Short SSW
SSW-ACK [AP/PCP]
  RA contains STA MAC address
  TA contains BSSID
  CDOWN Select 1/2 fields are ignored

## Slide 6: Proposed Short SSW packet format
Direction=0(I-TXSS), Addressing Mode=0(SU)
 | Packet Type | Direction | Addressing Mode | Source AID | Destination AID | CDOWN | RF Chain ID | Short Scrambled BSSID | Unassociated | FCS
Bits: | 2 | 1 | 1 | 8 | 8 | 11 | 2 | 10 | 1 | 4

## Slide 7: Proposed solution for CBAP (comparison)
Associated
AP/PCP
STA
DTI
Short SSW (DA, SA=Random)
Short SSW (DA=Rcvd DA, SA=Rcvd SA)
…
…
SSW-FB (RA=BSSID, TA=STA MAC Addr)
SSW-ACK (RA=STA MAC Addr, TA=BSSID)
AP/PCP
STA
DTI
Short SSW (DA=BSS AID, SA=STA AID)
Short SSW (DA=STA AID, SA=BSS AID)
…
…
SSW-FB (RA=BSSID, TA=STA MAC Addr)
SSW-ACK (RA=STA MAC Addr, TA=BSSID)
Unassociated

## Slide 8: Signaling of support
1 bit in the DMG Beacon’s SSW field is used to indicate support of Short SSW reception from unassociated STAs during the CBAP
  The RX Unassociated Short SSW field is set to 1 to indicate that the STA supports reception of Short SSW packets from unassociated STAs during the CBAP. Otherwise it is set to 0.
Figure 46 —SSW field format when transmitted in a DMG Beacon frame
Direction
CDOWN
Sector ID
DMG Antenna ID
Quasi-omni TX
Reserved
RX Unassociated Short SSW
Bits:
1
9
6
2
1
1
1
B0
B1 B9
B10 B15
B16 B17
B18
B22
B23
PCP/AP Coverage Parameter
3
B19 B21

## Slide 9: Conclusion
Use of Short SSW should be extended to support use by unassociated STAs to reduce beamforming overhead during discovery
Short SSW format and procedure for unassociated STAs for CBAP has been proposed
DMG Beacon signals if unassociated Short SSW reception is supported

## Slide 10: References
[1] Draft P802.11ay_D0.35
[2] 11-17-0109-01-00ay-11ay-short-ssw-feedback-ack

## Slide 11: Straw poll
Do you agree to include the changes described in 11-17-0938-00-00ay to enable Short SSW usage in CBAP by unassociated STAs?