## Slide 1: Data Rate for Range Requirement in 11ba
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
We already agreed to use multiple data rates for the payload part of wake-up packet
  In [1], we discussed the necessity of multiple data rates
In this contribution, we investigate possible data rates for the payload part of wake-up packet from a range requirement viewpoint of 11ba
To this end, we first define a target SNR for 11ba by considering the performance of the main radio, the noise figure and the power regulation in 2.4GHz and 5GHz bands
  In this contribution, we consider two candidates for the main radio performance, L-SIG performance [2] and data part performance [3]
Then, we examine the performance for various data rates in 11ba even considering the BCC
Finally, we confirm data rates required for 11ba by comparing the performance with the target SNR

## Slide 3: Target SNR for Range Requirement
The target SNR for the range requirement in 11ba is equal to 12dB/15dB lower SNR than the minimum SNR required for a reliable operation of the main radio in 2.4GHz/5GHz, respectively [4]
  To achieve the range requirement, 11ba should guarantee at least 10% PER at the target SNR
The minimum SNR required for the main radio and the target SNR for 11ba can be obtained as follows by considering the L-SIG performance (at 1%) and the data part performance (at 10%) of the main radio shown in Appendix
Note that the required SNR for the data part is higher than that of the L-SIG, and thus the transmission range which guarantees a reliable operation of the data part is shorter than that of the L-SIG
  That means some STAs can decode the L-SIG reliably but cannot decode the data part in the main radio
  Hence, these STAs don’t have to be awakened to receive data
  Thus, it seems that the transmission range of wake-up packet just satisfies that of the data part of the main radio
Candidate for the main radio performance |  | Minimum SNR required for the main radio [dB] |  | Target SNR for 11ba [dB] | 
 |  | 2.4GHz | 5GHz | 2.4GHz | 5GHz
L-SIG performance | TGnD channel | 6.7 | 6.7 | -5.3 | -8.3
 | UMi NLoS channel | 9.6 | 9.6 | -2.4 | -5.4
Data part performance | TGnD channel | 8.3 | 8.3 | -3.7 | -6.7
 | UMi NLoS channel | 10 | 10 | -2 | -5

## Slide 4: Simulation Assumptions
4MHz signal bandwidth (13 subcarriers)
48 symbols in payload
  Four data rates : 15.625Kbps/31.25Kbps/62.5Kbps/125Kbps with or without BCC
CFO [3], Phase noise [4] applied
No timing error
Butterworth filter
  2.5MHz cut off frequency, second order
20MHz sampling rate
TGnD and UMi NLoS channels in 2.4GHz and 5GHz
SNR defined in 20MHz

## Slide 5: OOK Symbol
125Kbps
  Option 1 (Without BCC) : 8us OOK symbol with Manchester coding (4us ON + 4us OFF or vice versa)
  Option 2 (With BCC) : 4us normal OOK symbol + BCC w/ ½ code rate
62.5Kbps
  Option 1 (Without BCC) : 16us OOK symbol with Manchester coding (4us ON + 4us OFF + 4us ON + 4us OFF or vice versa)
  Option 2 (With BCC) : 8us OOK symbol with Manchester coding (4us ON + 4us OFF or vice versa) + BCC w/ ½ code rate
31.25Kbps
  Option 1 (Without BCC) : 32us OOK symbol with Manchester coding (4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF or vice versa)
  Option 2 (With BCC) : 16us OOK symbol with Manchester coding (4us ON + 4us OFF + 4us ON + 4us OFF or vice versa) + BCC w/ ½ code rate
15.625Kbps
  Option 1 (Without BCC) : 64us OOK symbol with Manchester coding (4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF or vice versa)
  Option 2 (With BCC) : 16us OOK symbol with Manchester coding (4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF + 4us ON + 4us OFF or vice versa) + BCC w/ ½ code rate

## Slide 6: PER Performance for Various Data Rates
2.4GHz
TGnD Channel
UMi NLoS Channel

## Slide 7: PER Performance for Various Data Rates
5GHz
TGnD Channel
UMi NLoS Channel

## Slide 8: Required SNR at 10% PER
The required SNR at 10% PER for all options are as follows
Data Rate [Kbps] | Option | Required SNR in TGnD [dB] |  | Required SNR in UMi NLoS [dB] | 
 |  | 2.4GHz | 5GHz | 2.4GHz | 5GHz
15.625 | Option 1 (w/o BCC) | -6.6 | -6.1 | -6.8 | -6.5
 | Option 2 (w/ BCC) | -8.8 | -8.3 | -9.6 | -9.2
31.25 | Option 1 (w/o BCC) | -5 | -4.6 | -5.2 | -4.7
 | Option 2 (w/ BCC) | -7.3 | -6.8 | -8.1 | -7.6
62.5 | Option 1 (w/o BCC) | -3.2 | -2.8 | -3.3 | -3
 | Option 2 (w/ BCC) | -5.8 | -5.4 | -6.5 | -6.1
125 | Option 1 (w/o BCC) | -1.4 | -0.9 | -1.5 | -1.1
 | Option 2 (w/ BCC) | -4 | -3.5 | -4.8 | -4.4
Candidate for the main radio performance | Target SNR in TGnD [dB] |  | Target SNR in UMi NLoS [dB] | 
 | 2.4GHz | 5GHz | 2.4GHz | 5GHz
L-SIG | -5.3 | -8.3 | -2.4 | -5.4
Data part | -3.7 | -6.7 | -2 | -5

## Slide 9: Discussion (1/2)
The following data rates meet the target SNR
 | Option | TGnD |  | UMi NLoS | 
 |  | 2.4GHz | 5GHz | 2.4GHz | 5GHz
L-SIG | Option 1 (w/o BCC) | 15.625Kbps | Lower than 15.625Kbps | 15.625Kbps, 31.25Kbps, 62.5Kbps | 15.625Kbps
 | Option 2 (w/ BCC) | 15.625Kbps, 31.25Kbps, 62.5Kbps | 15.625Kbps | all data rates | 15.625Kbps, 31.25Kbps, 62.5Kbps
Data part | Option 1 (w/o BCC) | 15.625Kbps, 31.25Kbps | Lower than 15.625Kbps | 15.625Kbps, 31.25Kbps, 62.5Kbps | 15.625Kbps
 | Option 2 (w/ BCC) | all data rates | 15.625Kbps, 31.25Kbps | all data rates | 15.625Kbps, 31.25Kbps, 62.5Kbps

## Slide 10: Discussion (2/2)
For overhead minimization, the following data rates with BCC can be selected in each case
If 11ba is not allowed to use BCC due to the power consumption issue, the following data rates can be selected in each case
 | TGnD |  | UMi NLoS | 
 | 2.4GHz | 5GHz | 2.4GHz | 5GHz
L-SIG | 62.5Kbps | 15.625Kbps | 125Kbps | 62.5Kbps
Data part | 125Kbps | 31.25Kbps | 125Kbps | 62.5Kbps
 | TGnD |  | UMi NLoS | 
 | 2.4GHz | 5GHz | 2.4GHz | 5GHz
L-SIG | 15.625Kbps | Lower than 15.625Kbps | 62.5Kbps | 15.625Kbps
Data part | 31.25Kbps | Lower than 15.625Kbps | 62.5Kbps | 15.625Kbps

## Slide 11: Conclusion
In this contribution, we verified necessary data rates for the payload part of wake-up packet to guarantee the range requirement of 11ba
Those data rates are different according to the candidate for the main radio performance
  Note that the lowest data rate of the payload part of wake-up packet can be determined by the data part performance of the main radio given a reliable operation of the main radio
They also depend on whether to use BCC or not
  BCC is recommended for overhead reduction but its power consumption should be further discussed
The lowest data rate can be determined by the required data rate in the 5GHz band if 11ba operates at this band
Candidate for the main radio performance | Required data rates w/ BCC |  | Required data rates w/o BCC | 
 | 2.4GHz | 5GHz | 2.4GHz | 5GHz
L-SIG | ≤ 62.5Kbps | ≤ 15.625Kbps | ≤ 15.625Kbps | < 15.625Kbps
Data part | ≤ 125Kbps | ≤ 31.25Kbps | ≤ 31.25Kbps | < 15.625Kbps

## Slide 12: Straw Poll #1
Do you agree to use binary convolution code (BCC) rate 1/2 as in the 802.11 spec for the payload part of wake-up packet?
Y/N/A : 10/11/12

## Slide 13: Straw Poll #2
Which data rate do you agree to use as the lowest data rate for the payload part of wake-up packet?
  15.625Kbps
  31.25Kbps
  62.5Kbps
  125Kbps
15.625/31.25/62.5/125/A : 0/11/27/4/6

## Slide 14: Straw Poll #3
Do you agree to add the following to the 11ba SFD?
  The data rate of 31.25Kbps for the payload part of wake-up packet is computed by applying BCC with the code rate of ½ to 16us OOK symbol with Manchester coding (i.e., 4us ON + 4us OFF + 4us ON + 4us OFF or vice versa)
Y/N/A :

## Slide 15: Straw Poll #4
Do you agree to add the following to the 11ba SFD?
  The data rate of 62.5Kbps for the payload part of wake-up packet is computed by applying BCC with the code rate of ½ to 8us OOK symbol with Manchester coding (i.e., 4us ON + 4us OFF or vice versa)
Y/N/A :

## Slide 16: Motion
Move to add the following to the 11ba SFD
  The lowest data rate for the payload part of wake-up packet is 62.5Kbps
Move : Eunsung Park
Second :
Y/N/A :

## Slide 17: References
[1] IEEE 802.11-17/0654r3 Multiple Data Rates for WUR
[2] IEEE 802.11-17/0655r4 OOK Signal Bandwidth for WUR
[3] IEEE 802.11-17/0656r0 WUR PHY Performance Study with Phase Noise and ACI
[4] IEEE 802.11-17/0365r0 Regulations and Noise Figure - Impact on SNR

## Slide 18: Appendix

## Slide 19: PER Performance for Main Radio
TGnD Channel
UMi NLoS Channel
Data part : 100bytes with MCS0