## Slide 1: Consideration on WUR packet Design
Date: 2017-09-08
Authors:
Name | Affiliation | Address | Email
Kaiying Lv | ZTE Corp. | NO.9 Wuxing Duan Xifeng Road, Xi’an, China | lv.kaiying@zte.com.cn
Ning Wei |  |  | 
Bo Sun |  |  | 

## Slide 2: Introduction
The wake-up format based on the previous discussions[1-3] can be summaried as:
  WLAN legacy preamble for intra-frame protection and coexistence with WLAN devices
  A BPSK symbol for 11n device to restrain false alarm
  WUR sync sequence for the identification to wake-up packet (WUP)
  WUR signature sequence for data rate indication
  WUR payload for carrying necessary control and management and/or traffic information
We propose to introduce some considerations for the WUR Payload (frame format) design
  Special considerations for power saving
  Security issues

## Slide 3: Power saving in WUR frame design
Point A: WUR TX’s identifier
  The Wakeup Request should at least include WUR TX’s identifier which is of very low collision probability. Eg. BSS Color
  WUR TX’s identifier could be used for earlier detection or identification for an WUR device to have more power saving by filtering the WUR packets transmitted from OBSS without decoding the whole WUR packets
Point B: Length Indication
  Length indication could be used for indicating how long the WUR device can be in shallow sleep if an OBSS WUR packet is detected.
Point A and B need immediate process for power saving, so they’re not supposed to be checked together with other payload information after all payload is received. So we propose to define a WUR SIG filed for such information requesting immediate process
  A CRC sub-field is added at the end of WUR SIG field

## Slide 4: Security in WUR frame design
  IoT devices are sensitive to power-costing attack. The WUR frame design should consider to protect privacy information from malicious attacks.
  When a simple security protocol is used, typically an unicast secret sequence and a broadcast secret sequence are used for unicast WUR packet and broadcast/multicast WUR packet respectively.
    It’s necessary to understand whether the unicast secret sequence or the broadcast secret sequence is used before decoding the payload part.
    Similar as Length indication and transmitter’s identifier, the unicast/broadcast indication needs immediate process and is suitable to be located in WUR SIG field.

## Slide 5: Conclusion
In this contribution, we discussed WUR packet design with consideration of power saving and security
  an “WUR SIG” field might be useful for power saving when considering a WUR packet design
  The encryption for WUR packet is discussed to protect WUR from malicious attacks. Two options are proposed:
    both WUR SIG and WUR payload are encrypted with implicit indication to secure-key type
    Only WUR payload is encrypted with explicit indication to secure-key type.

## Slide 6: Reference
[1]11-17-0084-00-00ba-high-level-phy-design
[2]11-17-0675-00-00ba-wur-coexistence-and-packet-format
[3]11-17-0679-01-00ba-1-wur-packet-format-and-preamble- design
[4]11-16-1460-01-0wur-wur-mac-discussion

## Slide 7: Straw Poll 1
Do you agree that 11ba should add WUR SIG into WUP format?
  Yes
  NO
  Abstain

## Slide 8: Straw Poll 2
Do you agree that 11ba should consider security issue when design an WUP format?
  Yes
  NO
  Abstain