## Slide 1: Analysis on the Impact of Blank GI to ISI
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Jia Jia |  |  |  | 
Osama Aboul-Magd |  |  |  | 

## Slide 2: Background
Performance gain was observed during the RX filtering and over IEEE Chan D with Blank GI pre-pended WFC [1]
The proposed Blank GI is effective to cope with Inter Symbol Interference (ISI), however still the Intra Symbol Interference remains
  Analysis on Blank GI impact to ISI and Intra Symbol Interference

## Slide 3: Three Waveform Coding Designs
L-LTS occupied for middle 13 tones to generate the waveform
Equal symbol energy of WFC I, II, and III
  TX power is boosted per i and q sample by ,
  where 2, 2.5, 3.33 correspond to 4us/2us, 4us/1.6us, 4us/1.2us, respectively for WFC I, II, and III
  WFC I : No CP
Information “1”
0us 2us 4us
Information “0”
0us 2us 4us
Time dispersion
ISI area

## Slide 4
WFC II: A blank energy GI with 0.8us duration is placed before transmitting each of the 3.2us symbol. The GI is removed at RX before performing symbol detection.
WFC III: A blank energy GI with 0.8us duration is placed before each of the 1.2us ON and OFF portion in a Symbol. The GI is removed at RX before performing symbol detection.
Blank
Information “1”
0us 0.8us 2.4us 4us
Information “0”
0us 0.8us 2.4us 4us
Blank
Information “1”
0us 0.8us 2.0us 2.8us 4us
Information “0”
Blank
GI
Blank
GI
Blank
GI
Blank
GI
0us 0.8us 2.0us 2.8us 4us
ON
OFF
OFF
ON

## Slide 5: Analysis on Inter and Intra Symbol Interference
  WFC I : No CP
  For the simplification of the analysis, it is assumed to have 5 samples per ON portion, and 5 samples per OFF portion.
  Analysis is done over 4 symbols (4 bit WUR data)
  Delay spread is assumed to be across two samples
  5 samples are not mixed with another portion or symbol in a different energy  weight 1, weight 0 otherwise
2us
4us
6us
8us
10us
12us
14us
ON
OFF
OFF
ON
ON (OFF)
OFF (ON)
OFF (ON)
ON (OFF)
ON (OFF)
OFF (ON)
OFF (ON)
ON (OFF)
ON (OFF)
OFF (ON)
OFF (ON)
ON (OFF)

## Slide 6
 |  |  |  | Sum of weights
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 2
0 | 1 | 0 | 1 | 3
0 | 1 | 1 | 0 | 2
0 | 1 | 1 | 1 | 1
0 : OFF – ON
1: ON - OFF
 |  |  |  | Sum of weights
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 2
1 | 0 | 1 | 0 | 3
1 | 0 | 1 | 1 | 2
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 2
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0

## Slide 7
  WFC II : Blank GI pre-pended to a Symbol
  For the simplification of the analysis, it is assumed to have 2 samples per Blank GI, 4 samples per ON portion, and 4 samples per OFF portion.
  Analysis is done over 4 symbols (4 bit WUR data)
  Delay spread is assumed to be across two samples
  4 samples are not mixed with another portion or symbol  weight 1, weight 0 otherwise
ON
OFF
OFF (1)
ON
ON
OFF
OFF (1)
ON
ON
OFF
OFF (1)
ON
ON
OFF
OFF (1)
ON
4us
8us
12us
Removed by GI removal

## Slide 8
  WFC III : Blank GI pre-pended to each ON/OFF portion
  For the simplification of the analysis, it is assumed to have 2 samples per Blank GI, 3 samples per ON portion, and 3 samples per OFF portion.
  Analysis is done over 4 symbols (4 bit WUR data)
  Delay spread is assumed to be across two samples
  3 samples are not mixed with another portion or symbol  weight 1, weight 0 otherwise
ON
OFF (1)
OFF (1)
ON
ON
OFF (1)
OFF (1)
ON
ON
OFF (1)
OFF (1)
ON
ON
OFF (1)
OFF (1)
ON
4us
8us
12us
Removed by GI removal

## Slide 9: Trivial for the Analysis
The expected value of the sum of weights indicates the performance of compensating the ISI, Inter Portion Interference as well as Intra Symbol Interference
  WFC III > WFC II > WFC I
  The gain of the expected value is always 3 dB between WFC III and WFC II regardless of the number of symbols
  The gain of the expected value between WFC II and WFC I depends on the number of symbols, that is, the larger the size of symbols, the bigger gain on the expected value is observed
Time diversity to compensate the deep fades of the channel is not considered in the analysis
  WFC I > WFC II > WFC III for time diversity
Spectrum in the freq domain gets increased for the shorter pulse in time domain
  WFC III > WFC II > WFC I for the size of the side lobes in freq domain

## Slide 10: Performance of different RX Filter Taps w/ or w/o Blank GI
AWGN and RF impairments (CFO and Phase noise) considered
Packet size, 100 bits

## Slide 11: Performance over Chan D
Waveform Coding applied with L-LTS
based waveform generation
Over-sampled to 100 MHz and TX filter applied
@ 4MHz BW and 100 MHz Sampling rate
for the image rejection
After Chan D is applied, down-convert the signal
to 20 MHz sampling rate based signal and then
AWGN is added  20 MHz based SNR
LPF at the RX is applied @ 4 MHz BW and
20 MHz sampling rate
RF impairments (CFO and Phase noise) considered
Packet size, 100 bits

## Slide 12: RF impairments Baseband model
CFO is 200 ppm of 2.4 GHz, i.e., -240 KHz ~ 240 KHz
  Linearly shifts every 4 usec (based on 802.11 residual CFO model)
    “n” varies linearly every 4 usec in
    4 usec is the data rate, 250 KHz
Phase noise based on 802.11 phase noise model
AWGN
Phase
Noise
Carrier
Freq
Offset
X
X
+
RF impairments
Phase
Noise
AWGN
Baseband
Signal

## Slide 13: Conclusion
Analysis and more simulations are provided
  WFC III shows the best in the analysis
  In consideration of the time diversity and spectrum efficiency, WFC II is a good choice between ISI compensation and time diversity
  Smaller filter taps are better to avoid ISI and Intra Symbol Interferences
    Trade-off between Interference rejection and ISI
    We will follow the filter design according to EVM documentation, once it is decided

## Slide 14: Reference
[1] Junghoon Suh, et. al. “17/696r0 Blank GI for the Waveform Coding”, IEEE 802.11 TGba, May 2017, Daejeon, South Korea