## Slide 1: WUR Beacon Frame Format
Date: 2018-1-11
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Background
WUR Beacon frame can be transmitted periodically to WUR STAs for synchronization.
The FCS carries the CRC of the frame
TXID is a transmitter identifier that is decided by the AP, e.g., Partial BSSID or BSS Color
WUR Beacon frame format in 11ba SFD[1]

## Slide 3
Discussion
According to R.4.9.1.K of 11ba SFD [1], the FCS additionally embeds BSSID information. It is not applicable for pre-association WUR frames.
  WUR Beacon frame is NOT a pre-association WUR frame.
  Unlike PCR Beacon frames which need to be received by associated and unassociated STAs, WUR Beacon frames need to be received by associated WUR STAs only.
  The TXID contained in the Address field of a WUR Beacon frame actually becomes redundant.
  BSSID information embedded in the FCS field of the WUR Beacon frame identifies the AP transmitting the WUR Beacon frame.

## Slide 4
Proposal
The Address and TD Control fields jointly indicate 24-bit partial TSF, which help achieve much better WUR synchronization than 12-bit partial TSF
Proposed WUR Beacon frame format
The FCS embeds BSSID information.

## Slide 5: Reference
11-17-0575-08-00ba-spec-framework

## Slide 6: SP
Do you support to make the following modifications in 11ba SFD?
  R.4.9.2.A: The Address field contains an identifier of the transmitter when the frame is WUR Beacon.
  R.4.9.2.B: The Address field and the TD Control field of a WUR Beacon contains the lower and higher portions of the partial TSF, respectively.
  R.4.9.1.F: The contents of the Address field are as defined below
  Y/N/A:
Address field | WUR frame
WID | Unicast Wake Up
GID | Multicast Wake Up
TXID | Beacon, Broadcast Wake Up
Lower portion of partial TSF | Beacon
OUI1 | Vendor Specific