## Slide 1: Efficient Positioning Method using Beacon Frames
Date: 2017-07-12
Authors:

## Slide 2: Abstract
We propose a method for positioning, which can be used in dense multiuser scenarios. The main objective is to reduce the number of transmissions needed.
The proposed method does not require synchronization of the APs and can support a virtually unlimited number of STAs.
Some initial measurements results are provided.

## Slide 3: Localization in Dense Multi User Scenarios
The Fine Timing Measurement (FTM) protocol generates additional traffic overhead and is hardly applicable in scenarios with a large number of users
According to [1], 384 µs is the minimum time per single FTM exchange
  With 1000 users and 0.5 Hz update rate (one update per 2 seconds) the medium is consumed for 19% of the time. [1]
  With N co-channel APs, the overhead gets N-fold worse [1]
  Averaging is usually used for improving the measurement precision. This additionally increases the overhead

## Slide 4: Solution [IEEE 802.11-16/1249r0] – sequential beacons
The proposed solution has similarities with GPS
  Except: Sequential transmission with virtual synchronization of APs
  AP1 transmits a timing frame (TF) frame to AP2, AP2 to AP3 and so on
  Replies from AP2 to AP1, AP3 to AP2 and so on, can be very short ACKs
  STAs also receive the TFs form the APs
AP1
AP2
AP3
AP4
STA
TF
TF
TF
TF
ACK
ACK
ACK

## Slide 5: Testing scenario
Transceiver
  Channel BW (3dB): 25 MHz, roll-off 1.00
  Sample rate: 50 MSps
  Ranging sequence: m-sequence, 1023 chips, BPSK, 2x oversampling

## Slide 6: Obtained results mobile scenario
Processing
  In software
  4-5 measurements per second
Position filtering
  Moving average 5 last estimates
  Maximum velocity limit
Accuracy: 1-2 meter

## Slide 7: Precision in a static case
Variation of the performed measurements with respect of the mean value
CDF of the estimated distance difference (not a CDF of position estimate)

## Slide 8: Proposed modifications with respect to [IEEE 802.11-16/1249r0]
AP1
AP2
AP3
AP4
BF
BF
BF
BF
STA
APs
  Transmit beacon frames (BF) (not sequentially)
  Receive beacon frames and estimate ToA
  Include estimated ToA in the transmitted beacon frames
STA
  Receives beacon frames and estimates ToA
  Use the ToAs in the beacon frames to estimate position

## Slide 9: Proposed modifications (2)
APs
  Need to be able to listen to the other APs
  Must estimate ToA of the arriving beacon frames and report to the STAs (e.g. including them in beacon frames)
STA
  Must be able to listen to all of the APs – at best simultaneously
Pros:
  Passive, i.e. number of STAs not limited
  Low number of transmissions for positioning purposes
Cons:
  Additional complexity to listen to all APs
  Time between transmission of beacon frames from different nodes must not be too big

## Slide 10: Conclusion
The proposed approach further reduces the number of transmissions needed to perform localization of mobile stations
APs must not be synchronized, but must be able to listen to the neighboring APs
The larger the number of involved APs, the better the precision - scalable system.

## Slide 11: References
[1] Brian Hart et al., Scalable Location, IEEE 802.11-14/1235r0

## Slide 12: Straw pool
Should the APs and STAs support listening on multiple channels simultaneously in order to enable passive positioning of STAs?
Yes: No: Abstain: