## Slide 1: WUR Mode Transition Mechanism
Date: 2017-07-09
Authors:

## Slide 2: Introduction
This submission discusses rules for determining WUR Mode Transition timing

## Slide 3: Power Management
Active mode: The STA receives and transmits frames at any time. The STA remains in the awake state.
Power save (PS) mode: The STA enters the awake state to receive or transmit frames. The STA remains in the doze state otherwise.
WUR mode: The STA turns off the 802.11 main radio but it uses the WUR to receive a wakeup frame which triggers that the STA turns on the 802.11 main radio.

## Slide 4: Entering the WUR Mode
According to IEEE 802.11-2016, a STA can enter the PS mode at any time.
But, what about entering the WUR mode?
  Can a STA enter the WUR mode at any time?
  What if the AP has buffered frame for the STA? In such a case, if the STA enters the WUR mode, the unnecessary subsequent Wakeup frame can waste the wireless medium.

## Slide 5: Entering the WUR Mode
A STA may enter the WUR mode only if the AP does not have any buffered frame individually addressed to the STA and also the STA’s buffers are empty.
Otherwise, a STA shall not enter to WUR mode.

## Slide 6: Entering the WUR Mode
A STA in the PS mode can know if the AP has any buffered frame individually addressed to the STA or not via:
  More Data subfield in Frame Control field in MAC header indicate
    A non-DMG STA uses the More Data subfield to indicate to a STA in PS mode that more BUs are buffered for that STA at the AP. The More Data subfield is valid in individually addressed Data or Management frames transmitted by an AP to a STA in PS mode.
  TIM element
    Each bit in the traffic indication virtual bitmap corresponds to traffic buffered for a STA within the BSS that the AP is prepared to deliver at the time the Beacon frame is transmitted.

## Slide 7: Entering the WUR Mode
But, a STA in the Active mode can’t know if the AP has any buffered frame individually addressed to the STA or not.
Proposal
  Option 1) A STA in the Active mode shall not directly enter the WUR mode. The power management transition must follow the below:
    First step: The STA in Active mode moves to the PS mode.
    Second step: The STA in PS mode checks if the AP has any buffered frame individually addressed to the STA or not, through the More Data subfield in Frame Control field in MAC header or the TIM element as shown in Slide 6.
    Third step: The STA moves to the WUR mode only if the AP does not have any buffered frame individually addressed to the STA and also the STA’s buffers are empty.
Active mode
PS mode
WURmode

## Slide 8: Entering the WUR Mode
Proposal
  Option 2) When a STA in the Active mode succeeds in WUR setup, an AP signals to the STA if any buffered frame individually addressed to the STA exists or not.
    When the AP succeeds the WUR setup with the STA in the Active mode, the More Data subfield is set to 1 for indicating to the STA in the Active mode that more BUs are buffered for that STA at the AP.
    When the AP succeeds the WUR setup with the STA in the Active mode, each bit in the traffic indication virtual bitmap that corresponds to traffic buffered for the STA in the Active mode is set to 1.
    And, the STA in the Active mode may enter the WUR mode only if the AP does not have any buffered frame individually addressed to the STA and also the STA’s buffers are empty.

## Slide 9: Entering the WUR Mode
In a congested traffic environment, an AP needs to have a tool for actively controlling a wakeup frame overload.
For this purpose, a WUR Mode transition timer can be defined as follows:
  A STA may enter the WUR mode only if the AP does not have any buffered frame individually addressed to the STA for a WUR Mode transition timer and also the STA’s buffers are empty.
  Otherwise, a STA shall not enter to WUR mode.
WUR Mode transition timer can be negotiated in the WUR setup procedure.

## Slide 10: Exiting from the WUR Mode
A STA should send a response frame to the AP using primary connectivity radio after receiving an unicast wake-up packet [1].
  Any response frame received from 802.11 main radio can be used to indicate that a STA is in Active mode or PS mode.
  However, a STA that has been in WUR mode for a long time may have a security vulnerability.
  Similar to the BSS Max Idle Period management, an AP and a STA can negotiate if a STA shall use the protected frame as the response frame for a exiting from WUR mode.
AP
WUR STA
Attacker
WUR Mode
PS mode
PS-Poll
ACK
DATA
ACK

## Slide 11: Summary
This submission proposes rules for determining WUR Mode Transition timing.
  Entering the WUR Mode.
  Exiting from the WUR Mode.

## Slide 12: References
[1] https://mentor.ieee.org/802.11/dcn/17/11-17-0575-01-00ba-spec-framework.docx

## Slide 13: Straw Poll 1
Do you support the following WUR Mode Transition Mechanism?
  A STA in the WUR mode should enter the doze state only if the AP does not have any buffered frame individually to be addressed to the STA and also the STA’s buffers are empty.

## Slide 14: Straw Poll 4
Do you support the following?
  An AP and a STA can negotiate if the response frame transmitted to the AP using primary connectivity radio after receiving a unicast wakeup packet shall be the protected frame.