## Slide 1: Power Save Mode for WUR
Date: 2017-07-07
Authors:

## Slide 2: Introduction
This presentation discusses how to integrate WUR into the current power save mode

## Slide 3: Recap of the current power save mode
An 802.11 STA can work in the active mode or power save mode
  A STA can be in awake state or doze state under power save mode
  The STA periodically receives TIM for traffic indication information in the Beacon frame
  The STA sends PS-Poll to the AP to indicate it’s in awake state
  The STA goes back to doze state after receiving a frame with more data=0
Awake State
Doze State
Send PS-Poll
More data = 0
Awake State
Power Management = 1
Power Management = 0
Active Mode
Power Save Mode

## Slide 4: Rules of the current power save mode
AP behavior: The STAs that currently have buffered BUs within the AP are identified in a TIM, which shall be included as an element within all Beacon frames generated by the AP.
STA behavior: A STA shall determine that a BU is buffered for it by receiving and interpreting a TIM. A STA operating in PS mode that is not in WNM sleep mode shall periodically listen for Beacon frames, as determined by the ListenInterval parameter of the MLME-ASSOCIATE.request or MLME-REASSOCIATE.request primitive and the ReceiveDTIMs parameter of the MLME-POWERMGT.request primitive

## Slide 5: WUR mode
Passed Motion: Move to add the following to 11ba SFD:
  Define WUR Action frame to enable WUR negotiation
  Note that WUR Action frame is sent through primary connectivity radio
Passed Motion: WUR mode signaling shall be defined for the WUR STA to enter the WUR mode
  Explicit or implicit signaling is TBD
  If signaling is explicit, WUR mode signaling is done on the Primary connectivity radio
  Wake-up operating parameter may be notified in WUR mode signaling
  Detailed parameters are TBD

## Slide 6: Integration with the current power save mode
How to integrate the WUR mode with the current power save mode?
  Opt1: A STA can be in either the current power save mode or the WUR sleep mode
  Opt2: A STA can be in both the current power save mode and the WUR sleep mode
We can go with Opt2, then the design of WUR sleep mode is decoupled with the current power save mode, which simplifies the SPEC design

## Slide 7: Motivation
If a STA uses both the power save mode and the WUR mode simultaneously, the STA shall
  Wakeup its PCR periodically to receive the Beacon, and check the TIM in the Beacon
  Turn on its WURx, and receives the WUP from the AP
In that case, when the STA uses both the power save mode and the WUR mode simultaneously, the power consumption is even higher than that of the current power save mode

## Slide 8: Proposed change to the current power save mode
We propose that when the STA uses both the power save mode and the WUR mode simultaneously:
  The STA does NOT need to wake up its PCR periodically to receive the Beacon

## Slide 9: Conclusion
In this contribution, we propose some rules when the traditional power save mode and the WUR mode are used simultaneously

## Slide 10: Straw Poll 1
Do you support that the STA does not need to wake up its PCR periodically to receive the Beacon when the STA uses both the power save mode and the WUR mode simultaneously?

## Slide 11: Motion 1
Move to add the following to the 802.11ba SFD:
the STA does not need to wake up its PCR periodically to receive the Beacon when the STA uses both the power save mode and the WUR mode simultaneously

## Slide 12: Reference
11-17-0575-01-00ba-spec-framework