## Slide 1: Considerations on WUR frame format
Date: 2017-07-04
Authors:

## Slide 2: Introduction
Certain WUR operations have been defined in the SFD
  Synchronization based on WUR Beacon RX which carries partial TSF[1]
  Unicast WUR operation for waking up an individual WUR STA
  Multicast WUR operation for waking up multiple/all WUR STAs
However the WUR frame format has not been defined yet:
  Not using MAC addresses for identifying the TX/RX entities[2]
We propose to introduce some basics for the WUR frame format
  With special considerations to the incurring overhead (keep at minimum)
  Providing required signaling for RX(s)/TX IDs
  Provide flexibility for a wide range of use cases and scenarios

## Slide 3: Considerations
Propose a WUR frame that follows IEEE802.11 structure:
  PHY Preamble to contain information for decoding the PSDU
    The PSDU contains one MPDU (frame) which in turn contains
      MAC header
        Common fields present in every WUR frame
        Type specific fields that may not be present in every WUR frame
      Frame Body – Does not carry data payloads
      FCS – cyclic redundancy check or message integrity check depending on the type of WUR frame
Target a WUR frame format that minimizes required TX times
  Expect very low TX rates, e.g. 62.5Kbps & operation in heavily utilized ISM bands
    For example transmitting 7 Bytes of MPDU would require ~1 ms TX time
      Assumed that PHY preamble and each octet of PSDU would cost 128 us of TX time
 | PHY Preamble | MAC Header | Frame Body | FCS
PSDU [MPDU]
WUR PPDU
 | Frame Control | Paged IDs (RA) | PBSS ID (TA) | Timestamp | Reason
Octets | 1 | TBD | TBD | TBD | TBD
CRC/MIC/BSS
TBD

## Slide 4: MAC Header
Frame Control [1B] - Information required to identify the MPDU type/length etc.
  Protocol Version [1b] – Use 0 and let 1 for our kids
  Type subfield [2b] – Different frame types can be defined (e.g., WUR Beacon, WUR Control frame)
  Length/Subtype [3/4b] subfield different frame subtypes or Paged IDs length (recommend 3 bits)
  Reserved [2b] – Reserved for future use (one bit maybe used for security)
  NOTE:FC field can be moved to the PHY preamble if there is a SIG field in it
PBSSID ID [TBD]– Early identification of the BSS (recommend TBD=0 Bytes)
  Could be used by STA to early terminate reception of WUR frames not generated by its AP
    Preferred to have some bits in the PHY preamble for this purpose (similar to HE and S1G BSS Color (e.g., 3 bits)
  Additionally BSS identifier is also hidden in the FCS and/or Paged IDs field (see next slides)
Timestamp [TBD] – Contains partial TSF that can be used by WUR STAs for (recommend TBD=1 Bytes)
  Synchronizing the internal clocks of all STAs associated to that AP [1] and also for replay attack avoidance (see next slides)
  The Timestamp field may not be present in all types of packets
 | PHY Preamble | MAC Header | FCS
WUR PPDU
 | Frame Control | Paged IDs | PBSS ID | Timestamp
Octets | 1 | TBD | TBD [0] | TBD [1]
CRC/MIC/BSS
TBD

## Slide 5: Paged IDs
One or more Paged IDs [1B each or 2B each] – List of intended receivers
  Option 1: One octet is sufficient to identify 256 STAs, and if more then AP can:
    Schedule clones in orthogonal periods to avoid waking unintended STAs
    Pros: Reduced field size leads to minimal overhead
    Cons: Some loss of flexibility
  Option 2: Two octet is sufficient to identify up to 2007 STAs and AP can:
    Pros: Same signaling as PCR, flexible, allows extra control information to be exchanged
    Cons: increased field size leads to increased overhead
  Multiple Paged IDs are present in multicast WUR frames (Length dependent)
    For paging more than 8 STAs then AP can use group ID (similar to 11ac) or
    Send back2back WUR frames (IDs in ascending order to optimize sleep pattern)
  One Paged ID is present in unicast and broadcast WUR frames
    Value 0 of Paged ID reserved for broadcast, and each Paged ID can be XORed with Partial BSS Identifier
 | PHY Preamble | MAC Header | FCS
WUR PPDU
 | Frame Control | Paged IDs | PBSS ID | Timestamp
Octets | 1 | TBD [1-8/2-16] | 0 | 1
CRC/MIC/BSS
TBD
AID8
8
Paged ID field
AID12 | WUR Control
12 | 4
Paged ID field

## Slide 6: Additional Considerations
Many proposals to have a field for special purposes [3, …]
  Depends on compelling reasons and/or decisions
  Currently propose to not be present (recommend TBD=0)
 | PHY Preamble | MAC Header | FCS
WUR PPDU
 | Frame Control | Paged IDs (RA) | PBSS ID (TA) | Timestamp | Reason
Octets | 1 | 1 to 8 | 0 | 1 | TBD
CRC/MIC/BSS
TBD

## Slide 7: FCS
The FCS [TBD] contains:
  CRC - Cyclic redundancy check for detecting errors in unsecured MPDU
  MIC – Message integrity check for detecting errors and replay attacks in secure MPDU
    No need for explicit CRC in this case
BSS identifier is hidden within the FCS:
  For example the AP XORs the BSSID (e.g., BSSID[23:38]) with the FCS
    Or CRC/MIC is computed assuming presence of BSS ID, but BSS ID itself is not sent in the frame
  STA successfully decodes only WUR frames generated by its AP
  WUR frames generated by other APs will come up as corrupted
  Avoids sending the (Partial) BSS ID field
Propose an FCS field of 2 or 3 octets (recommend TBD=2 Bytes):
  Provide good protection, low false alarms, and prevent replay attacks
 | PHY Preamble | MAC Header | FCS
WUR PPDU
 | Frame Control | Paged IDs | PBSS ID | Timestamp
Octets | 1 | 1 to 8 | 0 | 1
CRC/MIC/BSS
TBD

## Slide 8: Security considerations
Ensure that STAs are not woken up by messages of an attacker
  Proposal is to have a simple security protocol with low incurred overhead
    Avoid CCMP-like signaling (MIC of 8/16 Bytes, CCMP header of 8 bytes)
    Where MIC is a truncated output of the selected cipher suite (baseline) and
    TSF timer can act as the packet number in some cases
      A packet number could be used for the multicast case, although out of scope for this presentation
As such WUR frames can be:
  Unsecure: The FCS contains the CRC with camouflaged BSS ID
  Secure: The FCS contains the MIC with camouflaged BSS ID
With Frame Control field signaling differentiating them
  Maybe a bit that differentiates between them
 | PHY Preamble | MAC Header | FCS
WUR PPDU
 | Frame Control | Paged IDs | PBSS ID | Timestamp
Octets | 1 | 1 to 8 | 0 | 1
CRC/MIC/BSS
2

## Slide 9: Security considerations
MIC computation is based on the entire MPDU
  Can be intended to one single STA or to multiple STAs
MIC is generated based on a PCR group key, i.e., IGTK
  Known by all STAs associated to the AP that are the intended receivers
Partial TSF in Timestamp provides part of the monotonically increasing counter
  E.g., the Timestamp contains the most significant byte (MSB) of the 2 LSBs of the TSF timer
    Providing 256 us steps in time and a wrap around of the timestamp every 65536 ms [1]
  Full TSF timer at STA is updated using the partial TSF of the Timestamp [1]
    Full TSF timer is given as input parameter for the MIC computation
    Which in turn protects from replay attacks
 | PHY Preamble | MAC Header | FCS
WUR PPDU
 | Frame Control | Paged IDs | PBSS ID | Timestamp
Octets | 1 | 1 to 8 | 0 | 1
CRC/MIC/BSS
2

## Slide 10: Summary
We propose a WUR frame format that:
  Provides flexibility to cover a wide range of scenarios
  Has short sizes [5B-12B or 6B-20B MPDU lengths]
    Reducing any redundancies and minimizing TX times
      TX time ranges between ~0.8ms to ~1.7ms @ 62.5Kbps
      TX time ranges between ~0.9ms to ~2.7ms @ 62.5Kbps
  Allows unicast, multicast, and broadcast addressing
  Provides security and signaling for a wide range of applications
 | PHY Preamble | MAC Header | FCS
WUR PPDU
CRC/MIC/BSS
2
 | Frame Control | Paged IDs | Timestamp
Octets | 1 | 1-8 or 2-16 | 1

## Slide 11: Straw Poll 1
Do you agree to have a Type field that identifies the type of WUR frame?

## Slide 12: Straw Poll 2
Do you agree to wake-up a group of STAs using a group identifier in a WUR frame (e.g., similar to 11ac grouping)?

## Slide 13: Straw Poll 3
Do you agree to optionally protect WUR frames using message integrity check (MIC)?

## Slide 14: Straw Poll 4
Do you agree to define a Frame Check Sequence (FCS) that could carry either the MIC (if protected frame) or the CRC (if unprotected frame) of the frame?
  Length and computation of FCS is TBD (for both MIC and CRC)

## Slide 15: References
[1] S. Shellhammer (Qualcomm), “17/671r2 Considerations on WUR Synchronization”
[2] L. Chu (Marvell), “17/124r4 WUR MAC and Wakeup Frame”
[3] X. Wang (InterDigital), “17/387r6 Purpose Indication for WUR Packets”