## Slide 1: Considerations on WUR frame format
Date: 2017-07-04
Authors:

## Slide 2: Introduction
Certain WUR operations have been defined in the SFD
  Synchronization based on WUR Beacon RX which carries partial TSF[1]
  Unicast WUR operation for waking up an individual WUR STA
  Multicast WUR operation for waking up multiple/all WUR STAs
However the WUR frame format has not been defined yet:
  Not using MAC addresses for identifying the TX/RX entities[2]
We propose to introduce some basics for the WUR frame format
  With special considerations to the incurring overhead (keep at minimum)
  Providing required signaling for RX(s)/TX IDs
  Provide flexibility for a wide range of use cases and scenarios

## Slide 3: Considerations
Propose a frame format that enables:
  Constant-length WUR frames
    Constant length for all these frame types
    Contains necessary information for interoperation (mandatory in RX)
      Simplifies receiver implementation while preserving essential functionalities
    E.g., constant MPDU size of 6 Bytes (~0.9ms of TX time@62.5Kbps)
  Variable-length WUR frames
    Length indicated in the MAC header
    Contains additional information for optional features (optional in RX)
      Advanced receiver implementation capable of processing variable lengths
    E.g., maximum MPDU size of 13 Bytes (~1.7ms of TX time@62.5Kbps)
WUR PPDU
 | PHY Preamble | MAC Header | Frame Body | FCS

## Slide 4: MPDU format
 | Frame Control | Address | TSD Control
Bits | TBD | TBD | TBD
Propose a WUR frame that follows the IEEE802.11 structure:
  PHY Preamble to contain information for decoding the PSDU
  The PSDU contains one MPDU (frame) which in turn contains
    MAC header - Common fields present in every frame, and is of fixed size
    Frame Body – Does not carry data payloads, and is present in variable length frames
    FCS – cyclic redundancy check or message integrity check depending on the frame type
Target a WUR frame format with reduced transmit times
  Expect very low TX rates, e.g. 62.5Kbps & operation in heavily utilized ISM bands
    For example transmitting 7 Bytes of MPDU would require ~1 ms TX time
      Assumed that PHY preamble and each octet of PSDU would cost 128 us of TX time
 | PHY Preamble | MAC Header | Frame Body | FCS
WUR PPDU
CRC/MIC
TBD

## Slide 5: Frame Control field
Frame Control [1B]-Information identifies MPDU type/length, etc.
  Protocol Version [0/1b] – Use 0 and let 1 for future use (if needed)
  Type subfield [2/3b] – Differentiates types (e.g., WUR Beacon, Wake Up)
    Certain frame types can be constant length frame
    Other types if defined need to be inline with this frame format
  Length/Subtype [3/4b] subfield different frame subtypes/length
    Indicates frame subtype for constant length frames
    Indicates length for variable length frames
  Reserved [TBD] – Reserved for future use
    Maybe one bit for protected frames
MAC Header | Frame Body | FCS
 | Frame Control | Address | TSD Control
Bits | TBD | TBD | TBD
CRC/MIC
TBD
Miscellaneous
0 or more

## Slide 6: MPDU format (samples)
Address field contains the identifier of the frame
  When the frame is a broadcast frame it contains a partial transmitter identifier
  When the frame is a unicast or multicast frame it contains a partial receiver(s) identifier
TD Control field contains control information that is type dependent
  For WUR Beacon contains partial TSF; For Wake Up contains packet number/partial TSF, etc.
    Other contents for each WUR frame depends on functionality and security protocol and is TBD
Frame Body field is only present in variable length frames
  Presence is indicated by a nonzero Length field in the Frame Control and is optional in RX
  A list of paged IDs can be contained in Frame Body field of Wake Up frame (see next slide)
    Useful to individually identify more than one STA
 | Frame Control | PBSSID(TA) | PTSF
 | PHY Preamble | MAC Header | Frame Body | FCS
WUR PPDU
Beacon (constant)
Uni/multi Wake Up (constant)
 | Frame Control | Paged ID(RA) | PN/PTSF
CRC/MIC
CRC/MIC
6
6
Miscellaneous
variable
 | Frame Control | Address | TSD Control
Bits | 8 | 12 | 12
General format
Not present
Uni/multi Wake Up (variable)
 | Frame Control | Paged ID(RA) | PN/PTSF
CRC/MIC
6+[1-7]
Miscellaneous
Not present
1 or more
CRC/MIC

## Slide 7: List of Paged IDs
One or more Paged IDs [1B each or 2B each] – List of intended receivers
  Option 1: One octet is sufficient to identify 256 STAs, and if more then AP can:
    Schedule clones in orthogonal periods to avoid waking unintended STAs
    Pros: Reduced field size leads to minimal overhead, Cons: Some loss of flexibility
  Option 2: Two octet is sufficient to identify up to 2007 STAs and AP can:
    Pros: Same signaling as PCR, flexible, allows extra control information to be exchanged
    Cons: increased field size leads to increased overhead
Paged ID List can only be present in variable length Wake Up frames
  For paging more than 8 STAs then AP can use group ID (similar to 11ac) or
  Send back2back WUR frames (IDs in ascending order to optimize sleep pattern)
Only one Paged ID is present in constant length Wake Up frames (no Frame Body)
  Frame is either individually addressed to one STA (e.g., STA AID),
  Or addressed to multiple STAs (e.g., using a group ID similar to 11ac)
 | PHY Preamble | MAC Header | Frame Body | FCS
WUR PPDU
AID8
8
AID12 | WUR Control
12 | 4
 | Frame Control | Paged ID(RA) | PN/PTSF
Paged ID List
TBD [1-7/2-15]

## Slide 8: FCS
The FCS [TBD] contains:
  CRC - Cyclic redundancy check for detecting errors in unsecured MPDU
  MIC – Message integrity check for detecting errors and replay attacks in secure MPDU
    No need for explicit CRC in this case
BSS identifier can be hidden within the FCS:
  For example the AP XORs the BSSID (e.g., BSSID[23:38]) with the FCS
    Or CRC/MIC is computed assuming presence of BSS ID, but BSS ID itself is not sent in the frame
  STA successfully decodes only WUR frames generated by its AP
  WUR frames generated by other APs will come up as corrupted
  Avoids sending the (Partial) BSS ID field
Propose an FCS field of 2 or 3 octets (recommend TBD=2 Bytes):
  Provide good protection, low false alarms, and prevent replay attacks
 | PHY Preamble | MAC Header | FCS
WUR PPDU
CRC/MIC
TBD

## Slide 9: Security considerations
Ensure that STAs are not woken up by messages of an attacker
  Proposal is to have a simple security protocol with low incurred overhead
    Avoid CCMP-like signaling (MIC of 8/16 Bytes, CCMP header of 8 bytes)
    Where MIC is a truncated output of the selected cipher suite (baseline) and
    TSF timer can act as the packet number in some cases
      A packet number could be used for the multicast case, although out of scope for this presentation
As such WUR frames can be:
  Unsecure: The FCS contains the CRC with camouflaged BSS ID
  Secure: The FCS contains the MIC with camouflaged BSS ID
With Frame Control field signaling differentiating them
  Maybe a bit that differentiates between them
 | PHY Preamble | MAC Header | FCS
WUR PPDU
CRC/MIC
2

## Slide 10: Security considerations
MIC computation is based on the entire MPDU
  Can be intended to one single STA or to multiple STAs
MIC is generated based on a PCR group key, i.e., IGTK
  Known by all STAs associated to the AP that are the intended receivers
Partial TSF provides part of the monotonically increasing counter
  E.g., the Timestamp contains the most significant byte (MSB) of the 2 LSBs of the TSF timer
    Providing 256 us steps in time and a wrap around of the timestamp every 65536 ms [1]
  Full TSF timer at STA is updated using the partial TSF of the Timestamp [1]
    Full TSF timer is given as input parameter for the MIC computation
    Which in turn protects from replay attacks
 | PHY Preamble | MAC Header | FCS
WUR PPDU
CRC/MIC/BSS
2

## Slide 11: Summary
We propose a WUR frame format that:
  Provides flexibility to cover a wide range of scenarios
  Has short sizes [6B-13B MPDU lengths]
    Reducing any redundancies and minimizing TX times
      TX time ranges between ~0.9ms to ~1.8ms @ 62.5Kbps
  Allows unicast, multicast, and broadcast addressing
  Provides security and signaling for a wide range of applications
 | PHY Preamble | MAC Header | Frame Body | FCS
WUR PPDU
 | Frame Control | Address | TSD Control
Bits | TBD | TBD | TBD
CRC/MIC
TBD

## Slide 12: Straw Poll 1
Do you agree with the following MAC frame:
  The length of the MAC header is fixed
  Whether the Address field contains more than one identifier is open for discussion
  Results: Y 18, N 2, A 10.
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | TBD | TBD | TBD

## Slide 13: Straw Poll 2
Do you agree to have a Type subfield that identifies the WUR frame type?
  The Type subfield is contained in the Frame Control field of the MAC header
  One Type subfield value assigned to WUR Beacon and one to Wake Up frame
Results: Y 9, N 0, A 14

## Slide 14: Straw Poll 3
SP3a: Do you agree to have in the Address field an identifier that:
  Is the identifier of the transmitter when the frame is WUR Beacon
Results: Y 18 , N 1, A 7
SP3b: Do you agree to have in the Address field an identifier that:
  Is the identifier of the receiver when the frame is unicast Wake Up
    Presence of an additional addressing identifier is open for discussion
Results: Y 10, N 8, A 8

## Slide 15: Straw Poll 4
Do you agree to have a Type Dependent (TD) Control field in the MAC header that contains type dependent control information?
  The TD Control field of a WUR Beacon contains the partial TSF
Results: Y 10, N 0, A 10

## Slide 16: Straw Poll 5
SP5a: Do you agree to have an optionally present Frame Body field in the MPDU?
  The length of the Frame Body field is signaled in the Frame Control field
  It is optional for a STA to support reception of a frame with nonzero length Frame Body
Results: Y 5, N 6, A 14
SP5b: Do you agree to have an optionally present Frame Body field in the MPDU?
  It is optional for a STA to support reception of a frame with nonzero length Frame Body
Results: Y 5, N 0, A 20

## Slide 17: Straw Poll 5c
Do you agree to define a Frame Check Sequence (FCS) that carries the CRC of the frame?
  Length and computation of FCS is TBD
Results: Y 21, N 0, A 5

## Slide 18: Straw Poll 6
Do you agree to authenticate WUR frames using message integrity check (MIC)?
  This procedure is optional
Results:

## Slide 19: Straw Poll 6
Do you agree to define a Frame Check Sequence (FCS) that could carry either MIC (if protected frame) or CRC (if unprotected frame) of the frame?
  Length and computation of FCS is TBD (for both MIC and CRC)

## Slide 21: References
[1] S. Shellhammer (Qualcomm), “17/671r2 Considerations on WUR Synchronization”
[2] L. Chu (Marvell), “17/124r4 WUR MAC and Wakeup Frame”
[3] X. Wang (InterDigital), “17/387r6 Purpose Indication for WUR Packets”