## Slide 1: Vendor Specific WUR Frame
Date: 2017-07-10
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Daniel F Bravo |  |  |  | DanielF.Bravo@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com

## Slide 2: Abstract
We have agreed to have unicast/multicast wake-up frame and WUR Beacon
We discuss the need for an vendor specific WUR frame

## Slide 3: Need for Vendor Specific WUR Frame
We expect that only the basic function of WUR, specifically the wake-up operation, is going to be designed in IEEE to meet the timeline of 11ba.
However, we recognize that there could be potential applications of low power WUR for enhancement and other applications, and there is likely to be following WFA program or vendor specific design to fulfil the need.
In the current 802.11 spec, vendor specific public action frame and vendor specific element, etc., are designed for this purpose.
We think it is required to design a container to enable similar purpose in 11ba.

## Slide 4: Consideration for Vendor Specific WUR Frame
To carry vendor specific content, we think the design shall not be limited to extend unicast/multicast wake-up frame or WUR Beacon
  The new invention may not be related to wake up operation
  The new invention may not related to WUR Beacon transmission
  Overload unicast/multicast wake up frame or WUR Beacon for future extension may increase the overhead due to additional design consideration and possibilities. Note that WUR data rate is expected to be as low as 62.5 kbps.
We propose to define Vendor Specific WUR frame
  An entry in type/subtype field can be used for the purpose
  The most flexible approach and a frame container is designed for this purpose

## Slide 5: Content for Vendor Specific WUR Frame
We understand that the discussion of unicast/multicast WUR frame and WUR Beacon frame format is ongoing
  Alignment with the design can be done
  Similar ideas or format maybe reused
For now, we only identify some basic element below
  Way to identify the specific vendor
    Similar requirement of identifying the transmitter for other WUR frames
  Way to validate the frame
    Similar requirement for other WUR frames
  Way to limit the length
    May only allow several predefined length and have indication for it
An example is shown below
Type | Vendor ID | Length | Vendor specific content | FCS

## Slide 6: Conclusion
We propose to define a vendor specific WUR Frame
  Have a specific entry in the type/subtype field for this purpose
  Enable future invention in WFA
  Enable further invention for specific vendor