## Slide 1
WUR with conventional 802.11 power save
follow up
Date: 2017-07-10
Authors:

## Slide 2: Introduction
WUR in Conventional Power Save procedure has been discussed[1][2][3]
11ba does not need to change legacy power save protocol to use WUR procedure[1][2]
  Does not need to change legacy power save protocol, only additional procedure and additional fields which have been reserved are utilized, if they are required
Multiuser WUR shall be considered because of its delay and power save requirements[4]
  Broadcast (Multicast) WUP and its basic procedure is defined[4]
  PSMP is the conventional power save mechanism for multi user case
In order to achieve power save requirements, WUR duty cycle need to be considered in legacy power save modes, too
  WUR duty cycle mode element could be exchanged in legacy power save procedures

## Slide 3: 802.11 power save coexistence with WUR
WUR AP could transmit both multicast WUR signal and unicast WUR signal[4]
  Multicast WUR signal could be transmitted for transmitting multicast or broadcast frame(s)
WUR procedures for the conventional 802.11 power save mechanisms are not defined in 802.11ba
  Coexistence with legacy power save STAs shall be considered
  Independent procedure or harmonized procedure
WUR could be utilized in Conventional Power Save procedure[1][2]
  WUR could be operated in conventional power save procedures
  Conventional power save with WUR could be regarded as implicit WUR procedure
  Explicit WUR procedures also could be discussed as a new 11ba procedure

## Slide 4: PS-Poll with WUR
Without any changes on the conventional power save procedure, WUR could be utilized
However it requires large delay and additional power usage due to TIM reception delay

## Slide 5: U-APSD with WUR
Without any changes on the conventional U-APSD procedure, WUR could be utilized
U-APSD does not require additional delays caused by channel access of an AP because presence check is initiated by an uplink STA

## Slide 6: Modified PS Poll with WUR
If PS-poll frame is needed to be utilized in WUR procedure, spec shall specify to regard WUR frame reception as a TIM reception
It could be a basic WUR operation for unicast WUP

## Slide 7: PSMP with WUR
Because wake-up frame and the preparation period do a role of time scheduler, additional scheduling procedure for PSMP frame is not needed
Multiple users could be supported and WUR STAs could be set to doze state during PSMP service period
Legacy STAs and WUR STAs could coexist in single PSMP sequence

## Slide 8: PSMP with WUR duty cycle information
PSMP action frame could include additional fields to control WUR parameters
PSMP action frame may be transmitted after broadcast WUP and PSMP could indicates WUR configuration parameters

## Slide 9: PSMP with WUR duty cycle information
PSMP frame have some reserved field and reserved type(=0 or 3)
WUR could utilize these reserved bits for WUR configuration
Specific WUR-PSMP group address field and other parameter fields need to be discussed for WUR configuration

## Slide 10: Conclusions
Conventional Power Save needs to be supported in 802.11ba
For unicast wake-up procedure, conventional power save modes do not require major changes on existing spec
  Additional procedures and information fields using reserved bits could be defined for coexistence, it requires further discussions
For multicast wake-up procedure, using PSMP could be a solution
  It provides scheduling information over its PSMP service period
  Group addressed transmission time need to be used for MU transmission period (DTT would be used for MU transmission)
WUR duty cycle configuration in conventional power save mode could be considered to optimize power consumption

## Slide 11: References
[1] 11-17-0653-00 “Examples of integrating WUR with existing power save”
[2] 11-17-0716-03 “WUR with conventional 802.11 power save”
[3] 11-17-0936-00 “Integration of WUR to Power Save Mode”
[4] 11-17-0575-01 “Specification Framework for TGba”

## Slide 12: Straw poll
Do you agree to add the followings to 802.11ba SFD?
  802.11ba shall define WUR procedures operated with conventional 802.11 power save procedures. Specific WUR configuration procedures in conventional 802.11 power save procedures are TBD.
  Y/N/A