## Slide 1
Status mismatch problem in
WUR transmission procedure
Date: 2017-07-11
Authors:

## Slide 2: Introduction
The wake-up radio transmission procedures are agreed in [1], based on the unicast Wake-up operation
  In unicast WUR operation, a STA should send a response frame to the AP using primary connectivity radio after receiving a unicast wake-up packet.
  AP may retransmit the WUR packet when it does not receive the response frame of wake-up packet from STA.
However, since STA may wake up arbitrary, AP may not know the STA’s state accurately before the Wake-up packet transmission
  If a STA stays in awake state before AP transmits the WUR packet, transmitting undecodable Wake-up packet may cause inefficiency because of the lack of response frame of Wake-up packet
  The undecodable Wake-up packet wastes the channel, interrupting the transmission of other IEEE 802.11 device transmission.
In this presentation, the inefficiency issue of WUR procedure in case of AP’s wake-up packet transmission to the STA in awake state is discussed

## Slide 3: Recap: Wake-up radio procedure
Data transmission procedure using Wake-up radio
  In multicast WUR procedure, after sending the wake-up packet, AP may wait for the wake-up delay, contend to access the channel, and send the downlink packet
  If AP and STA are negotiated to use a response frame in unicast transmission, AP may wait for the response frame (WU Poll) first, and then transmit the data frame

## Slide 4: State mismatch problem in WUR procedure with response frame (1)
If STA’s main transceiver is already turned on before the transmission of Wake-up packet, the new transmission procedure may not be started
  The transition to power save mode is not mandatory, STA may stay in awake state
  AP assumes that the STA is in sleep state, and transmits Wake-up packet in order to transmit the downlink packet
  Since STA’s main transceiver cannot decode the wake-up radio, STA cannot transmit the response frame to the wake-up packet
  AP retransmits the wake-up packets and STA cannot transmit the response frame to the wake-up packet repeatedly, causing the inefficiency of data transmission

## Slide 5: State mismatch problem in WUR procedure with response frame (2)
In previous IEEE 802.11 procedure, STA in awake state doesn’t cause inefficiency of data transmission
The problem occurs because the STA in awake state cannot decode the wake-up packet, when it turns off the WUR
→ The procedure to reduce the inefficiency in needed
To deal with this problem 4 options are possible:
  Indication of STA’s transition to the power save state
  STA’s procedure to enter the power save state implicitly
  Procedure to decode the wake-up packet
  Transmission of IEEE 802.11 frame prior to the wake-up packet

## Slide 6: Option 1: indication of STA’s state transition to AP
Whenever a STA enters WUR state, STA indicates it to AP
Whenever STA wakes up, STA indicates it to AP by sending UL Data frame or Poll frame
However, this procedure wastes power, causing power inefficiency

## Slide 7: Option 2: define the STA’s procedure to enter the power save state implicitly
If there is no data transmission for predetermined time, STA should go to the sleep state
  STA may go back to the sleep state implicitly, without sending the indication packet to the AP
  In this case, the transmission of wake-up packet is not repeated too much, without changing the procedure of structure of WUR procedure
Notes: 과도한 wake-up packe의 재전송이 일어나지 않음.

## Slide 8: Option 3: add the procedure for STA decodes the Wake-up packet
If STA in awake state can decode the wake-up packet, it may response to the wake-up packet immediately after the transmission of wake-up packet
  When the STA’s WUR on in awake state, the wake-up packet can be decoded by STA without changing the packet structure
  If wake-up packet is includes the STA’s address before the wake-up payload, STA may transmit the response frame immediately after the transmission of wake-up packet

## Slide 9: Option 4: transmitting the 802.11 frame
If AP may transmit the 802.11 frame (i.e. TIM, QoS Null frame, etc) prior to the transmission of the wake-up packet, STA in awake state may transmit the response immediately
If STA is in sleep state and transmits no response, AP transmits the wake-up packet to wake the STA up

## Slide 10: Conclusion
In this presentation, we discussed the inefficiency problem when STA is awake and AP transmits the wake-up packet to wake the STA up
To resolve the inefficiency problem, the 4 examples are shown
  Indication of STA’s transition to the power save state
  STA’s procedure to enter the power save state implicitly
  Procedure to decode the wake-up packet
  Transmission of IEEE 802.11 frame prior to the wake-up packet
We may discuss further to deal with this issue

## Slide 11: Reference
[1] IEEE 802.11-17/0575r1 “Spec framework”

## Slide 12: Straw poll 1
Do you agree with the following sentence?
  TGba should consider the inefficiency in case AP transmits wake-up frame to STA in awake state