## Slide 1: Some Results on Synchronization Performance
Date: 2017-07-10
Authors:

## Slide 2: Abstract
In [1] it is shown that the PER performance is improved if the bandwidth of the WUS as well as the channel selective filter is increased using a relatively long syncword
In this presentation we investigate how long syncword is needed for different coding schemes and also how this required length depends on the bandwidth of the WUS
It is found that for the same path loss, a system using a wider bandwidth may only require a syncword of half the length compared to a 13 sub-carrier system, leading to additional gain on top of what is already achieved by allowing for higher data rate

## Slide 3: Outline
Recap of link budget considerations
Motivation
Simulations
  Simulation set-up & performance metric
  Performance in AWGN
  Performance in Frequency selective channels
Conclusions
Straw polls

## Slide 4: Motivation
To obtain a spectrum efficient transmission, the length of the synchronization word should be as short as possible, still giving sufficient performance
Here we present simulation results for synchronization performance and relate this to the corresponding performance of the data presented in [1]
In particular, we discuss the gain in spectrum efficiency that can be achieved by using a large bandwidth of the channel in demanding channel conditions as proposed in [1]

## Slide 5: Model for receiver processing
ADC runs at 4x oversampling relative WUS symbol rate
Correlator (coeff. +-1) operating on signal with DC bias
Manchester coding used, so no need to estimate the decision threshold DC
CSF selected to signal BW + 500 kHz
ADC
Env. Det.
|
.
|
LPF
-
correlator
4
CSF

## Slide 6: Varying the signal bandwidth
The power of the WUS is boosted by allocating more sub-carriers to the WUS
The smallest BW corresponds to the 13 sub-carriers first proposed in [7]
4 MHz
8 MHz
16 MHz
Frequency

## Slide 7: Simulations – AWGN channel
Assuming that the PER target is 10%, it is reasonable to have a synchronization error target of 1%
In a similar way as for the data performance, the gain by reducing the bandwidth 2x is around 1 dB, effectively meaning a 2 dB gain in link budget for a 2x increase in signal bandwidth due to increased TX power

## Slide 8: Example 1 – AWGN - 13 sub-carriers
Synchronization error < 1% at a PER of 10% gives required syncwords lengths of 24,40, and 64 bits, respectively
Using 64 bits at all times would mean a waste of 160us, corresponding to 20 bits in a 125 kb/s packet

## Slide 9: Example 2 – AWGN – 52 sub-carriers
Synchronization error < 1% at a PER of 10% gives required syncwords lengths of 24,40, and 64 bits, respectively
The change in signal bandwidth does not change the relative performance of synchronization and data

## Slide 10: Simulations – TGn B/D channel

## Slide 11: Example 3 – PER = 10% Manchester coding 125 kb/s
Select the SNR such that PER ~ 10% for ideal sync
Change syncword length
Channels: AWGN, TGnB, and TGnD
Choice of syncword length 24 seems sufficient

## Slide 12: Example 4 – PER = 10% Manchester coding + convolutional coding
Select the SNR such that PER ~ 10% for ideal sync
Change syncword length
Channels: AWGN, TGnB, and TGnD
Choice of syncword length 40/48 seems sufficient

## Slide 13: Example 5 – PER = 10% Manchester + conv. + 2x rep coding
Select the SNR such that PER ~ 10% for ideal sync
Change syncword length
Channels: AWGN, TGnB, and TGnD
Choice of syncword length 64 seems sufficient

## Slide 14: Example 6 – Comparing bandwidths
As a benchmark, take 13 sub-carrier WUS received at SNR = -10 dB
For equivalent pathloss, the reiceved SNR in case of a 52 sub-carrier WUS would be -4 dB
Suppose the data part of the packet is 64 bits
For 13 sub-carriers, this means 62.5 kb/s and 40 bits syncword => 1.18ms
For 52 sub-carriers, we have 125 kb/s and 24 bits syncword = 0.61ms. The change in signal bandwidth does not change the relative performance of synchronization and data

## Slide 15: Additional benefits
The length of the sync word can be used for detecting the MCS

## Slide 16: Conclusions
Different syncword length can be used for different MCS
For less coding, shorter syncwords suffice
The length of the syncword is independent of the bandwidth used for the wake-up signal
The length of the syncword can be used to detect the MCS

## Slide 17: Straw Poll
Do you support to add to the SFD that the length of the syncword for the wake-up signal may be varied depending on data rate in the wake-up packet?
Y/N/A: 0/0/0

## Slide 18: Straw Poll
Do you support to add to the SFD that the bandwidth used for the syncword may be selected independently of the bandwidth used for the data part of the packet?
Y/N/A: 0/0/0

## Slide 19: References
L. Wilhelmsson et al. “Variable signal bandwidth of the wake-up signal for enhanced WUR performance”, IEEE 802.11-17/1017r0.
M. Park et al., “Low-power wake-up receiver (LP-WUR) for 802.11,” IEEE 802.11-15/1307r1
J. Liu et al., “On waking-up multiple WUR stations,” IEEE 802.11-17/0028r0