## Slide 1: mmWave Mesh Network Usage Model
Date: 2017-07-10
Authors:

## Slide 2: Abstract
This presentation describes a use case for a mmWave mesh network that can be applied in different deployment scenarios:
Broadband residential access (WTTB, WTTH)
Wi-Fi AP & Small cell backhaul
It is proposed to add a new usage model on mmWave Mesh network to the 802.11ay use case document.
WTTH: Wireless Ro The Home
WTTB: Wireless To The Building

## Slide 3: Introduction
mmWave Mesh networks exhibit a promising cost-efficient high-performance alternative and/or complement to conventional fixed access networks.
In comparison to usage model 8, focus is more on Mesh wireless backhaul and Fixed wireless access, beside Small cell & WiFi AP BH.
Adaptive PtMP approach and Mesh functionality required, as changing LOS conditions for single links can cause problems.
Mesh network architecture deployment is expected to lead to significant increase in operational efficiency and reliability.
Existing standards cover aspects of mmWave technology [1] and meshed wireless networks [2].
In order to cover mmWave Mesh networks, the 11ay use case document [3] has to be extended by a respective usage model.

## Slide 4: Service Provider Motivation for mmWave Mesh Networks
Conventional fiber access networks provide high performance and reliability but are very expensive and time consuming in their deployment.
mmWave Mesh networks have the potential to provide several advantages from provider perspective:
  Fast time-to-market through rollout speedup
  Aiming at high coverage and low upfront cost
  Synergy with other radio rollouts (e.g. SC, WLAN)
Besides that SPs are targeting to different aspects that can be also delivered by a mmWave Mesh Network:
  Adaptive topologies (mesh, tree, point-to-point etc.)
  Resilience and redundancy (e.g. for avoiding LoS link failures / outages)
  Steering of traffic and bandwidth/link utilization
It is assumed that a mmWave Mesh Network is able to cover typical customer bases of a few street cabinets (in terms of range, number of subscribers, and bandwidth).
  Little to no installation at customer site
  Less coordination with various building owners

## Slide 5: mmWave Mesh Network – Area View
Small cell
Wi-Fi AP
Fiber PoP (cabinet)
  WTTH
  WTTB
Small cell
  WTTB
  WTTH
Wi-Fi-AP
Alternative: Wireless inhouse
  WTTB
RGW
  Mesh Wireless Backhaul
  LOS 60 GHz narrow beam system
  Own management and control per mmWave mesh access area
  Route control protocol supports re-routing over radio links
  Auto-alignment installations via adaptive beamforming
  Redundancy of active equipment at “first” pole next to fiber PoP or via connections to 2 or more fiber PoPs
  Radio link degradation and outage recognition w/ failure localisation
Use case c) WiFi AP / SC
Focus on use case specific Mesh WBH requirements
  Mesh WBH
fiber
Provider
Network
mmWave AP
mmWave link
Fiber PoP (to Provider Network)
Use case a) WTTH
Use case b) WTTB

## Slide 6: mmWave Mesh Network Use Case Matrix
Street pole
a) WTTH
b) WTTB
Rooftop
House wall
      X
      X
      X
      X
Wireless AP + Repeater2)
Inhouse
Window antenna1)
Mesh Wireless BH
1) No additional building outside-wall antenna for WTTH
2) E.g. wireless AP in the floor plus repeater at home NT
c) Wi-Fi AP & Small Cell
mmWave Wireless Backhaul
      X
      X
a) Wireless To The Home (WTTH)
  A fixed-wireless access (FWA) scenario for residential access
  Each flat is equipped with a receive / transmit window antenna (sector)
b) Wireless To The Building (WTTB)
  A FWA scenario for residential access
  Each building is equipped with a receive / transmit outdoor-wall antenna (sector)
  The in-building distribution is achieved by an in-building wireless or fixed network
c) WiFi AP / Small Cell Backhaul
  A nomadic and mobile usage scenario for Wi-Fi or 5G services
  Each user equipment / device represents an end node

## Slide 7: Distance Distribution – Operator Example for mmWave Mesh Networks
Dense urban area
  Purpose and methodology
  Provide broadband coverage for dense urban, urban, rural service areas in a timely and cost efficient way
  Exemplary assessment: Dense urban area
Basis: Behrens, C.; Lange, C.; Gladisch, A.: Challenges for Optical Wireless: An Operator’s Perspective. In: Optical Fiber Communications Conference (OFC). Workshop: Optical Wireless – Can it Become a Gigabit Wireless Alternative? — Capabilities, Opportunities, Challenges and Threats, Los Angeles (CA, USA), March 19–23, 2017
  Result: Distance classes
  Street Furniture to Building
  Standard distance < 15 m
  Extended distance < 100 m
  Street Furniture to Street Furniture
    Standard distance < 60 m
    Extended distance 1 < 120 m
    Extended distance 2 < 300 m

## Slide 8: New Usage Model: mmWave Mesh Network
Fiber PoP
fiber
mmWave Mesh Network
b) WTTB
a) WTTH
c) Wi-Fi AP/ Small Cell
Provider Network
optical fiber termination node
mmWave Distribution Node, one or more collocated mmWave sectors
mmWave sector
Legend:
fiber
Fiber PoP
Fiber PoP
Use cases:

## Slide 9: New Usage Model: mmWave Mesh Network
Environment:
Devices operate in outdoor environment with LOS under most conditions. For multiple hop wireless backhauling devices, distance per hop between the paired DNs is < 300 m (street-poles), < 1000 m (rooftop), and the distance between DNs and WTTH/B Home/Building APs is < 100 m.
Interference Conditions:
Interference from environmental conditions or other mmWave operations in the same area.
Obstructions of the LOS and beam un-alignments.
Use Case:
The mmWave WTTH/B DNs, which offer FTTH-like broadband access for residential customers as well as Small cells and WiFi-APs (e.g. 802.11ac), which offer mobile and nomadic services, are connected to a mmWave mesh backhaul network.
The 11ay mmWave Mesh backhaul network connects by optical fiber to 1 or more fiber-PoPs towards the Telco / Service Provider network.
Redundancy of active radio equipment via Mesh topology and redundant central WBH DN at “first” pole near the fiber-PoP (no Single-Point-of-Failure)
The Internet connectivity QoS/QoE and latency requirements are met with the user’s applications.
Pre-Conditions:
A number of 11ay DNs forms a wireless outdoor mmWave Mesh network over multiple hops in order to reach coverage. In addition to the Mesh backhaul, also a point-to-multipoint mmWave access network is build to serve homes, buildings, WiFi-AP and small cells.
Application – WTTH Access:
The mmWave Mesh backhaul will be used for backhauling of WTTH DNs, which are placed at street poles (e.g. lamppost). The WTTH DNs serve the individual homes/ flats via a window AP at client side instead of deploying expensive fiber networks in the building branch and inhouse. The WTTH radio links work on the same or optional on different mmWave frequency than the mmWave Mesh backhaul links.
Application – WTTB Access:
The mmWave Mesh backhaul will be used for backhauling of WTTB DNs, which are placed at street poles (e.g. lamppost) or at walls or rooftops. The WTTB links work on the same mmWave frequency as the mmWave Mesh backhaul links. If street poles are used, the WTTB DNs serve the buildings via an outdoor-wall AP. In case of Wall-to-Wall or Roof-to-Roof backhaul, it serves at the same time as mmWave building access network without usage of additional street poles. The WTTB scenario requires an additional wireless or fixed inhouse network to serve the individual flats.
Application – WiFi-AP & Small cell Backhaul:
The mmWave Mesh backhaul will be used for backhauling of Small Cells and Wi-Fi APs, which are e.g. placed at street poles. Traffic of mobile and nomadic services will be aggregated and carried towards the mobile core. The sub-6 GHz NLOS operation of the Small Cells and Wi-Fi APs imposes less challenges compared to WTTH/B to reach inhouse (mobile) users, however does not reach the capacity level of the WTTH/B solutions.

## Slide 10: New Usage Model: Operational Requirements
Redundancy will be achieved via the Mesh topology
Single-Points-of-Failure have to be avoided, either by redundant active equipment at the “first” pole next to the fiber-PoP or alternative via connection of the Mesh network to 2 or more fiber-PoPs
The 11ay Mesh network connects by optical fiber towards the Telco / Service Provider network.
The mmWave Mesh network will be formed by a number of 11ay outdoor DNs, which are used for backhauling of the proposed applications.
In addition to the Mesh backhaul, also a PtMP mmWave access network is build to serve the homes/buildings.
The mmWave Mesh network need to support a transmission over multiple hops in order to reach area coverage.
Distance per hop between paired DNs is up to 300 m and distance between DN sites and WTTH/B Home/Building APs is up to 100 m.
The number of hops in a daisy-chain is limited by area topology constraints, resulting in < 5 hops typically.
The system have the capability to support up to 15 hops to meet region specific requirements.
The mmWave DNs have to operate in outdoor environments with LOS under most conditions, taking into account potential constraints.
  Interference from environmental conditions or other mmWave operations in the same area
  Obstructions of the LOS and beam un-alignments.
  The network has to support different DN placement options such as street poles (e.g. lamppost), house-walls and rooftops.
Requirements (operator example) | mmWave Mesh Wireless Backhaul | mmWave Home/ Building Access
# of hops (outdoor)* | < 5 (typically) < 15 (system capability) | 1
LOS distance / link | < 300 m (street-poles) < 1000 m (rooftops) | < 100 m
# of DN | < 80 / km² | home/building density
Topology support | Mesh, PtMP, Daisy chain | PtP, PtMP
Data Rate (DL sustainable) | > 4 Gbps / DN site | > 1 Gbps / Home AP > 2 Gbps / Building AP
Antenna features | Beam-forming/tracking; Auto-alignment | 
Latency (RTT) (e-t-e mmWave) | < 15 ms (WTTH/B, WiFi AP BH) < 5 ms (5G Small cell BH) | 
QoS, Security, Sync. | QoS/QoE, Security C/I and Sync. support | 
Availability of sust. data rate | No guarantees in an unlicensed environment. > 99% should be aimed (e-t-e mmWave) | 
‘ # of hops depends on latency requirements

## Slide 11: Proposed changes to 11ay use case document [3]
The authors of this presentation request the TGay to agree on the sketched use case “mmWave mesh network” as a valid use case for 802.11ay that should be added to the 11ay use cases.
The authors of this presentation propose to add a corresponding use case description (slides 8-10) to the 802.11ay use case document IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases” [3].

## Slide 12: Summary
Three use cases of mmWave mesh networks have been presented:
  mmWave-based broadband home access (WTTH)
  mmWave-based broadband building access (WTTB)
  Wi-Fi AP & Small Cell backhaul
A description of this use case should be added to the 802.11ay use case document IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases”[3].
802.11ay related requirements for the mmWave mesh network architecture will be derived for the above mentioned use case and presented to TGay.

## Slide 13: Straw Poll #1
Do you support the proposal to add the usage model “mmWave mesh network” described in this document (slides 8-10) to a revised version of document IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases”?
Yes:
No:
Abstain:

## Slide 14: Motion #1
Do you agree on the proposal to add the usage model “mmWave mesh network” described in this document (slides 8-10) to a revised version of document IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases”?
Yes:
No:
Abstain:

## Slide 15: Straw Poll #2
Do you support the proposal to add the usage model “mmWave mesh network” (slides 8-10) as a separate usage model to document IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases” ?
Yes:
No:
Abstain:

## Slide 16: Motion #2
Do you agree on the proposal to add the usage model “mmWave mesh network” (slides 8-10) as a separate usage model to document IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases” ?
Yes:
No:
Abstain:

## Slide 17: References
[1] IEEE Standards Association: IEEE P802.11ad™, “Standard for Information Technology – Telecommunications and Information Exchange Between Systems – Local and Metropolitan Area 12 Networks – Specific Requirements – Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications – Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band”, 2012.
[2] IEEE Standards Association: IEEE Std 802.11s™, “IEEE Standard for Information Technology – Telecommunications and information exchange between systems – Local and metropolitan area networks – Specific requirements – Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications – Amendment 10: Mesh Networking”, 2011.
[3] IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases”
[4] Challenges for Optical Wireless: An Operator’s Perspective. Behrens, C.; Lange, C.; Gladisch, A.: Optical Fiber Communications Conference (OFC). Workshop: Optical Wireless – Can it Become a Gigabit Wireless Alternative? – Capabilities, Opportunities, Challenges and Threats, Los Angeles (CA, USA), March 19–23, 2017

## Slide 18: Abbreviations
PoP Point of Presence
PtMP Point to Multipoint
QoE Quality of Experience
QoS Quality of Service
RGW Residential Gateway
RTT Round Trip Time
SC Small Cell
WBH Wireless Backhaul
WLAN Wireless Local Area Network
WTTB Wireless to the Building
WTTH Wireless to the Home
AP Access Point
BH Backhaul
C/I Confidentiality/Integrity
DL Downlink
DN mmWave Distribution Node
EIRP Equivalent Isotropically Radiated Power
EMC Electromagnetic Compatibility
FTTH Fiber to the Home
FWA Fixed-Wireless Access
LOS Line of Sight
NLOS Non-Light of Sight
NT Network Termination

## Slide 19: Appendix
Use case details
  WTTH Access
  WTTB Access
  Wi-Fi AP & Small Cell BH

## Slide 20: Use Case: a) WTTH Access
Environment:
Devices operate in outdoor environment with LOS under most conditions. For multiple hop wireless backhauling devices, distance per hop between the paired DNs is < 300 m and distance between DNs and WTTH Home APs is < 100 m.
Interference Conditions:
- Potential interference from environmental factors and obstruction of the LOS, beam un-alignment.
- Street canyon effect
Use Case:
The mmWave WTTH DNs, which serve FTTH-like residential broadband access for individual homes, are connected to a mmWave mesh backhaul network.
The 11ay mmWave Mesh backhaul network connects by optical fiber to 1 or more fiber-PoPs towards the Telco / Service Provider network.
Redundancy of active radio equipment via Mesh topology and redundant central WBH DN at “first” pole near the fiber-PoP (no Single Point of Failure)
The Internet connectivity QoS/QoE and latency requirements are met with the user’s applications.
Pre-Conditions:
A number of 11ay DNs forms a wireless outdoor mmWave Mesh backhaul network. The transmissions in the mmWave Mesh network can be over multiple hops. In addition to the Mesh backhaul, also a point-to-multipoint mmWave home access network is build.
Application:
The mmWave Mesh backhaul will be used for backhauling of WTTH DNs, which are placed at street poles (e.g. lamppost). The WTTH DNs serve the individual homes/ flats via a window AP at client side instead of deploying expensive fiber networks in the building branch and inhouse. The WTTH radio links may work on same or optional on different mmWave frequency than the mmWave Mesh backhaul links.
Requirements (operator example) | mmWave Mesh Wireless Backhaul | mmWave Home Access
# of hops (outdoor) | < 5 | 1
LOS distance / link | < 300 m | < 100 m
# of DN | < 80 / km² | home density
Topology support | Mesh, PtMP, Daisy chain | PtP, PtMP
Data Rate (DL sust.) | > 4 Gbps / DN site | > 1 Gbps / Home AP
EIRP / EMC | < 40 dBm / Beam (FCC) | 
Antenna gain | Today’s regulation for PtP links (e.g. >35 dBi Germany)  Subject to change for PtMP (e.g. >20 - 22 dBi) | 
Antenna features | Beam-forming/tracking; Auto-alignment | 
Latency (RTT) | < 15 ms (e-t-e mmWave) | 
QoS, Security, Sync. | QoS/QoE, Security C/I and Sync. support | 
Availability of sust. data rate | No guarantees in an unlicensed environment. > 99% should be aimed (e-t-e mmWave) | 

## Slide 21: Use Case: b) WTTB Access
Environment:
Devices operate in outdoor environment with LOS under most conditions. For multiple hop wireless backhauling devices , distance per hop between the paired DNs is < 300 m (pole/wall) resp. < 1000 m (rooftop) and distance between DNs at pole and WTTB building APs is < 100 m.
Interference Conditions:
- Potential interference from environmental factors and obstruction of the LOS, beam un-alignment.
- Street canyon effect
Use Case:
The 11ay mmWave WTTB DNs, which serve FTTH-like residential broadband access for buildings, are connected to a mmWave Mesh backhaul network.
The 11ay mmWave Mesh backhaul network connects by optical fiber to 1 or more fiber-PoPs towards the Telco / Service Provider network.
Redundancy of active radio equipment via Mesh topology and redundant central WBH DN at “first” pole near the fiber-PoP (no Single Point of Failure)
The Internet connectivity QoS/QoE and latency requirements are met with the user’s applications.
Pre-Conditions:
A number of DNs forms a wireless outdoor mmWave Mesh backhaul and point-to-multipoint mmWave building access network. The transmissions in the mmWave Mesh network can be over multiple hops.
Application:
The mmWave Mesh backhaul will be used for backhauling of WTTB DNs, which are placed at street poles (e.g. lamppost) or at walls or at rooftops. The WTTB DNs work on the same mmWave frequency as the mmWave Mesh backhaul DNs. If street poles are used, the WTTB DNs serve the buildings via an outdoor-wall AP. In case of Wall-to-Wall or Roof-to-Roof mmWave Mesh backhaul, it serves at the same time as mmWave building access network without usage of additional street poles. The WTTB use case requires an additional wireless or fixed inhouse network, in contrast to WTTH, to serve the individual flats.
Requirements (operator example) | mmWave Mesh Wireless Backhaul |  |  | mmWave Building Access
 | Street Pole-to-Pole | Wall-to-Wall | Roof-to-Roof | Additional in case of WBH at street pole
# of hops (outdoor) | < 5 | < 5 | < 5 | 1
LOS distance / link | < 300 m | < 300m | < 1000 m | < 100 m
# of DN | < 80 / km² |  |  | building density
Topology support | Mesh, PtMP, Daisy chain |  |  | PtP, PtMP
Data Rate (DL sust.) | > 4 Gbps / DN site |  |  | >2 Gbps/ Building AP
EIRP / EMC | < 40 dBm / Beam (FCC) |  |  | 
Antenna gain | Today’s regulation for PtP links (e.g. >35 dBi Germany)  Subject to change for PtMP (e.g. >20 - 22 dBi) |  |  | 
Antenna features | Beam-forming/tracking; Auto-alignment |  |  | 
Latency (RTT) | < 15 ms (e-t-e mmWave) |  |  | 
QoS, Security, Sync. | QoS/QoE, Security C/I and Sync. support |  |  | 
Availability of sust. data rate | No guarantees in an unlicensed environment. > 99% should be aimed (e-t-e mmWave) |  |  | 

## Slide 22: Use Case: c) WiFi AP & Small Cell BH
Environment:
Devices operate in outdoor environment with LOS under most conditions. For multiple hop wireless backhauling devices , distance per hop between the paired DNs is < 300 m.
Interference Conditions:
- Potential interference from environmental factors and obstruction of the LOS, beam un-alignment.
- Street canyon effect
Use Case:
5G Small cells (mobile radio) and WiFi APs (e.g. 802.11ac) are backhauled via mmWave Mesh network.
The 5G Small cells and Wi-Fi APs offer mobile and nomadic services to the customers.
The 11ay mmWave Mesh backhaul network connects by optical fiber to 1 or more fiber-PoPs towards the Telco / Service Provider network.
Redundancy of active radio equipment via Mesh topology and redundant central WBH DN at “first” pole near the fiber-PoP (no Single Point of Failure)
The Internet connectivity QoS/QoE and latency requirements are met with the user’s applications.
Pre-Conditions:
A number of 11ay DNs forms a wireless outdoor mmWave Mesh backhaul network. The transmissions in the mmWave Mesh network can be over multiple hops.
Application:
The mmWave Mesh backhaul will be used for backhauling of Small Cells and Wi-Fi APs, which are e.g. placed at street poles. Traffic of mobile and nomadic services will be aggregated and carried towards the mobile core. The sub-6 GHz NLOS operation of the Small Cells and Wi-Fi APs imposes less challenges compared to WTTH/B to reach inhouse (mobile) users, however does not reach the capacity targets of the WTTH/B solutions.
Requirements (operator example) | mmWave Mesh Wireless Backhaul | 
 | for 5G Small cells | for Wi-Fi APs
# of hops (outdoor) | < 5 | < 5
LOS distance / link | < 300 m | < 300 m
# of DN | < 80 / km² | 
Topology support | Mesh, PtMP, Daisy chain | 
Data Rate (DL sust.) | > 1 Gbps / AP | > 300 Mbps / AP
EIRP / EMC | < 40 dBm / Beam (FCC) | 
Antenna gain | Today’s regulation for PtP links (e.g. >35 dBi Germany)  Subject to change for PtMP (e.g. >20 - 22 dBi) | 
Antenna features | Beam-forming/tracking; Auto-alignment | 
Latency (RTT) | < 5 ms (e-t-e mmWave) | < 15 ms (e-t-e mmWave)
QoS, Security, Sync. | QoS/QoE, Security C/I and Sync. support | Best effort
Availability of sust. data rate | No guarantees in an unlicensed environment. > 99% should be aimed (e-t-e mmWave) |