## Slide 1: mmWave Distribution Network Usage Model
Date: 2017-07-11
Authors:

## Slide 2: Abstract
This presentation describes a use case for a mmWave distribution network that can be applied in different deployment scenarios:
Broadband residential access (WTTB, WTTH)
Wi-Fi AP & Small cell backhaul
It is proposed to add a usage model on mmWave Distribution network to the 802.11ay use case document.
WTTH: Wireless Ro The Home
WTTB: Wireless To The Building

## Slide 3: Introduction
mmWave Distribution Networks exhibit a promising cost-efficient high-performance alternative and/or complement to conventional fixed access networks.
In comparison to usage model 8, the extended scope is on wireless distribution networks and fixed wireless access, besides Small cell & WiFi AP BH.
Adaptive PtMP approach and mesh functionality required, as changing LOS conditions for single links can cause problems.
Mesh based architecture deployment is expected to lead to significant increase in operational efficiency and reliability.
Existing standards cover aspects of mmWave technology [1] and meshed wireless networks [2].
In order to cover mmWave Distribution Networks, the 11ay use case document [3] has to be extended by a respective usage model.

## Slide 4: Service Provider Motivation for mmWave Distribution Networks
Conventional fiber access networks provide high performance and reliability but are very expensive and time consuming in their deployment.
mmWave Distribution Networks have the potential to provide several advantages from provider perspective:
  Fast time-to-market through rollout speedup
  Aiming at high coverage and low upfront cost
  Synergy with other radio rollouts (e.g. SC, WLAN)
Besides that SPs are targeting to different aspects that can be also delivered by a mmWave Distribution Network:
  Adaptive topologies (mesh, tree, point-to-point etc.)
  Resilience and redundancy (e.g. for avoiding LoS link failures / outages)
  Steering of traffic and bandwidth/link utilization
It is assumed that a mmWave Distribution Network is able to cover typical customer bases of a few street cabinets (in terms of range, number of subscribers, and bandwidth).
  Little to no installation at customer site
  Less coordination with various building owners

## Slide 5: mmWave Distribution Network – Area View
Small cell
Wi-Fi AP
Fiber PoP (cabinet)
  WTTH
  WTTB
Small cell
  WTTB
  WTTH
Wi-Fi-AP
Alternative: Wireless inhouse
  WTTB
RGW
  mmWave Distribution Network
  LOS 60 GHz narrow beam system
  Own management and control per mmWave wireless access area
  Route control protocol supports re-routing over radio links
  Auto-alignment installations via adaptive beamforming
  Redundancy of active equipment at “first” pole next to fiber PoP or via connections to 2 or more fiber PoPs
  Radio link degradation and outage recognition w/ failure localisation
Use case c) WiFi AP / SC
fiber
Provider
Network
mmWave AP
mmWave link
Fiber PoP (to Provider Network)
Use case a) WTTH
Use case b) WTTB

## Slide 6: mmWave Distribution Network Use Case Matrix
Street pole
a) WTTH
b) WTTB
Rooftop
House wall
      X
      X
      X
      X
Wireless AP + Repeater2)
Inhouse
Window antenna1)
Deployment Scenario
1) No additional building outside-wall antenna for WTTH
2) E.g. wireless AP in the floor plus repeater at home NT
c) Wi-Fi AP & Small Cell
mmWave Distribution Network
      X
      X
a) Wireless To The Home (WTTH)
  A fixed-wireless access (FWA) scenario for residential access
  Each flat is equipped with a receive / transmit window antenna (sector)
b) Wireless To The Building (WTTB)
  A FWA scenario for residential access
  Each building is equipped with a receive / transmit outdoor-wall antenna (sector)
  The in-building distribution is achieved by an in-building wireless or fixed network
c) WiFi AP / Small Cell Backhaul
  A nomadic and mobile usage scenario for Wi-Fi or 5G services
  Each user equipment / device represents an end node

## Slide 7: Distance Distribution – Operator Example for mmWave Distribution Networks
Dense urban area
  Purpose and methodology
  Provide broadband coverage for dense urban, urban, rural service areas in a timely and cost efficient way
  Exemplary assessment: Dense urban area
Basis: Behrens, C.; Lange, C.; Gladisch, A.: Challenges for Optical Wireless: An Operator’s Perspective. In: Optical Fiber Communications Conference (OFC). Workshop: Optical Wireless – Can it Become a Gigabit Wireless Alternative? — Capabilities, Opportunities, Challenges and Threats, Los Angeles (CA, USA), March 19–23, 2017
  Result: Distance classes
  Street Furniture to Building
  Standard distance < 15 m
  Extended distance < 100 m
  Street Furniture to Street Furniture
    Standard distance < 60 m
    Extended distance 1 < 120 m
    Extended distance 2 < 300 m

## Slide 8: Usage Model: mmWave Distribution Network
Fiber PoP
fiber
mmWave Distribution Network
b) WTTB
a) WTTH
c) Wi-Fi AP/ Small Cell
Provider Network
optical fiber termination node
mmWave Distribution Node, one or more collocated mmWave sectors
mmWave sector
Legend:
fiber
Fiber PoP
Fiber PoP
Use cases:

## Slide 9: Usage Model: mmWave Distribution Network
Environment:
Devices operate in outdoor environment with LOS under most conditions. For multiple hop wireless backhauling devices, distance per hop between the paired DNs is < 300 m (street-poles), < 1000 m (rooftop), and the distance between DNs and WTTH/B Home/Building APs is < 100 m.
Interference Conditions:
Interference from environmental conditions or other mmWave operations in the same area.
Obstructions of the LOS and beam un-alignments.
Use Case:
The mmWave WTTH/B DNs, which offer FTTH-like broadband access for residential customers as well as Small cells and WiFi-APs (e.g. 802.11ac), which offer mobile and nomadic services, are connected to a mmWave distribution network.
The 11ay mmWave distribution network connects by optical fiber to 1 or more fiber-PoPs towards the Telco / Service Provider network.
Redundancy of active radio equipment via mesh topology and redundant central WBH DN at “first” pole near the fiber-PoP (no Single-Point-of-Failure)
The Internet connectivity QoS/QoE and latency requirements are met with the user’s applications.
Pre-Conditions:
A number of 11ay DNs forms a wireless outdoor mmWave Distribution network over multiple hops in order to reach coverage. In addition to the wireless backhaul network, also a point-to-multipoint mmWave access network is build to serve homes, buildings, WiFi-AP and small cells.
Application – WTTH Access:
The mmWave distribution network will be used for backhauling of WTTH DNs, which are placed at street poles (e.g. lamppost). The WTTH DNs serve the individual homes/ flats via a window AP at client side instead of deploying expensive fiber networks in the building branch and inhouse. The WTTH radio links work on the same or optional on different mmWave frequency than the mmWave backhaul links.
Application – WTTB Access:
The mmWave distribution network will be used for backhauling of WTTB DNs, which are placed at street poles (e.g. lamppost) or at walls or rooftops. The WTTB links work on the same mmWave frequency as the mmWave backhaul links. If street poles are used, the WTTB DNs serve the buildings via an outdoor-wall AP. In case of Wall-to-Wall or Roof-to-Roof backhaul, it serves at the same time as mmWave building access network without usage of additional street poles. The WTTB scenario requires an additional wireless or fixed inhouse network to serve the individual flats.
Application – WiFi-AP & Small cell Backhaul:
The mmWave distribution network will be used for backhauling of Small Cells and Wi-Fi APs, which are e.g. placed at street poles. Traffic of mobile and nomadic services will be aggregated and carried towards the mobile core. The sub-6 GHz NLOS operation of the Small Cells and Wi-Fi APs imposes less challenges compared to WTTH/B to reach inhouse (mobile) users, however does not reach the capacity level of the WTTH/B solutions.

## Slide 10: Usage Model: Operational Requirements
Redundancy will be achieved via the mesh topology
Single-Points-of-Failure have to be avoided, either by redundant active equipment at the “first” pole next to the fiber-PoP or alternative via connection of the distribution network to 2 or more fiber-PoPs
The mmWave distribution network connects by optical fiber towards the Telco / Service Provider network.
The mmWave distribution network will be formed by a number of 11ay outdoor DNs, which are used for backhauling of the proposed applications.
In addition to the mmWave distribution network, also a PtMP mmWave access network is build to serve the homes/buildings.
The mmWave distribution network need to support a transmission over multiple hops in order to reach area coverage.
Distance per hop between paired DNs is up to 300 m and distance between DN sites and WTTH/B Home/Building APs is up to 100 m.
The number of hops in a daisy-chain is limited by area topology constraints, resulting in < 5 hops typically.
The system have the capability to support up to 15 hops to meet region specific requirements.
The mmWave DNs have to operate in outdoor environments with LOS under most conditions, taking into account potential constraints.
  Interference from environmental conditions or other mmWave operations in the same area
  Obstructions of the LOS and beam un-alignments.
  The network has to support different DN placement options such as street poles (e.g. lamppost), house-walls and rooftops.
Requirements (operator example) | mmWave Distribution Network | mmWave Home/ Building Access
# of hops (outdoor)* | < 5 (typically) < 15 (system capability) | 1
LOS distance / link | < 300 m (street-poles) < 1000 m (rooftops) | < 100 m
# of DN | < 80 / km² | home/building density
Topology support | Mesh, PtMP, Daisy chain | PtP, PtMP
Data Rate (DL sustainable) | > 4 Gbps / DN site | > 1 Gbps / Home AP > 2 Gbps / Building AP
Antenna features | Beam-forming/tracking; Auto-alignment | 
Latency (RTT) | < 15 ms (WTTH/B, WiFi AP BH) (e-t-e)** < 5 ms (5G Small cell BH) (e-t-e)** < 2 ms (per hop latency) | 
QoS, Security, Sync. | QoS/QoE, Security C/I and Sync. support | 
Availability of sust. data rate | No guarantees in an unlicensed environment. > 99% should be aimed (e-t-e mmWave) | 
‘ * of hops depends on latency requirements ** may differ based on operator deployments

## Slide 11: Proposed changes to 11ay use case document [3]
The authors of this presentation request TGay to agree on the sketched use cases for “mmWave distribution network” as a valid use case for 802.11ay that should be added to the 11ay use cases.
The authors of this presentation propose to add a corresponding usage model description (slides 8-10) to the 802.11ay use case document IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases” [3] by replacing existing Usage Model 8 which is considered as subset of mmWave distribution Usage Model.

## Slide 12: Summary
Proposed mmWave distribution network usage model covers three deployment scenarios:
  mmWave-based broadband home access (WTTH)
  mmWave-based broadband building access (WTTB)
  Wi-Fi AP & Small Cell backhaul
A description of the mmWave distribution network usage model should be added to the 802.11ay use case document IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases”[3].
802.11ay related requirements for the mmWave distribution network architecture will be derived for the above mentioned use case and presented to TGay.

## Slide 13: Straw Poll #1
Do you support replacing Usage Model 8 in document IEEE 802.11-15/0625r3 by the description of usage model “mmWave distribution network” (slides 8-10)?
Yes:
No:
Abstain:

## Slide 14: References
[1] IEEE Standards Association: IEEE P802.11ad™, “Standard for Information Technology – Telecommunications and Information Exchange Between Systems – Local and Metropolitan Area 12 Networks – Specific Requirements – Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications – Amendment 3: Enhancements for Very High Throughput in the 60 GHz Band”, 2012.
[2] IEEE Standards Association: IEEE Std 802.11s™, “IEEE Standard for Information Technology – Telecommunications and information exchange between systems – Local and metropolitan area networks – Specific requirements – Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specifications – Amendment 10: Mesh Networking”, 2011.
[3] IEEE 802.11-15/0625r3 “IEEE 802.11 TGay Use Cases”
[4] Challenges for Optical Wireless: An Operator’s Perspective. Behrens, C.; Lange, C.; Gladisch, A.: Optical Fiber Communications Conference (OFC). Workshop: Optical Wireless – Can it Become a Gigabit Wireless Alternative? – Capabilities, Opportunities, Challenges and Threats, Los Angeles (CA, USA), March 19–23, 2017

## Slide 15: Abbreviations
PoP Point of Presence
PtMP Point to Multipoint
QoE Quality of Experience
QoS Quality of Service
RGW Residential Gateway
RTT Round Trip Time
SC Small Cell
WBH Wireless Backhaul
WLAN Wireless Local Area Network
WTTB Wireless to the Building
WTTH Wireless to the Home
AP Access Point
BH Backhaul
C/I Confidentiality/Integrity
DL Downlink
DN mmWave Distribution Node
EIRP Equivalent Isotropically Radiated Power
EMC Electromagnetic Compatibility
FTTH Fiber to the Home
FWA Fixed-Wireless Access
LOS Line of Sight
NLOS Non-Light of Sight
NT Network Termination