## Slide 1: Usage of Doppler Bit in 11ax
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com

## Slide 2: Time-varying Channels and Mid-amble
Channel variation is one important feature of channel condition and should be feedback to assist the transmitter for following transmissions.
Mid-amble is adopted in 11ax to combat time-varying channel conditions by enabling channel tracking [1-2].
  Mid-amble is used to re-estimate or tracking the time-varying channel
  Mid-amble appears after a fixed duration, for example, a fixed number of symbols.
    This fixed duration is named as the mid-amble duration, say M symbols.

## Slide 3: Dual use of Doppler bit
  When packet length is larger than the mid-amble duration, Doppler bit is used to indicate if there exist mid-ambles in the packet.
    The receiver can detect time-variation of channels based on the received packet and mid-ambles.
    Note a transmitter can transmit a packet with mid-amble without knowing the channel condition just like use of different GIs.
  When packet length is not larger than the mid-amble duration (N_SYM≤ M), then Doppler bit is used as an indication if channel is time varying. (The packet can not contain any mid-amble anyway.)
    Note in this scenario the receiver is not able to detect time-variation of channels since the received packet is short.
    In this scenario, it is important for the receiver to get the information of time-varying channel to help its following transmissions.
      For example, an AP received a PS-poll from a STA, knowing if the channel is time-varying can help AP to configure the following transmissions to the STA.

## Slide 4: Illustration of Dual use of Doppler bit
Preamble
M symbols
M symbols
Payload
Mid-ambles
Doppler bit set to 1
N_SYM <= M symbols
Preamble
Doppler bit set to 1
N_SYM > Mid-amble periodicity (M), Doppler bit set to 1 indicates mid-amble presents.
N_SYM <= Mid-amble periodicity (M), Doppler bit set to 1 indicates the channel Doppler is high.

## Slide 5: Straw poll #1
Do you agree the dual use of Doppler bit as followings?
  For HE PPDUs with N_SYM ≤ Midamble periodicity, Doppler subfield of HE-SIG-A field set to 1 indicates that the current channel between the transmitter and the recipient is with high Doppler.
  For HE PPDUs with N_SYM > Midamble periodicity, Doppler subfield of HE-SIG-A field set to 1 indicates that Midamble is present in the PPDU.
Jianhan Liu, Mediatek, et. al.

## Slide 6: References
[1] “802.11AX Midamble Design for Doppler”, IEEE 802.11-17/0734r1, Hongyuan Zhang, etc.
[2] “Thoughts on Doppler Design in 802.11ax”, IEEE 802.11-17/0773r2, Lochan Verma, etc.
Jianhan Liu, Mediatek, et. al.