## Slide 1: EDMG BlockAck Retransmission
Date: 2017-05-2
Authors:
Name | Affiliation | Address | Phone | email
Oren Kedem | Intel |  |  | oren.kedem@intel.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com
Solomon Trainin | Qualcomm |  |  | strainin@qti.qualcomm.com
Nir Paz | Intel |  |  | nir.paz@intel.com
Ran Mor | Intel |  |  | ran.mor@intel.com
Alon Pais | Intel |  |  | alon.pais@intel.com
Igor Brainman | Intel |  |  | igor.brainman@intel.com
Dror Markovich | Intel |  |  | dror.markovich@intel.com

## Slide 2
Purpose and definitions
Purpose relaxation to EDMG retransmission rules to allow more throughput and reduce device cost

## Slide 3
DMG retransmission rules
Below is DMG retransmission rules as indicated in REVmc
10.24.7.7 Originator’s behavior
An originator that is a DMG STA shall transmit MPDUs sent under a BA agreement such that:
  MPDUs that need to be retransmitted are transmitted first, in sequential order of sequence number, starting from the oldest MPDU that needs to be retransmitted
  MPDUs that are being transmitted for the first time are sent after any MPDUs that need to be retransmitted, in sequential order of sequence number, starting from the oldest MPDU that has not been transmitted
  MPDUs are transmitted with the Ack Policy subfield set to Block Ack if the A-MPDU that contains them is followed after SIFS or RIFS by another A-MPDU

## Slide 4
Problem Statement
MPDUs retransmission typically occur SIFS after BACK is received
Since device is not capable to retrieve all retransmitted MPDUs from host, common implementation is to store it in device memory.
To achieve high throughput, large memory is required. EDMG throughput is increased compared to DMG, hence higher memory size will be required. Large memory increase the device cost.
This limitation is only for DMG STA. HT/VHT STA doesn’t need to comply with the above rules. Receiver can handle the reordering without this limitation

## Slide 5
Suggested Improvement
Like HT/VHT STA, EDMG STA could transmit to another EDMG STA new transmitted MPDUs before retransmitted MPDUs while keeping the Window Size agreement
In case EDMG STA is originator that sent MPDUs to DMG Responder STA, it shall follow the DMG retransmission rules.

## Slide 6
Example1 – current behavior

## Slide 7
Example2 – Suggested improvement

## Slide 8: Impact on Receiver
DMG receiver should be ready for the worse case in which retransmitted MPDUs were dropped.
Hence there shouldn’t be functional impact on receiver capabilities.
In below example, the receiver capabilities in DMG/EDMG retransmission are the same
There might be additional latency of forwarding MPDU 4,5,6,7 until MPDU3 is received
DMG Retransmission
Suggested EDMG Retransmission

## Slide 9: Straw Poll
Do you agree with the following changes:
10.24.7.7 Originator’s behavior
Change the second to last paragraph as follows
An originator that is a DMG STA shall transmit MPDUs sent under a BA agreement such that:
  If the originator or the recipient are a non-EDMG STA:
    MPDUs that need to be retransmitted are transmitted first, in sequential order of sequence number, starting from the oldest MPDU that needs to be retransmitted
    MPDUs that are being transmitted for the first time are sent after any MPDUs that need to be retransmitted, in sequential order of sequence number, starting from the oldest MPDU that has not been transmitted
  MPDUs are transmitted with the Ack Policy subfield set to Block Ack if the A-MPDU that contains them is followed after SIFS or RIFS by another A-MPDU

## Slide 10
10.24.7.6.2 Operation for each received Data frame
2) Pass MSDUs or A-MSDUs up to the next MAC process if they are stored in the buffer in order of increasing value of the Sequence Number subfield starting with the MSDU or A-MSDU that has SN=WinStartB or if SN>WinStartB, the STA is a non-EDMG STA, and one of the following conditions is met:
  i) The MPDU is received as non-first frame in the A-MPDU; the bit at position SN=WinStartR – 1 is set to 1; and all delimiters between the received MPDU and the preceding MPDU (SN=WinStartR – 1) are valid.
  ii) The MPDU is received as first frame in the A-MPDU; the A-MPDU is received in SIFS or RIFS after an A-MPDU or in SIFS after transmission of a BlockAck frame; the bit at position SN=WinStartR – 1 is set to 1; and all delimiters after the MPDU(SN=WinStartR – 1) in the preceding A-MPDU are valid.
  iii) The MPDU is received in SIFS or RIFS after an A-MPDU or in SIFS after transmission of a BlockAck frame; the bit at position SN=WinStartR – 1 is set to 1; and all delimiters after the MPDU (SN=WinStartR – 1) in the preceding A-MPDU are valid.
  iv) The MPDU is received as first frame in the A-MPDU; the A-MPDU is received in SIFS or RIFS after an MPDU or in SIFS after transmission of an Ack frame; and the bit at position SN=WinStartR – 1 is set to 1.
  v) The MPDU is received in SIFS or RIFS after the preceding MPDU or in SIFS after transmission of an Ack frame; and the bit at position SN=WinStartR – 1 is set to 1. This process is continued sequentially until there is no buffered MSDU or A-MSDU for the next sequential value of the Sequence Number subfield

## Slide 11: BACKUP