## Slide 1: Overview of 3GPP SA Next Generation System Documents Related to Non-3GPP Access to the 5G Core Network
Date: 2017-07-05
Authors:

## Slide 2: Abstract
This document provides an overview of several 3GPP SA TSG Next Generation System documents:
Completed documents:
3GPP TR 23.799 “Study on Architecture for Next Generation System”
3GPP TR 33.899 “Study on the Security Aspects of the Next Generation System”
Documents in development:
3GPP TS 23.501 System Architecture for the 5G System (Stage 2), companion to TS 23.502
And
The 3GPP Study Item in progress: Access Traffic Steering, Switch, and Splitting support in the 5G system architecture (SP-170411)

## Slide 3: Contents
Completed documents:
  3GPP TR 23.799 “Study on Architecture for Next Generation System”
  3GPP TR 33.899 “Study on the Security Aspects of the Next Generation System”
Documents in development:
  3GPP TS 23.501 System Architecture for the 5G System (Stage 2), companion to TS 23.502
  Note: 3GPP TS 23.502 Procedures for the 5G System (Stage 2), companion to TS 23.501 and 3GPP TS 33.501 Security Architecture and Procedure for the 5G System currently contain minimal Non-3GPP access information.
3GPP Study Item in progress: Access Traffic Steering, Switch, and Splitting support in the 5G system architecture (SP-170411)

## Slide 4: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 1/14
Support the new RAT(s), the Evolved E-UTRA, and non-3GPP access types. GERAN and UTRAN are not supported:
  As part of non- 3GPP access types, WLAN access (including "untrusted WLAN" according to the meaning defined in pre Rel. 14 for the term "untrusted") and Fixed access shall be supported.
Support unified authentication framework for different access systems.
Support multiple simultaneous connections of an UE via multiple access technologies.
Support a separation of Control plane and User plane functions.
Support transmission of IP packets, non-IP PDUs and Ethernet frames. (assumes a p2p link).
Efficiently support different levels of UE mobility (including stationary UE)/service continuity.
Support services that have different latency requirements between the UE and the Data Network.
Minimize the signalling (and delay) required to start the traffic exchange between the UE and the Data Network
Architectural Overview (only WLAN related items included below) [1]:

## Slide 5: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 2/14
Efficient network support for a large number of UEs in periods without data traffic.
Support network sharing.
Support roaming:
Support broadcast services.
Minimize energy consumption in the overall network operation.
Support critical communications, including mission-critical communications.
Support regulatory requirements for Lawful Intercept.
Support a flexible information model with relationships between user related managed data, and with a level of abstraction sufficient to be independent of any specific protocols.
Support for location services as per the related service requirements and in alignment with NR RAN TR 38.913 [10].
Support regulatory requirements for Public Warning System (PWS), e.g. ETWS, CMAS, KPAS
Architectural Overview (only WLAN related items included below) [1] (cont.):

## Slide 6: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 3/14
Initial High Level Architectural View [1]:
Architectural Principles:
The UE may be attached to the network without having an established session for data transmission.
The number of reference points between the UE and the NextGen Core Network for the control plane over a single RAN should be minimized, independently of the functional composition of the control plane CN functionality.
NG2: RP CP between NG AN and NG Core, NG3: RP UP between NG AN and NG Core,
NG1: RP CP NG UE and NG Core, NG6 RP between NG Core and the data network.

## Slide 7: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 4/14
Support of network slicing
QoS framework
Mobility management framework
Session management
Void
Support for session and service continuity and efficient user plane path
Network function granularity and interactions between them
Next Generation core and access - functional division and interface
3GPP architecture impacts to support network capability exposure and context information awareness
Policy Framework
Charging
Security framework
Broadcast/Multicast Capabilities
Support for Off-Network Communication
NextGen core support for IMS
3GPP system aspects to support the connectivity of remote UEs via relay UEs
3GPP architecture impacts to support network discovery and
Interworking and Migration
Architecture impacts when using virtual environments
Traffic Steering, Switching and Splitting between 3GPP and non-3GPP Accesses
Minimal connectivity within extreme rural deployments
Support of "5G connectivity via satellite" use case
This Technical Report discusses 22 Key Issues [1]:

## Slide 8: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 5/14
Investigating:
How the NextGen Core network and the NextGen UE can support access traffic steering (as defined in clause 3.1) between 3GPP and non-3GPP accesses.
How the NextGen Core network and the NextGen UE can support access traffic switching (as defined in clause 3.1) between 3GPP and non-3GPP accesses. This includes the conditions that can trigger the switching of a data flow to a new access.
How and if the NextGen Core network and the NextGen UE can support access traffic splitting (as defined in clause 3.1) between 3GPP and non-3GPP accesses. This includes the conditions that can trigger the splitting of a data flow across multiple accesses.
How the access traffic steering, switching and splitting (ATSSS) can be taken into account by the charging framework (considered in Key Issue 11) in order e.g. to enable the network operator to differentiate charging for data traffic that is switched and/or split between 3GPP and non-3GPP accesses. It is clarified that this key issue will not address the charging framework but it will only consider what information needs to be provided to the charging framework in order to charge traffic that is switched and/or split between 3GPP and non-3GPP accesses.
Note:
Potential policies provided to the UE for access traffic steering, switching and splitting (ATSSS), if any, will be defined under the key issue on Policy Framework.
This key issue is restricted only to ATSSS procedures applied in the NextGen core network. Similar procedures that may be applied in the NextGen RAN are outside the scope of this key issue.
The procedures for access traffic steering, switching and splitting take place after the session management procedures are executed, i.e. after PDU sessions are established over 3GPP and non-3GPP accesses.
Key issue 20: Traffic Steering, Switching and Splitting between 3GPP and non-3GPP Accesses [1]

## Slide 9: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 6/14
Non-Roaming
Roaming
Solutions for Key Issue 20: 3GPP architecture impacts to support access traffic steering and switching (note: this solution does not address splitting aspects) [1]:

## Slide 10: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 7/14
New data flow by UE
Steering DL data flow by the network dual radio- capable UE
Solutions for Key Issue 20: 3GPP architecture impacts to support access traffic steering and switching (note: this solution does not address splitting aspects) [1]:

## Slide 11: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 8/14
Switching of an ongoing data flow by the UE
Solutions for Key Issue 20: 3GPP architecture impacts to support access traffic steering and switching (note: this solution does not address splitting aspects) [1]:

## Slide 12: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 9/14
Architecture
ATSSS (Access Traffic Steering, Switching and Splitting)
Solutions for Key Issue 20: Solution based on ATSSS Function [1]:

## Slide 13: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 10/14
High-level concept of operation
Solutions for Key Issue 20: Solution based on ATSSS Function [1]:

## Slide 14: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 11/14
Protocol Architecture
Solutions for Key Issue 20: Solution based on ATSSS Function [1]:

## Slide 15: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 12/14
Modes of SSF Operation (UE side)
SSF: Switching/ Splitting Function
Solutions for Key Issue 20: Solution based on ATSSS Function [1]:

## Slide 16: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 13/14
Switching the traffic of a TCP flow between 3GPP and WLAN access
Solutions for Key Issue 20: Solution based on ATSSS Function [1]:

## Slide 17: 3GPP TR 23.799 “Study on Architecture for Next Generation System” 14/14
Splitting the traffic of a TCP flow between 3GPP and WLAN access
Solutions for Key Issue 20: Solution based on ATSSS Function [1]:

## Slide 18: 3GPP TR 33.899 “Study on the Security Aspects of the Next Generation System”
#1.27: Authentication and Key Agreement procedure for untrusted non-3GPP Access [2]:
General architecture

## Slide 19: 3GPP TR 33.899 “Study on the Security Aspects of the Next Generation System”
#1.27: Authentication and Key Agreement procedure for untrusted non-3GPP Access [2]:
High-level Control Plane Procedure for Untrusted non-3GPP Access

## Slide 20: 3GPP TR 33.899 “Study on the Security Aspects of the Next Generation System”
#1.28: Authentication and Key agreement procedure for NextGen architecture with stand-alone non-3GPP access [2]:
High-level 3GPP EAP-AKA flow for Non-3GPP Access

## Slide 21: 3GPP TS 23.501 System Architecture for the 5G System (Stage 2)
Currently 23.501 supports [3]:
  Connectivity of the UE only via non-3GPP access networks, e.g. WLAN access.
  Non-3GPP access is standalone untrusted non-3GGP access
  A UE access the 5G Core Network supports NAS signaling using N1 reference point
  Non-3GPP access networks shall be connected via a Non-3GPP InterWorking Function (N3IWF).
  A UE shall establish an IPSec tunnel with the N3IWF, the UE shall be authenticated by and attached to the 5G Core Network during the IPSec tunnel establishment procedure.
  N1 NAS signaling over standalone non-3GPP accesses shall be protected with the same security mechanism applied for N1 over 3GPP access.

## Slide 22: 3GPP TS 23.501 System Architecture for the 5G System (Stage 2)
Non-roaming architecture for 5G Core Network with Non-3GPP access [3]:
AMF: Access and Mobility Management Function
SFM: Session Management Function
N3IWF: Non-3GPP InterWorking Function
UPF: User Plane Function

## Slide 23: 3GPP TS 23.501 System Architecture for the 5G System (Stage 2)
Roaming architecture for LBO for 5G Core Network with Non-3GPP access – N3IWF in the VPLMN [3]:

## Slide 24: 3GPP TS 23.501 System Architecture for the 5G System (Stage 2)
Home-routed Roaming architecture for 5G Core Network with Non-3GPP access – N3IWF in a different the VPLMN from the 3GPP access [3]:

## Slide 25: 3GPP Study Item in progress: Access Traffic Steering, Switch, and Splitting support in the 5G system architecture (SP-170411) [6]
Justification
“Today, non-3GPP access is a vital companion access infrastructure for mobile networks that can help mobile operators deal with the explosive rate of growth in network traffic. Non-3GPP access such as Wi-Fi can relieve the pressure on the mobile network and can offer fast indoor data connections.”
“Increasingly, many operators are seeking ways to balance data traffic between mobile networks and non-3GPP access in a way that is transparent to users and reduces mobile network congestion. This can be achieved by not only steering traffic from the mobile network onto non-3GPP access, but also to switch or split traffic in a managed way …”
“For UEs that can be simultaneously connected to both 3GPP access and non-3GPP access, the 5G system should be able to take advantage of these multiple accesses in a way that improves the user experience, optimizes the traffic distribution across various accesses, enables the provision of new high-data-rate services, etc. “
Note: Access Traffic Steering, Switching and Splitting is: ATSSS

## Slide 26: 3GPP Study Item in progress: Access Traffic Steering, Switch, and Splitting support in the 5G system architecture (SP-170411) [6] (cont.)
Objective
- “How the 5G Core network and the 5G UE can support multi-access traffic steering between 3GPP and non-3GPP accesses.”
- “How the 5G Core network and the 5G UE can support multi-access traffic switching between 3GPP and non-3GPP accesses. This includes the conditions that can trigger the switching of data traffic to a new access type.”
- “How the 5G Core network and the 5G UE can support multi-access traffic splitting between 3GPP and non-3GPP accesses. This includes the conditions that can trigger the splitting of data traffic across multiple accesses.”
“How the multi-access traffic steering, switching and splitting (ATSSS) can be taken into account by the charging framework in order e.g. to enable the network operator to differentiate charging for data traffic that is switched and/or split between 3GPP and non-3GPP accesses.”
“How the 5G core network can support multi-access PDU sessions, i.e. PDU sessions whose traffic can be sent over 3GPP access, or over NON-3GPP access, or both.”
Work Plan: Approved: June 2017, Target Completion: Sept 2018

## Slide 27: References
3GPP TR 23.799 “Study on Architecture for Next Generation System”
3GPP TR 33.899 “Study on the Security Aspects of the Next Generation System”
3GPP TS 23.501 System Architecture for the 5G System (Stage 2), companion to TS 23.502
3GPP TS 23.502 Procedures for the 5G System (Stage 2), companion to TS 23.501
3GPP TS 33.501 Security Architecture and Procedure for the 5G System
3GPP Work Item Description for: Study on Access Traffic Steering, Switch, and Splitting support in the 5G system architecture (SP-170411)