## Slide 1: Power Consumption Evaluation for A Few WUR MAC Procedures
Date: 2017-07-10
Authors:

## Slide 2
Abstract
In this contribution, we evaluate the power consumption for a few WUR MAC procedures using simulation results and discuss the benefits of purpose indication for overhead reduction and power saving for WUR devices.

## Slide 3: Introduction
STAs may be woken up by another STA for very different reasons:
  Individual (Re)Configuration/BSS-wide parameters changes
  UL and/or DL data transmissions
Optimization is possible if a STA is informed of the purpose of the wake up [1]
  Overhead reduction and power saving
We evaluate two potential wake up procedures for power consumptions with/without the STA being informed of the purpose of wake up
  Scenario 1: STA being woken up for (re)configuration: e.g.,
    STA woken up for WUR duty cycle renegotiation
    STA woken up for WUR channel configuration
  Scenario 2: STA being woken up for UL data transmission

## Slide 4: Purpose Indication Scenario (1)
Scenario 1: AP wakes a STA for (Re)configuration, e.g., WUR duty cycle renegotiation
  Without Purpose Indication in WUP, STA’s behavior may be :
    Receives WUP without purpose indication and wakes up
    Sends PS-Poll
    Receives Configuration request
    Sends Config preference; receives Config Confirm and sends ACK
    Returns to sleep
  With Purpose Indication in WUP, STA’s behavior may be optimized:
    Receives WUP with purpose indication and wakes up
    Sends Config Preference
    Receive Configuration Request
    Sends Config Confirm; receives ACK
    Returns to sleep

## Slide 5: Purpose Indication Scenario (2)
STA’s PCR on
STA’s PCR on
  With purpose indication in WUP, one frame can be reduced from the frame exchange; shortens awake time for STA
  Cost: a few (e.g., 2 or 3) bits in purpose indication in WUR packets

## Slide 6: Purpose Indication Scenario (3)
Scenario 2: AP wakes STAs for UL data transmission
  Without Purpose Indication in WUP, STA’s behavior may be:
    Receives a WUP without purpose indication and wakes up
    Sends PS-Poll
    Receives UL packet request/poll
    Sends UL packet; receives ACK
    And returns to sleep
  With Purpose Indication in WUP, STA’s behavior may be optimized:
    Receives a WUP with purpose indication and wakes up
    Sends UL packet
    Receives ACK
    And returns to sleep

## Slide 7: Purpose Indication Scenario (4)
STA’s PCR on
STA’s PCR on
  With purpose indication in WUP, two frames can be removed from the frame exchange; shortens awake time for STA
  Cost: A few (e.g., 2 or 3 bits) in purpose indication in WUR packet

## Slide 8: Analysis assumptions (1)
Usage Scenario 3 (Cattle farm) [5]:
  1 farmer (Mobile AP)
  50 cows (STAs)
  UL data only
  Packet rate in Scenario 2: packets being polled every [5:5:50]s
Power consumption evaluated at the STA side
  Scenario 1: Power consumption for one configuration exchange
  Scenario 2: Power consumption for one UL data exchange for 100s

## Slide 9: Analysis assumptions (2)
Parameters (WUR) | Values
P.Tx | 88 mW
P.Rx | 77 mW
P.Listen | 100 uw
Beacon Duration | 144 us
Beacon Interval | 10 s
WUR PHY rate | 250 kbps
WUR Packet size | 10 bytes
Parameters (PCR) | Values
P.Tx | 352 mW
P.Rx | 154 mW
P.Listen | 55 uw
P.DeepSleep | 3 uw
Beacon Frame size | 100 bytes
Beacon Interval | 100 ms
PCR PHY rate | 6.5 mbps
  Assumed packet sizes:
  UL Data packet size: 32 bytes
  PS-Poll: 20 bytes
  Data-poll: 20 bytes
  Config Req size: 30 bytes
  Config Pref size: 30 bytes
  Config Confirm size: 20 bytes
  ACK: 14 bytes

## Slide 10: Results for Scenario 1
no PI (uW) | 0.4072
with PI (uW) | 0.3264
Gain | 19.8%
Chart: Scenario 1
| no PI | with PI
 | 0.4072 | 0.3264
Power saving gain comparing to no purpose indication case

## Slide 11: Observation for Scenario 1
For each round of (Re)Configuration, ~20% power saving can be achieved by indicating in the wake up packets that a STA is being woken up for individual (Re)Configuration
More beneficial if (Re)Configuration takes place more frequently
  WUR duty cycle configuration:
    Not expected frequently
  WUR channel configuration may be needed more frequently:
    WUR channel being narrowband, more likely subject to deep fading
    Device movement expected: cows, goods, etc.
    (Re)Configuration frequency depends on coherent channel time
Achieved power saving may be significant over a long life time expected of WUR devices
  Sensors attached to cows, e.g.

## Slide 12: Results for Scenario 2
Packet Arrival duration | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
gain (%) | 39.4 | 39.4 | 39.4 | 39.4 | 39.4 | 39.4 | 39.4 | 39.4 | 39.4 | 39.4
Power saving gain comparing to no purpose indication case
Chart: Scenario 2
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
no PI | 6.3231 | 3.1614 | 1.8968 | 1.5806 | 1.2645 | 0.9484 | 0.6323 | 0.6323 | 0.6323 | 0.6322
with PI | 3.8315 | 1.9157 | 1.1494 | 0.9578 | 0.7663 | 0.5747 | 0.3831 | 0.3831 | 0.3831 | 0.3831

## Slide 13: Observation for Scenario 2
For each round of UL data transmission, ~40% power saving can be achieved by indicating in the wake up packets that a STA is being woken up for UL data transmission
Achieved power saving could be very significant over a long life time expected of WUR devices

## Slide 14: Conclusion
We evaluated two potential wake up procedures for their power consumptions and compared the results for the scenarios where the STA is/is not informed of the purpose of the wake up process
  Scenario 1: a STA is woken up for individual (Re)Configuration
  Scenario 2: a STA is woken up for UL data transmission
Simulation results show that significant power saving and overhead reduction can be achieved if the WUP indicates the purpose of the wake up process
    A WUP may need to use a few bits to indicate the purpose of the wake up process

## Slide 15
References
[1] 11-17/0387r6, Purpose Indication of WUR Packets, May 2017
[2] 11-17/0124r1, WUR MAC and Wakeup Frame, Jan. 2017
[3] 11-17/0034r0, WUR Use Cases and Requirements, Jan. 2017
[4] 11-16/1400r0, Power Efficient WUR AP Discovery, Nov. 2016
[5] 11-16/0029r4, WUR Usage Model Document, Jan. 2017

## Slide 16: SP 1
Do you agree to add to the 802.11ba SFD:
A WUP may carry the indication that the receiving STA is being woken up for UL data transmissions.

## Slide 17: SP 2
Do you agree to add to the 802.11ba SFD:
A WUP may carry the indication that the receiving STA is being woken up for individual (Re)Configuration.