## Slide 1: IEEE 802.1AS REV D5.0 Review Comments
Date: 2017-07-10
Authors:

## Slide 2: Motivation/Background
IEEE 802.1AS REV project includes use of IEEE 802.11-2016 Fine Timing Measurement as an additional 802.11 protocol to generate timestamps that 802.1AS would use for clock synchronization
IEEE 802.1AS REV project includes use of IEEE 802.11ak General Links for interfacing 802.11 MAC SAP to IEEE 802.1AC
802.1AS Rev D5.0 WG Ballot is currently open and closes July 13th, 2017.

## Slide 3: Summary of comments
 | Type | Count | 
1 | Editorial | 4 | 
2 | Technical | 2 | Needs discussion with ARC (REJECT)
 |  | 8 | Needs discussion with 802.1AS
 |  | 1 | Needs discussion with 802.11md amd 802.11az
Notes:   Should the Capabilities bit(s) apply to all ranging protocols? Or should we allow for indications in the Beacon to indicate Initiator/Responder capabilities for each Ranging Protocol independently? What about Ranging Protocols that do not have a distinct Initiator/Responder?

## Slide 4: Comments that need discussion with 802.11 ARC
802.11 MAC interfacing with ISS without support for 802.11ak
Figures 7.8 and 8.2 in IEEE 802.1AS D5.0
Open Issues:
  Should 802.1AS over 802.11 require 802.11ak?
  If 802.11ak is required how would current implementations of 802.11 and 802.1AS-2011 be addressed?
ISS layer sits atop 802.11. Bridging of 802.11 to/from the ISS layer depends on if 802.11 supports 802.11ak or not. Hence these comments are Rejected.

## Slide 5: Comments that requires discussion in 802.11md and/or 802.11az
What is the “disconnect” between IEEE 802.11-2016 and IEEE 802.1AS REV D5.0?
  IEEE 802.1AS D5.0
    Use FTM with the following parameters
      ASAP=1
      Single Burst (Burst Exponent = 0)
      FTMs per Burst – infinite number of FTMs (not explicit in D5.0)
  IEEE 802.11-2016 Fine Timing Measurement
    Does not have a mechanism to indicate “infinite” for FTMs per Burst

## Slide 6: Requirements
Simple Change
Must not break existing IEEE 802.11-2016 implementations of Fine Timing Measurement

## Slide 7: Proposed Solution-A
Amend 802.1AS REV D5.0 to use multiple burst instead of single burst
  Each burst has up to 32 FTM frames
Issues
  Still does not allow for “infinite” number of FTM frames to be sent; as the maximum number of bursts is limited to 215
  May cause discontinuity in the flow of time information from the top of the network to the leaf
    This is because all burst excepting the first one needs to be started with a FTM Request frame from the Slave to the Master
    This discontinuity may not be an issue if the slave transmits the FTM Request to trigger a new burst in a timely manner

## Slide 8: Recap of Multiburst FTM Session

## Slide 9: Fine Timing Measurement Parameters Element
 | Category | Public Action | Trigger | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory)
Octets | 1 | 1 | 1 | variable | variable | 11
 | Status Indication | Value | Reserved | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16

## Slide 10: Burst Duration Field
Value | Represents
0-1 | Reserved
2 | 250 us
3 | 500 us
4 | 1 ms
5 | 2 ms
6 | 4 ms
7 | 8 ,ms
8 | 16 ms
9 | 32 ms
10 | 64 ms
11 | 128 ms
12-14 | Reserved
15 | No Preference
12 | forever
13-14 | Reserved
Initiator: Burst Duration field set to 15 (no preference) and FTMs per Burst set to 0 (no preference)
Responder: Burst Duration field set to 12 (forever) and FTMs per Burst set to 0 (infinite)

## Slide 11: Proposed Solution-B
Amend IEEE 802.11-2016 to allow for a new choice for the number of FTMs per Burst
  Use one of the reserved values from the possible values for Burst Duration (values 12-14 are reserved in IEEE 802.11-2016)
  Initiator sets FTMs per burst to 0 (indicating no preference) and sets Burst Exponent to 0 (Single Burst)
  Responder sets Burst Duration to 12 (indicating “Forever”) and sets Burst Exponent to 0 (Single Burst)
  Responder sets FTMs per Burst to 0 (currently disallowed in IEEE 802.11-2016) indicating “infinite” FTMs (new behavior)
How does one enable both Location Services and 802.1AS between two peers?
  Only one FTM Session can exist at any one time between two peers.

## Slide 12: Proposed Solution-C
Move to multiburst – supports up to 215 bursts. The FTM Session needs to be renegotiated and restarted after that for the next 215 bursts.
Set FTMs Per Burst to 1, 2 or 3
Allows for the Slave to go to sleep, move to another channel, etc., between bursts
If in the middle of the session, a need to start an FTM Session for non-802.1AS use arises, the current 802.1AS FTM Session can be terminated by sending an FTM frame with the Dialog Token set to 0 and restarted later at a later time with an FTM negotiation
See Slide #8 for the message flow
No changes needed in 802.11-2016

## Slide 13: FTM Session for Proposed Solution - D

## Slide 14: Proposed Solution-D
Use Single Burst ASAP=1 (unchanged from D5.0)
Set FTMs Per Burst to 1, 2 or 3
Allows for the Slave to go to sleep, move to another channel, etc., between bursts; Allows for co-existence of applications using FTM for Time Synchronization (802.1AS) and Location Services
The Slave renegotiates a new FTM Session after collecting a set of t1, t2, t3 and t4. The Slave and Master state machines restarts as a result. t1 and t2 are zero when the first FTM frame is received with an FTM Session
  One could envisage running TM in this mode as well (each pair of TM frame exchange will reset the Master and Slave state machines)
See Slide #13 for the message flow
No changes needed in 802.11-2016

## Slide 15: Proposal-E
Move to multiburst – Define a mechanism to indicate “infinite” bursts in the FTM Parameters element (use Reserved bit-7?)
Set FTMs Per Burst to 1, 2 or 3
Allows for the Slave to go to sleep, move to another channel, etc., between bursts
If in the middle of the session, a need to start an FTM Session for non-802.1AS use arises, the current 802.1AS FTM Session can be terminated by sending an FTM frame with the Dialog Token set to 0 and restarted later at a later time with an FTM negotiation
See Slide #8 for the message flow
IEEE 802.11-2016 needs to be amended to include a definition for “infinite” bursts

## Slide 16: Comments to discuss with 802.1AS
Mandatory and optional support for Timing Measurement and Fine Timing Measurement protocols in Bridges and end-points
  Timing Measurement should be mandated to ensure interoperability
Some sub-sections of 802.1AS REV D5.0 need to be updated to address support for Fine Timing Measurement
Determination of asCapable
Fallback to Timing Measurement if FTM negotiation fails