## Slide 1: Resource Negotiation for Unassociated STAs in SU Request and Response in MU Operation
Date: 2017-05-08
Authors:
Name | Affiliation | Address | Phone | Email
Chao-Chun Wang | MediaTek Inc |  |  | Chao-chun.wang@mediatek.com
James Yee | MediaTek Inc |  |  | James.yee@mediatek.com
Yongho Soek | MediaTek Inc. |  |  | Yongho.seok@mediatek.com
Chao-Chun Wang (MediaTek Inc)

## Slide 2: Background
0805r1 specifies the SU – SU negotiation procedure in 11az
  Frame exchange sequence is the same as REVmc:
  FTM Request and Response frame types and formats needs to be updated, for example the response frame for unassociated STAs carry an ID (Ranging, Pre) and the NGP IE
Resource negotiation for unassociated STAs in MU Operation is still Undecided.
  Unassociated STAs send request in SU mode and AP returns responses in MU mode
  Unassociated STAs send request in MU mode and AP returns responses in MU mode
The contribution focus on the whether 11az shall support
  Unassociated STAs send request in SU mode and AP returns responses in MU mode

## Slide 3: Recap
(SU-MU) An STA sends FTM request in SU mode and receive FTM response (in SU PPDU format) for MU operation
Do we need all protocol details before a decision can be made?

## Slide 4: An Enterprise Locatioing Scenario
An STA enters a large meeting venue/office space and moving/pacing through the area
  The STA associated with one ranging AP
  The SAT does not associated with any ranging APs
The STA finds its location with first set of three or more APs
The STA continues its movement and exiting the coverage area of one or more APs of the first set of APs and enters the coverage area of new APs
The STA repeating the locationing operation in a constant interval to maintain its location information.

## Slide 5: An Locationing STA’s behavior
An STA enters the coverage of three or more APs
Case 1 - An STA sends ranging (FTM) request without listening to beacons. The STA has no idea about APs capability.
  The SAT does not associated with any ranging APs
Case 1b - An STA sends ranging (FTM) request without listening to beacons but STA knows about the AP’s ranging capabilities using mechanisms like Neighbor Report
  The STA associated with one ranging AP
  The STA receives neighboring ranging APs’ information via some means
Case 2 - An STA sends ranging (FTM) request after receiving beacons from three or more APs. The STA knows about APs capability.
  How to guarantee that all STAs will behave as same.
Others ?

## Slide 6: Issues need to be addressed
An STA sends FTM request in SU mode and receives FTM response (in SU PPDU format) for MU operation
  Does FTM Request has a field indicating the preference by the STA as to how it wants to receive FTM Response?
  The MU response frame (in SU PPDU) has a pre-defined/announced unique AID/multicast address to indicate that it is a FTM response frame
    An STA is expected to read all fields of the response frame with RA set to a pre-defined/announced multicast Address,
    The MU response frame (in SU PPDU) carries FTM parameters for every STAs including the Ranging ID assignment.
    The succeeding measurement operations operate in MU mode

## Slide 7: More issues
Power Consumption: The STA that has sent an SU request will be required to process all the frames or a limited number of frames to identified the response frame addressing all STAs send SU request
Waiting time from transmitting FTM Request to Receiving FTM Response: Revmc has this value at 10msec
  Revmc has a value defined to allow for STAs to save power
  APs take time to process FTM Requests and allowing for a large number of requests can increase the waiting time for FTM Response(s) -> tradeoff to be addressed
Using frames defined in 11ax or defining new frames to allow for 11az support

## Slide 8: Straw Poll 1
11az

## Slide 9: Background

## Slide 10: Background
Recap
  17/0463r1 discussed all possible mode of resource negation for unassociated STAs
    SU – MU
      Y: 6 N: 0 A: 16
    MU – MU (mode 1)
      Y: 5 N: 1 A: 18
    MU – MU (mode 2)
      Y: 6 N: 0 A: 16
    MU - MU (mode 2)
      Note: AP do explicitly ACK the FTM request frames. The ACK frame will carry ranging ID assignment for multiple requesters.
      Y: 1 N: 5 A: 17
The presentation is to clarify the SU-SU mode requirement

## Slide 11: Mode of Operations - SU
Motion
  Move to adopt the following text to the SFD under the section 3.2 and grant the editorial license to the SFD editor.
  The SU – SU negotiation procedure in 11az shall have the following properities
    Frame exchange sequence is the same as REVmc:
    FTM Request and Response frame types and formats needs to be updated, for example the response frame for unassociated STAs carry an ID (Ranging, Pre) and the NGP IE.
  Mover : Chao-Chun
  Seconder : Edward AU
  Results: Y 16 N 0 Abs 0