## Slide 1: Wakeup Frame Format
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Recap: Wakeup Frame Recap[2][3]
12-bit BSS color is long enough to avoid color collision.
AID can indicate broadcast/multicast/unicast receivers.
  AID may not needed for broadcast announcement, e.g. if multiple BSSID is not supported
Payload of Wakeup frame may not be needed to decrease WUR frame overhead, or Wakeup frame can have different length to decrease WUR frame overhead
Type combined AID can indicate different type of wakeup signals
  Unicast data/management frame wakeup,
  Broadcast data frame wakeup,
  Broadcast management frame wakeup or management info announcement to announce new BSS operation parameters, e.g.
    new BSS operation parameter announcement, BSS operation channel, TSF time sync,
    BSS recovery announcement,
    Beacon announcement,
Type
BSS Color
AID
FCS
Bits:
3
12
11
4
TBD
Payload (Optional)

## Slide 3: Recap: Wakeup Frame Recap[3][4]
A group STAs can wake up together to receive group frames, receive DL MU PPDU.
Static groups (group ID, group member) which are similar to 11ac’s DL MU group are maintained through Action frame.
  An AP can allocates some AIDs which are not used by associated STAs as group ID.
  One group ID can be allocated to a multicast MAC address.
Dynamic group (multicast group without group announcement/negotiation) are defined through different methods:
  Part of multicast MAC address is put in AID field of LP Wakeup frame.
  The hash result of multicast MAC address is put in AID field of LP Wakeup frame.
  AID bit map which is similar to AID bitmap of TIM element is in LP Wakeup frame and/or sequential multiple LP Wakeup frames with SIFS inter-frame space.
  AID set which includes multiple AIDs is in LP Wakeup frame and/or sequential multiple LP Wakeup frames with SIFS inter-frame space.
Static group is preferable: Group negotiation can be managed through TWT negotiation, Group ID can be acquired from group ID set, e.g. 0 to 255, partial TSF time of TWT start time, or partial multicast address.
Type
Group ID
FCS
Bits:
3
8
4
11
CBSSID

## Slide 4: Proposed WUR Wake Up Frame
The Wakeup frame include
  Type,
    unicast,
    broadcast for data, broadcast for new management info, these two may be separated to two types or may need subtype
    LP Sync.
    multicast
  Compressed BSS Identifier (CBSSID),
  Optional STA Identifier (AID, partial AID or LPSTAID which is continuously allocated to LP STA),
  Optional payload,
  FCS
The lengths of various fields just example.
Type
CBSSID
AID
FCS
Bits:
4
12
11
8
TBD
Payload (Optional)
Unicast
Type
CBSSID
FCS
Bits:
4
12
8
TBD
Payload (Optional)
Broadcast
Type
Group ID
FCS
Bits:
3
8
4
11
CBSSID
Group

## Slide 5: Frame Length of LP Wakeup Frame
LP Wakeup frame length can be identified by Type field.
  No additional length field is needed in LP PPDU PHY header or LP Wakeup frame,
LP Wakeup frame Length (Type) can be either LP PHY header or MAC header
Type
CBSSID
AID/GroupID (optional)
FCS
Bits:
3
12
11
8
TBD
Payload (Optional)

## Slide 6: Reference
[1] 11-16/1460R01 WUR MAC consideration
[2] 11-17/124R0 WUR MAC and Wakeup Frame
[3] 11-17/437R0 WUR MAC and Wakeup Frame
[4]11-17/1114