## Slide 1: Wakeup Frame Format
Date: 2017-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Recap: Wakeup Frame Recap[2][3]
12-bit BSS color is long enough to avoid color collision.
AID can indicate broadcast/multicast/unicast receivers.
  AID may not needed for broadcast announcement, e.g. if multiple BSSID is not supported
Payload of Wakeup frame may not be needed to decrease WUR frame overhead, or Wakeup frame can have different length to decrease WUR frame overhead
Type combined AID can indicate different type of wakeup signals
  Unicast data/management frame wakeup,
  Broadcast data frame wakeup,
  Broadcast management frame wakeup or management info announcement to announce new BSS operation parameters, e.g.
    new BSS operation parameter announcement, BSS operation channel, TSF time sync,
    BSS recovery announcement,
    Beacon announcement,
Type
BSS Color
AID
FCS
Bits:
3
12
11
4
TBD
Payload (Optional)
Type
BSS Color
AID
FCS
Bits:
4
12
11
4
4
BSI Token
=0
Partial MAC address (may be removed)

## Slide 3: Recap: Wakeup Frame Recap[3][4]
A group STAs can wake up together to receive group frames, receive DL MU PPDU.
Static groups (group ID, group member) which are similar to 11ac’s DL MU group are maintained through Action frame.
  An AP can allocates some AIDs which are not used by associated STAs as group ID.
  One group ID can be allocated to a multicast MAC address.
Dynamic group (multicast group without group announcement/negotiation) are defined through different methods:
  Part of multicast MAC address is put in AID field of LP Wakeup frame.
  The hash result of multicast MAC address is put in AID field of LP Wakeup frame.
  AID bit map which is similar to AID bitmap of TIM element is in LP Wakeup frame and/or sequential multiple LP Wakeup frames with SIFS inter-frame space.
  AID set which includes multiple AIDs is in LP Wakeup frame and/or sequential multiple LP Wakeup frames with SIFS inter-frame space.
Static group is preferable: Group negotiation can be managed through TWT negotiation, Group ID can be acquired from group ID set, e.g. 0 to 255, partial TSF time of TWT start time, or partial multicast address.
Type
Group ID
FCS
Bits:
3
8
4
11
CBSSID

## Slide 4: Proposed WUR Wake Up Frame
The Wakeup frame include
  Type,
    unicast, (broadcast may shared with unicast where specific LPSTAID is used to indicate broadcast)
    broadcast for data, broadcast for new management info, these two may be separated to two types or may need subtype
    LP Sync.
    Extension
  Compressed BSS Identifier (CBSSID),
  Optional STA Identifier (AID, partial AID or LPSTAID which is continuously allocated to LP STA),
  Optional payload,
  FCS
The lengths of various fields just example.
Type
CBSSID
LPSTAID
FCS
Bits:
2
12
10
8
Unicast
Type
CBSSID
FCS
Bits:
2
12
8
4
New BSS Info
Broadcast
Type
Partial TSF Time
FCS
Bits:
2
18
8
12
CBSSID
LP Sync
Type
Subtype
FCS
Bits:
2
4
8
12
CBSSID
Extension
payload
variable

## Slide 5: Frame Length of LP Wakeup Frame
LP Wakeup frame length can be identified by Type field with the exception of extension frame.
  No additional length field is needed in LP PPDU PHY header or LP Wakeup frame,
LP Wakeup frame Length (Type) can be either LP PHY header or MAC header

## Slide 6: Reference
[1] 11-16/1460R01 WUR MAC consideration
[2] 11-17/124R0 WUR MAC and Wakeup Frame
[3] 11-17/437R0 WUR MAC and Wakeup Frame
[4]11-17/1114

## Slide 7: Straw Poll 1
Do you support that the basic Wakeup frame include
  unicast,
  broadcast for data, broadcast for new management info, these two may be separated to two types or may need subtype
  LP Sync.

## Slide 8: Straw Poll 2
Do you support that the basic LP Wakeup frame length can be identified by Type field?

## Slide 9: Straw Poll 3
Do you support that the unicast LPW wakeup frame includes
  Type, CBSSID, LPSTAID, FCS
Type
CBSSID
LPSTAID
FCS
Bits:
2
12
10
8
Unicast

## Slide 10: Straw Poll 4
Do you support that the broadcast LPW wakeup frame at least includes
  Type, CBSSID, FCS
Type
CBSSID
FCS
Bits:
2
12
8
Broadcast
4
New BSS Info

## Slide 11: Straw Poll 5
Do you support that the Sync LPW wakeup frame at least includes
  Type, CBSSID, Partial TSF Time, FCS
Type
Partial TSF Time
FCS
Bits:
2
18
8
12
CBSSID
LP Sync