## Slide 1: Relay Threat Model for TGaz
Date: 2017-07-07
Authors:
Name | Affiliations | Address | Phone | email
Wei Wang | Google Inc. |  |  | weiwa@google.com
Roy Want | Google Inc. |  |  | roywant@google.com

## Slide 2: Abstract
The relay threat model occurs when two attackers collaborate to fake the distance between two stations, making them appear closer than they really are.
TGaz should be resilient to a relay attack in both associated and unassociated modes.

## Slide 3: Background
Wireless Relay Attacks have been used to defeat wireless car locks and pose a real threat to property
https://www.wired.com/2016/03/study-finds-24-car-models-open-unlocking-ignition-hack/
Bridging the gap
Attacker Box A
Near Owner
Attacker Box B
Near Car

## Slide 4: Mitigating Relay Attacks
Using range and location can be a good defense against relay attacks, assuming that the range/location of each party can be validated.

## Slide 5: Applications using RTT range for secure operation
Associated (or prior shared key)
Building door locks
Car door locks
Document access (e.g. only at work)
Cloud Service Access (e.g. only within home)
Unassociated
Proof of presence at a location
Proximity transfer of a redeemable wireless coupon
Proximity control of a public device with a wireless token (IOT)

## Slide 6: Ranging in 11mc
FTM_Req
FTM
FTM(t4- t1)
FTM RESPONDER
MOBILE
Ack
Ack
t1
t2
t3
t4
Ack
Distance (d) can be used to verify a condition:
d < [opening criterion],
But ONLY if you can trust it.

## Slide 7: Relay Attack #1: Faking a Range in 11mc
Attacker Box A
Attacker Box B
t1
t4
t2
t3
FTM(t4- t1)
FAKE (t4- t1)
FTM_Req
FTM_Req_Ack
Ack
FTM
t2 ‘
t3 ‘
t1 ‘
t4’
FTM RESPONDER
MOBILE

## Slide 8: Relay Attack #2: Faking a Range in 11mc
Attacker Box A
Attacker Box B
t1
t4
t2
t3
FTM(t4- t1)
FTM (t4- t1)
FTM_Req
FTM_Req_Ack
FAKE (Ack)
FTM
VALID_SIG
Ignore t4’
t1 ‘
t3 ‘
t2 ‘
FTM RESPONDER
MOBILE

## Slide 9
11az
Authentication can prevent a relay attack if…
each packet has an authenticated payload
there is a shared symmetric key
the stations are in associated mode

## Slide 10: What about the unassociated mode in 11az? There are not likely to be any shared keys Secure ranging in unassociated mode is important: Proof of presence at a location Proximity transfer of a redeemable wireless coupon Proximity control of a public device with a wireless token (IOT)

## Slide 11: Separation of Concerns
11az
11az
APP/OS
CLOUD SERVICE
CHECKS X1 = X2
APP/OS
DERIVED X1
DERIVED X2

## Slide 12: Relay Attack Defense without shared keys
t1
t4
t2
t3
FTM(t4- t1) + Nonce-AB
FTM + Nonce-A
Ack + Nonce-B
Verify AB + (t4-t1) at
APP Level
Verify AB + (t4-t1) at
APP Level
MOBILE
FTM RESPONDER

## Slide 13: Possible relay solution for unassociated 11az
Attacker Box A
Attacker Box B
t1
t4
MOBILE
t2
t3
FTM(t4- t1) + Nonce-AX
FTM (t4- t1) + Nonce-AB
FTM_Req
FTM + Nonce-A
Ack + Nonce-B
t1’
t4’
t3’ generated
t2’
FTM_Req_Ack
Ack + Nonce-X
Verify
AB + (t4-t1) at
APP Level
FTM + Nonce-A
Verify
AB + (t4-t1) at
APP Level
FTM RESPONDER

## Slide 14: Considerations
For authenticated ranging (associated) 11az will likely need a nonce in both FTM and Ack messages to validate range.
Both end-STAs already have (t4-t1)
An unassociated mode, that protects against relay attacks could give the App layer access to the nonces and (t4-t1) parameters.
The App is then responsible for validating the parameters

## Slide 15: Straw Poll
TGaz should include a mechanism to defend against relay ranging attacks between pairs of both associated and unassociated stations
Y: N: A:

## Slide 16: References
Radio attack lets hackers steal 24 different car models
https://www.wired.com/2016/03/study-finds-24-car-models-open-unlocking-ignition-hack/