## Slide 1: CP-replay Threat Model for 11az
Date: 2017-07-11
Authors:

## Slide 2: Abstract
11az FRD [1] describes Type A and Type B adversaries that are characterized according to attacker’s response time.
  Adversary goal: to spoof the range of STA.
  Type A: 1msec response time.
  Type B: 1usec response time.
  A few security threat models are listed in [2].
We present another threat model in this submission.
  CP-replay attack: can be viewed as a variety of late-commit attack [3].
  Attacker exploits the repetition between CP and the latter part of waveform.
  Attacker late commits to transmit the observed CP.
  Can be realized by a “Type B adversary”.

## Slide 3
CP-Replay Attack (1)
For general waveforms without repetition replay/relay attack may not apply because:
  EM waves propagate at the speed of light.
  Triangle inequality: Replayed/relayed signal from attacker cannot arrive earlier than authentic signal.
OFDM with cyclic prefix (CP)
  Repetition of CP provides an opportunity for attacker to create paths that can arrive earlier than authentic ones.

## Slide 4
CP-Replay Attack (2)
Method of attack
  Acquire OFDM symbol timing information about the waveform for channel measurement.
    11REVmc: Legacy preamble serves for this purpose.
  Learn (fully or partially) the waveform by observing the full or partial CP.
    Minimally the part corresponding to CP can be predicted.
  Transmit the waveform with timing advance during its repetition.
    Adjust Tx power to fake an earlier path …
    Significant to be counted as an arrival.
    Insignificant to affect demodulation due to bad channel estimate.

## Slide 5
CP-Replay Attack (3)
Example 1
  The whole waveform can be derived from (partial) CP.
Example 2
  The waveform is composed by a random sequence, only CP repetition is observable.

## Slide 6
CP-Replay Attack (4)
Highly detrimental to proximity-based use cases.
  E.g., auto unlock.
Feasibility analysis
  Attacker setup.
    Can use a commercial SDR (software-defined radio) equipment, e.g., FPGA or DSP based.
  Knowledge required.
    Preamble structure of 802.11 packets.
    Symbol timing acquisition.
    Timing advance and Tx power for replayed waveform.

## Slide 7
CP-Replay Attack (5)
Fake path: Paths appeared at Rx side due to attacker.
Target fake path: The expected fake path by attacker.
  Tx signal from attacker does not obey CP structure.
  Rx side assumes whole OFDM symbol (w/ CP).
  Sidelobe fake paths are unavoidable.
Assumption:
20 MHz, CP = 16, NFFT = 64.
Nyquist sampling rate.
Delay of fake path is an integer multiple of sampling periods.

## Slide 8
CP-Replay Attack (6)
Metric for effectiveness of creating target fake path:
Additional SINR degradation for data decoding due to sidelobe fake paths.
  Assume interference dominates thermal noise.
  Directly use channel estimated in frequency, no further processing for noise reduction:
  where Pi denotes the power of the i-th fake path.
  Fake paths outside GI window are zeroed out for noise reduction:

## Slide 9
CP-Replay Attack (7)
PHY types | CP duration (us) | Useful symbol duration (us) | Nyquist sampling period* (ns)
non-HT (11a/g) | 1.6 | 3.2 | 50
HT-mixed (11n) | 0.8 | 3.2 | 50
VHT (11ac) | 0.8/0.4 | 3.2 | 50
HE (11ax) | 0.8/1.6/3.2 | 3.2/6.4/12.8 | 50
DMG (11ad) | 0.0727 | 0.655 | 0.57
EDMG (11ay) | 0.0727 | 0.655 | 0.57
CP duration affects the sidelobe levels at the intended receiver due to CP-replay attack.
Symbol duration constrains the response time of the attacker.

## Slide 10
CP-Replay Attack (8)
The effectiveness of target fake path creation depends on channel estimation headroom (determined by symbol timing at Rx side).

## Slide 11: CP-Replay Attack (9)
Channel estimation headroom and timing advance illustrated by using the channel impulse response.

## Slide 12
CP-Replay Attack (10)
Metric for effectiveness:
  Waveform is a random sequence.
  Only CP repetition is observable.
  20 MHz, CP = 16, NFFT = 64.
  Nyquist sampling rate.
  Delay of fake path is an integer multiple of sampling periods.
  Single path between transmitter and attacker, attacker and receiver.
As the headroom increases, CP-replay attack is less successful as expected.

## Slide 13
CP-Replay Attack (11)
Additional SINR degradation
  Simple noise reduction helps to decrease additional SINR degradation due to sidelobe fake paths.
  Additional SINR degradation is not a concern for data decoding.
Fake paths outside GI are zeroed out.
All fake paths are counted.

## Slide 14
Summary
CP of OFDM symbol or any other repetition of signals in the waveform for channel measurement is subject to attack.
We presented a threat model entitled as “CP-replay attack” and showed that fake paths can be created accurately by attacker even in the case of random waveform for channel measurement.
  Such fake paths may not trigger testing processes that require equalization and slicing.
  For certain use cases the goal of FTM is to be able to detect weaker but earlier paths, e.g., LOS ray is blocked.
Needs further investigation on other varieties of late-commit attacks.

## Slide 15: References
[1] IEEE 802.11-16/424R5, 11az FRD.
[2] IEEE 802.11-17/0120r2: “Intel secured location threat model”, B. Abramovsky, O. Bar-Shalom, and C. Ghosh, January 2017.
[3] “Attacks on time-of-flight distance bounding channels”, G. Hancke, et. al., http://www.cl.cam.ac.uk/~mgk25/wisec08-distance.pdf